## Slide 1: Design Experience of WAP Identity Module for M-Commerce
DaeHun Nyang
Information Security Technology Division
ETRI

## Slide 2: Abstract
WIM(Wireless application protocol Identity Module) Overview
  WAP Security Model
  WIM Functionalities
ETRI WIM Developing Environment
ETRI WIM Architecture
  Layered Architecture
  Transmission protocol: T=0
  Device Control: Logical Channel Support
  Data Access: File system supporting Access control
  Cryptography: Publickey crypto supporting Security Environment
  Verification: PIN (Admin, WTLS, Nonrepudiation)
  Drivers for ME
  API for ME to Interwork with WTLS
ETRI WIM Features
Concluding Remarks

## Slide 3: WIM Overview: WAP Security Model
Web Server
WTLS
SSL
WAP Gateway
WTLS : Wireless Transport Layer Security
WIM : Wireless Identity Module
WPKI : Wireless Public key Infrastructure
WAP : Wireless Application Protocol
SSL : Secure Socket Layer
WPKI
Portal
Transaction Security(e2e)
WIM
WMLScript
CryptoLib
WMLScript
CryptoLib
Channel Security

## Slide 4: WIM Overview: WAP Security Model
Feature
Class
1
Class
2
Class
3
Public-key exchange
M
M
M
Server Cert
O
M
M
Client Cert
O
O
M
Shared-secret handshake
O
O
O
Compression
-
O
O
Encryption
M
M
M
MAC
M
M
M
Smart card interface
-
O
O
Class
4
M
M
M
O
O
M
M
M
Class 1 – Anonymous
  No Authentication
?
?
Class 2
  Server Authentication ONLY
?
Class 3/Class 4
  Client & Server Authentication
Class of WTLS

## Slide 5: WIM Overview: WAP Security Model
WIM
Bearers:
Transport Layer(WDP)
Security Layer(WTLS)
Transaction Layer(WTP)
Session Layer(WSP)
Application Layer(WAE)
GSM
IS-136
CDMA
PHS
CDPD
IMT-2000
UMTS
Etc.
Comply with PKCS#15, ISO7816
WTLS Support
Digital Signature Generate/Verify
Unwrapped key
WML Microbrowser
WMLScript
interpreter
WTA Interface
WPKI client
/WALS app.
Other Services
&
Applications
WIM SAP

## Slide 6: WIM Overview: WAP Security Model
Read configuration:Directory File read, Check PIN-G
Generate random : ClientHello.Random
ClientHello
ServerHello
Certificate
CertificateRequest
ServerHelloDone
Read client certificate : X509 URL read
Verify server certificate : WTLSCert
Establish pre-master secret : RSA encryption
Derive master secret
Sign H(handshake_msg)
Calculate client finished check
Calculate server finished check
Calculate client write key
Calculate server write key
Certificate
ClientKeyExchange
CertificateVerify
[ChangeCipherSpec]
Finished
Finished
Write session data : WRITE sessions & peers
Application Data
Web Server
ME
WIM

## Slide 7: WIM Overview: WIM Functionalities
Device Control Primitives
  Logical Channel/Application Select Support
  WIM-OpenService, WIM-CloseService
Data Access Primitives
  File system access
  WIM-OpenFile, WIM-CloseFile, WIM-ReadBinary, WIM-UpdateBinary
Verification Related Primitives
  PIN related commands
  WIM-PerformVerification, WIM-UnblockReferenceData, etc..
Cryptography Primitives
  WIM-ComputeDigitalSignature, WIM-VerifySignature
  WIM-GetRandom, WIM-KeyTransport, etc..

## Slide 8: WIM Overview: WIM Functionalities
WTLS - WIM operation
  Handshaking Support
    Good qualified random number generation
    1024 bit RSA encryption, signature gen/verify
    Generation of data encryption key, MAC key, initial vector
  Acts as a storage for Session related data such as Pre-master secret, master secret
  Secure storage for Privatekey
Application - WIM operation
  1024 bit RSA decryption for Unwrapping key
  Digital signature gen for signText
  Signature verification

## Slide 9: WIM Overview: WIM Functionalities
Card
ME
Server
Read configuration
Generate random
ClientHello
Read client certificate
Verify server certificate
Establish pre-master secret
Derive master secret
Sign H(handshake_msg)
Calculate client finished check
Calculate server finished check
Calculate client write key
Calculate server write key
Finished
Write session data
ServerHello
Certificate *
CertificateRequest *
ServerHelloDone
Certificate *
ClientKeyExchange *
CertificateVerify *
[ChangeCipherSpec]
Finished
WIM-ReadBinary
WIM-VerifySignature
WIM-KeyTransport
WIM-DeriveMasterSecret
WIM-ComputeDigitalSignature
WIM-PHash
WIM-PHash
WIM-PHash
WIM-PHash
WIM-WriteBinary
WIM-ReadBinary
WIM-GetRandom

## Slide 10: WIM Overview: WIM Functionalities
Wallet of Certificates
  User certificates
  Server certificates
  Certificate Authority certificates
  What the certificate type(X.509, WTLS Cert, etc) is totally depends on the application. WIM does not care.

## Slide 11: ETRI WIM Developing Environment
PC/MS-Windows/Linux
Complier & Debugger
SDK(Smart Card Development Kit)
White Card
Card Emulation Board
Dummy Card Reader
ME Simulation Environment
SDK Box
White Card or
Card Emulation Board

## Slide 12: ETRI WIM Developing Environment
Procedure
  Chip Selection
  Acquisition of Development SW: Emulator Compiler, Debugger
  White Card
  Implement Application fully complied with WIM
  Download the binary code to white card
  Card Printing and Issuing

## Slide 13: ETRI WIM Architecture: Overview
WIM-Service Interface:
Set of WIM-Primitives
WIM-Service Primitive
e.g. WIM-PerformVerification
T0-Service Interface:
Set of T0-Primitives
T0-Service Primitive
e.g. T0-Service(BYTE * CAPDU, BYTE CSize, BYTE * RAPDU, BYTE Rsize)
Command
APDU
Response
APDU
T=0 Stack
Crypto
Data Access
Verification
Read
Config.
Verify
Server Cert.
App.:
Unwrapping a key
SE
PIN
FILE
APDU
TPDU with T=0
Device
Control
PHY: Bitstream
Server Process
T=0 Stack
Stack for
Card reader
Stack for
Card reader

## Slide 14: ETRI WIM Architecture: Transmission Protocol
Half-Duplex Asynchronous Protocol
Indicate T=0 or T=1 in a bit of ATR
T=0 Protocol
  Character based protocol
  Appropriate for small amount of data transmission
T=1 Protocol
  Block based protocol
  Require PPS(Protocol and Parameter Selection) procedure
  Appropriate for large amount of data transmission

## Slide 15: ETRI WIM Architecture: Transmission Protocol
Case 1.
Case 2.
CLA INS P1 P2 00
Processing
SWs
OK
CLA INS P1 P2 Le
Processing
Data || SWs
Data (Le) || OK
Case 3.
CLA INS P1 P2 Lc
Interpret
INS
INS
Data (Lc)
Processing
SWs
OK
Case 4.
CLA INS P1 P2 Lc
Interpret
INS
INS
Data (Lc)
Processing
SWs (61 XX)
Interpret
80 C0 00 00 xx (Le)
(Get Response)
Processing
Data || SWs
Data (Le) || OK

## Slide 16: ETRI WIM Architecture: Device Control
Logical Channel Support
Application Selection
  Direct: Prefered in WIM
  Indirect
  PKCS#15 Application or WIM Application in multi-application card with multiple PKCS#15 applications

## Slide 17: ETRI WIM Architecture: Data Access
File System
  Comply with ISO7816-4
  Comply with PKCS#15
  Comply with Access Control defined in WIM and PKCS#15
    Access control based on user identification by PIN
  Flexible design using File Description Table
  Can Accommodate multi-applications

## Slide 18: ETRI WIM Architecture: Data Access
EF(DIR)
EF(TokenInfo)
EF(AODF)
EF(CDF)
EF(ODF)
EF(DODF)
EF(UnusedSpace)
DF
(PKCS#15)
MF
EF(ATR)
EF(Peers)
EF(Sessions)
File System for WIM complying with PKCS#15

## Slide 19: ETRI WIM Architecture: Data Access

## Slide 20: ETRI WIM Architecture: Data Access
NEV never allowed
ALW always allowed
CHV allowed after card holder verification
SYS available only to the card issuer
Access Control

## Slide 21: ETRI WIM Architecture : Cryptography
Security Environment Support
Publickey Cryptography
  Encrypt/Decrypt
  Digital Signature Gen/Verify
Hash Function Support
PRF(Pseudo Random Function) Support
  Comply with [WAPWTLS]
Symmetric key cryptography

## Slide 22: ETRI WIM Architecture : Cryptography
Logical storage for data that is referenced during security related commands
SE
  WTLS_RSA [ CCT, DST, CT ]
  WTLS_ECDH [ CCT, DST, CT ]
  WIM_GENERIC_RSA [ DST, CT ]
  WIM_GENERIC_ECC [ DST, CT ]
Template
  CCT Cryptographic checksum template
  DST Digital signature template
  CT Confidentiality template

## Slide 23: ETRI WIM Architecture : Verification
PIN
  Concept of User login
  Admin PIN
  PIN for WTLS
  PIN for Non Repudiation
Perform, Change, Block/Unblock, Enable/Disable

## Slide 24: ETRI WIM Architecture : Remainings
Drivers for ME
  WIM primitive based General Purpose API
  WLTS Support
  Application level cryptographic operation support
  Transport protocol
API for ME to Interoperate with WTLS
  Interoperable with WTLS
  WTLS detects the insertion of a card and progresses with WIM if it has a card.
API for Administration
  Private/Public Key Install
  Certificate Install
  Update various files in WIM

## Slide 25: ETRI WIM Features
Fully comply with WIM of WAP Forum
  Channel Security: WTLS support
  Transaction Security:
    WMLScript CryptoLibrary/signText/encryptText/encrypt support
  X.509 with DER codec, WTLS Cert with WTLS codec
    WPKI support
  Comply with ISO 7816 –3/ 4/ 8
  Comply with PKCS #15 with DER codec
  Comply with PKCS#1
  PRF/SHA-1/ 1024 bit RSA
Layered architecuture
  Strict modularization: T=0 transport layer, APDU layer, Application layer
  Enhancement of portability
Rapid development for commercial products

## Slide 26: Concluding Remarks
WAP Security Overview
WIM Overview
Presentation of Experience of ETRI WIM Development
Smart cards with publickey cryptography does not have yet application. Publickey cryptography has been prevailed in the Internet and expects to be spread into smart cards.
Thanks.