## Slide 1: H.323 and some Security-related issues – a presentation in two parts
Simão Ferraz de Campos Neto
Counsellor – ITU-T Study Group 16
Multimedia Services, Systems and Terminals

## Slide 2: General contents
Part A: H.323 today and other VoIP Protocols
  The Basics of H.323
  Past to Present
  H.323 version 4
  New features since H.323v4
  The Future
  Interconnecting between carriers
  SIP
  Multimedia Communications
Part B: Multimedia Security within Study Group 16
  Question G/16 “Security of MM Systems & Services”
  Secure IP Telephony
  Media Gateway Decomposition & H.248.1 Security
  H.320 Audio/Video Security
  Security Aspects of Data Conferencing
  Security in other study groups

## Slide 3: Part A: Current State of H.323 and Relationship to other VoIP Protocols
Author: Paul E. Jones
Rapporteur ITU-T Q2/16

## Slide 4: The Basics of H.323

## Slide 5: What is H.323?
H.323* is a multimedia conferencing protocol, which includes voice, video, and data conferencing, for use over packet-switched networks
* H.323 is “ITU-T Recommendation H.323: Packet-based multimedia communications systems”

## Slide 6: General H.323 Scenario
H.323 Client via PPP
H.323 Intranet Client
Gatekeeper
H.323 Internet Client
Firewall
Gateway
(Access Server)
Gateway
(H.323/ISDN/H.320)
Intranet (LAN)
IP Phone (SET)
PSTN
Multicast Unit
Internet
PBX
IP
Analog and Digital Phones

## Slide 7: Elements of an H.323 System
Terminals
Multipoint Control Units (MCUs)
Gateways
Gatekeeper
Border Elements
Referred to as “endpoints”

## Slide 8: Terminals
Telephones
Video phones
IVR devices
Voicemail Systems
“Soft phones” (e.g., NetMeeting®)

## Slide 9: MCUs
Responsible for managing multipoint conferences (two or more endpoints engaged in a conference)
The MCU contains a Multipoint Controller (MC) that manages the call signaling and may optionally have Multipoint Processors (MPs) to handle media mixing, switching, or other media processing

## Slide 10: Gateways
The Gateway is composed of a “Media Gateway Controller” (MGC) and a “Media Gateway” (MG), which may co-exist or exist separately
The MGC handles call signaling and other non-media-related functions
The MG handles the media and possibly some signaling, such as DTMF
Gateways interface H.323 to other networks, including the PSTN, H.320 systems, and other H.323 networks (proxy)

## Slide 11: Gatekeeper
The Gatekeeper is an optional component in the H.323 system which is used for admission control and address resolution
The Gatekeeper may allow calls to be placed directly between endpoints or it may transparently route the call signaling through itself to perform functions such as follow-me/find-me, forward on busy, etc.

## Slide 12: Border Elements
Border Elements, which are often co-located with a Gatekeeper, exchange addressing information and participate in call authorization between administrative domains
Border Elements may aggregate address information to reduce the volume of routing information passed through the network
Border elements may assist in call authorization/authentication directly between two administrative domains or via a clearinghouse

## Slide 13: The Zone
T
T
T
GW
GW
GW
SCN
Packet Network
MCU
GK

## Slide 14: A Single Administrative Domain
BE

## Slide 15: Multiple Administrative Domains
Clearing House
Packet Network

## Slide 16: Past to Present

## Slide 17: Past to Present
The first version of H.323 protocol was published in 1996 and was “designed for local area networks”
Local Area Network
Or was it?
Notes: Version 1 (1996) was designed with the Local Area Network in mind. H.323 has its roots in the video conferencing area, borrowing much of the multimedia conferencing aspects from other H.32x-series Recommendations, such as H.320. H.323 was intended to allow people on a LAN to conduct an audio, video, and data conference (with the help of T.120). Or was it?

## Slide 18: Past to Present
The first thing companies tried to do was use H.323 in wide area networks, large private VoIP networks, and the Internet
  Guess what?
  It worked very well
Notes: Early comers to the H.323 market, such as VocalTec, recognized H.323’s potential for Internet Telephony.

## Slide 19: Past to Present
H.323 was an early adopter of such IETF protocols as RTP, which proved its ability to carry real-time audio and video over IP networks that span the globe
Indeed, H.323 was much more than a LAN protocol
Notes: RTP, as probably everyone in the IP Telephony space knows, is the same media transport protocol used by both H.323 and SIP devices. The early designers of H.323 recognized the potential of embracing, not only the packet network, but also the IETF protocols have helped make the Internet what is is today. For this and other reasons, H.323 is well-suited for multimedia conferencing over IP networks, including the Internet.

## Slide 20: Past To Present
Recognizing the fact that H.323 was more than a LAN protocol, the name was changed in H.323 Version 2 (1998)
Enhancements were made, including:
  Security
  Performance
  Supplementary Services
  Scalability
Notes: The name of H.323 was changed to “Packet-based multimedia communications systems”.

## Slide 21: Past to Present
H.323 version 3 introduced a few modest improvements, mostly geared for better PSTN integration and scalability
New annexes were introduced:
  Annex E/H.323 – UDP signaling
  Annex F/H.323 – Simple endpoint type
  Annex G/H.225.0 – Communication between administrative domains

## Slide 22: Past to Present
Various service features created up to H.323v3:
  Call forward at via “Facility” message
  Call hold via “empty capability set”
  Call transfer via “third party pause and re-routing”
  H.450.1 – Base protocol for services
  H.450.2 – Transfer
  H.450.3 – Diversion
  H.450.4 – Hold
  H.450.5 – Park/Pick-up
  H.450.6 – Call Waiting
  H.450.7 – Message Waiting Indication

## Slide 23
Version 4
And Beyond

## Slide 24: H.323 Version 4
H.323 version 4 was approved November 17, 2000 and brought a number of enhancements to H.323. Areas of focus included:
  Scalability
  Services
  Important New Enhancements
  Generic Extensibility Framework

## Slide 25: Scalability
Gateway decomposition with H.248
Additive Registrations
Alternate Gatekeepers*
Endpoint Capacity Reporting
*Alternate gatekeepers were first introduced in H.323v2. H.323 version 4 more fully defines the procedure and provides enhancements.
Notes: *Alternate gatekeepers were first introduced in H.323v2, but not documented. H.323 version 4 fully defines the procedure.

## Slide 26: Alternate Gatekeepers
By using Alternate Gatekeepers, endpoints are able to continue functioning in the face of one or more failures
T
GK
GK
GK
GK
GK
X
X

## Slide 27: Endpoint Capacity Reporting
By utilize endpoint capacity reporting, Gatekeepers may select an endpoint that is best capable of handling the call
This is extremely useful for large-scale deployments of Gateways and is also useful in call-center applications
GK
GK
GK
GK
GK
GW
23%
GW
77%
GW
48%
GW
64%
GW
14%
GW
36%
The GK selects the GW with the most capacity. Note that H.323 endpoints report capacity in absolute terms, not in percentage of free resources as suggested above.

## Slide 28: The Composite Gateway
Gateway
Traditional Gateways were designed in such a way that both media and call control were handled by the same box
The two components are referred to as the Media Gateway Controller (MGC) and Media Gateway (MG)
MGC
MG

## Slide 29: The Decomposed Gateway
The decomposed Gateway separates the MGC function and the MG function
Multiple MGs may exist to allow the decomposed Gateway to scale to support much more capacity than a composite Gateway
Communication between the MGC and MGs is done through H.248
Communication between MGCs is done through H.323
MGC
MG
MG
MG
MG
MG
MG
MG
MG
MG
MG
MG
MG
MG
MG
MG

## Slide 30: H.248.1 and MGCP
October 1998
November 1998
August 1998
February 1998
June 2000
MDCP
IPDC
SGCP
MGCP
H.248

## Slide 31: H.248.1 and MGCP
SGCP was the first protocol to address Media Gateway Control, but IPDC followed very soon
In October 1998, SGCP and IPDC were merged to create MGCP
Lucent (among others) did not like the design philosophy behind MGCP and proposed MDCP
  MGCP had an “endpoint” model
  MDCP had an “edgepoint” model
The ITU and IETF worked jointly to create H.248.1, which combines aspects of MGCP and MDCP

## Slide 32: H.248.1 and MGCP
ITU-T Study Group 9 is defining a “profile” of MGCP called “Trunking Gateway Control Protocol” or TGCP (J.171)
J.171 is intended to function over Cable Television networks
MGCP, including derivatives like J.171, is widely implemented by a number of vendors, as is H.248.1

## Slide 33: H.235 version 2
H.235 version 2 defines the security framework for H.323 and other H-Series terminals
In H.235 version 1, no “profiles” were defined to specify how endpoints should utilize the security framework; therefore, it was not widely used

## Slide 34: H.235 version 2
H.235 version 2 introduces a number of enhancements
  Security profiles (password and certificates)
  Elliptic curve cryptography
  Anti-spamming features
  Support for backend services (RADIUS authentication, etc.)

## Slide 35: H.235 - “H.323 Security“ Security Protocol Architecture
AV
Applications
Audio
G.711
G.722
G.723.1
G.729
Video
H.261
H.263
Encryption
RTCP
H.225.0
Terminal
to
Gatekeeper
Signaling
(RAS)
Terminal Control and Management
Data
Applications
Security
Capabilities
Security
Capabilities
T.124
T.125
Unreliable Transport / UDP, IPX
Reliable Transport / TCP, SPX
Network Layer / IP / IPSec
Link Layer /......
Physical Layer / .....
T.123
Scope of H.323
Scope of H.235
TLS/SSL
Multimedia Applications, User Interface
TLS/SSL
Authenti-
cation
RTP
Scope of T.120
H.225.0
Call
Signaling
(Q.931)
H.245
System
Control
Notes: This slide illustrates the work on security and encryption for H.323 (IP-based network) multimedia systems.
Rec H.235 covers authentication and privacy of all real-time media streams exchanged during a conference.
-the dotted areas shows the terminal part addressed in H.323 and the red parts the security features defined in H.235.
-->You can find a complete presentation of the SG16 work on security in the workshop which was held two months ago in Seoul!

## Slide 36: Security Profiles for H.235
Annex D/H.235 – Baseline security profile
Annex E/H.235 – Signature profile
Annex F/H.235 – Hybrid Security profile

## Slide 37: New Service Features
H.450.8 – Name identification
H.450.9 – Call Completion (busy and no answer)
H.450.10 – Call Offer
H.450.11 – Call Intrusion
H.450.12 – Common Information Additional Network Feature
H.323 Annex K – Services via HTTP
H.323 Annex L – Stimulus Control

## Slide 38: Important New Enhancements
Usage reporting
Caller Identification
Alias mapping
Better bandwidth management (multicast)
Fax enhancements
Tunneling other protocols (Annex M.x)
H.323-specific URL
Call credit-related capabilities
DTMF relay via RTP (RFC 2833)

## Slide 39: Generic Extensibility Framework (H.460.x sub-series)
The Generic Extensibility Framework (GEF) introduces a new means by which H.323 may be further enhanced or extended with optional features, which does not require changes to the current ASN.1 syntax

## Slide 40: H.460 Series
H.460 Series documents define new features that utilize the Generic Extensibility Framework
H.460 documents are all optional and may be implemented by any H.323v4 or newer device
Two H.460 documents approved thus far:
  H.460.1 – GEF Usage Guidelines
  H.460.2 – Number Portability

## Slide 41: Further Enhancements to V4
Annex R/H.323 – Robustness
Annex Q/H.323 – Far End Camera Control
H.501 – Mobility Management Protocol
H.510 – Mobility for H.323 (User, terminal, and service mobility)
H.530 – Symmetric Security Profiles for H.510

## Slide 42: The Future

## Slide 43: The Future (near-term)
Annex I/H.323 – Communication over error-prone channels
Annex O/H.323 – Relation of H.323 to other Internet protocols, such as ENUM and TRIP
Annex P/H.323 – Modem relay
Emergency / Disaster Relief scenarios
  Better guarantee of call completion
  Identification of caller
  Operator control of customer premise equipment

## Slide 44: The Future (near-term)
Continued PSTN interworking improvements
Extended Fast Connect
QoS Monitoring
Route re-querying capability
SRTP support for secure media
H.323v5, H.225.0v5, and H.235v3

## Slide 45: Future Work (long-term)
Protocol to communicate between Alternate Gatekeepers
Architecture and protocols to decompose the Gatekeeper
Usage of SCTP as a transport
Utilization of the firewall control protocol (under development in the IETF)
MIB enhancements

## Slide 46: Future Work (long-term)
Port reservation (possible part of emergency services)
Third Party Call Control and other services
Presence capabilities

## Slide 47: Interconnecting Between Carriers and Enterprise Locations

## Slide 48: Interconnection Issues
Security
“Information Hiding” to prevent peers from learning network topology
Address resolution
Firewall traversal
IP addresses are scarce

## Slide 49: Security
Zone-level security
  Endpoints must be authenticated (CPE, GW)
  Users may be authenticated (calling card)
Inter-zone, intra-domain
  Calls placed within the service providers network must be authenticated
  Tokens (irrespective of H.235) may be utilized, but must be universally supported

## Slide 50: Security
Inter-zone, inter-domain
  Annex G/H.225.0
    Border Elements may act as trusted entities between administrative domains to pass authentication data
    A centralized clearinghouse may be utilized between administrative domains that do not have established trust relationships
  As an alternative to Annex G/H.225.0, Gatekeeper-routed call signaling or IP/IP GWs may be used at the edge of the network to control and authenticate calls
  Lastly, tokens may be passed via RAS and H.225.0

## Slide 51: Information Hiding
In some cases, one carrier may wish to hide the topology of its network from another carrier
To hide the topology of the network, Gatekeepers or IP/IP gateways (proxies) may route the call signaling and/or media flows

## Slide 52: Address Resolution
RAS (Location Request messages)
H.323 Annex G
TRIP
ENUM
Backend server (perhaps an LDAP database, an SCP, or other entity)
Notes: RAS: Registration, Admission and Status

## Slide 53: Address Resolution
Location Request (LRQ) has been proven to be very useful for resolving addresses within a small domain or even multiple domains consisting of a hierarchy of Gatekeepers
Annex G offers comparable functionality as the LRQ, with respect to address resolution, but it can advertise “routes” to reduce the number of queries across the network and can provide authorization and settlement capabilities

## Slide 54: TRIP (Telephony Routing over IP)
Used for inter- and intra-domain routing of calls
TRIP is similar to Annex G/H.225.0, in that it exchanges addressing information prior to a call
TRIP is different in that it support multiple protocols, including SIP, H.323 Call Signaling, H.225.0 Annex G, and RAS

## Slide 55: ENUM (Telephone Number Mapping)
ENUM is a new IETF protocol [RFC 2916] that uses DNS to translate phone numbers into URLs
$ORIGIN 8.4.9.6.2.9.3.9.1.9.1.e164.arpa.
IN NAPTR 100 10 "u" “h323+E2U" "!^.*$!h323:paulej@cisco.com!" .
IN NAPTR 100 20 "u" "mailto+E2U" "!^.*$!mailto:paulej@cisco.com!" .
+1 919 392 6948
h323:paulej@cisco.com
DNS

## Slide 56: Firewall Traversal
Firewalls present problems to VoIP and multimedia conferencing applications, since UDP is used for media
The IETF formed a working group to create a “firewall control protocol” (MIDCOM).
Thus far, they have created drafts for STUN (Simple Traversal of UDP Through NATs) and TURN (Traversal Using Relay NAT), but have not yet created a firewall control protocol.
Notes: STUN - Simple Traversal of UDP Through NATs
TURN - Traversal Using Relay NAT

## Slide 57: IP Address Space
IPv4 addresses are limited and there is a desire by many to migrate to IPv6 where IP addresses are more plentiful
IPv6 has been implemented by many companies, but deployment timeframes are questionable– who will pay for its deployment?
H.323 and SIP are both IPv6-capable, but few (if any) companies have implemented support in their products

## Slide 59: Session Initiation Protocol (SIP)
The Session Initiation Protocol (SIP) is defined in RFC 2543
A lot of work has gone into corrections, additions, and changes to SIP, which has resulted in the soon-to-be published RFC 3261
RFC 3261 is larger in terms of pages than Recommendation H.323 and is the largest IETF document ever produced– complexity is increasing

## Slide 60: SIP
Sample Internet Drafts:
  Session Timers (“keep alive”) for stateful proxies
  Caller preferences and callee capabilities
  Reliable provisional responses
  Use of DNS SRV records for locating SIP servers
  Call Transfer
  REFER method
  UPDATE method
  Service Mobility
Over 100 Internet Drafts Presently

## Slide 61: SIP
In short, progress on SIP has moved forward quite rapidly, but much of the important work is still in Internet Draft form and is subject to change
The SIP specification itself has been changed substantially and has grown in size and complexity

## Slide 62: SIP
Debates in the IETF have occurred over problematic areas of SIP, including
  SDP is not sophisticated enough to address the needs of signaling things, including modem over IP capabilities (being addressed)
  SIP message sizes are too large (2 forms of compression considered)
  UDP has proven to be problematic (TCP was strongly advocated for a time)

## Slide 63: SIP
Support for SIP is growing and many carriers around the world are now examining SIP as a possible protocol for deployment in the next 12-18 months
This same statement has been made for the past 3 years now

## Slide 64: H.323 and SIP Interworking
One of the challenges we face is harmonizing the H.323 and SIP networks
  Basic call interworking (work in progress)
  Feature interworking (everybody wants it, but nobody wants to do the work)

## Slide 65: Multimedia Communications

## Slide 66: Where’s the Multimedia?
But why aren’t video and data conferencing systems and applications more prevalent?
  VoIP
  VoIP
  VoIP

## Slide 67: The Market Today
Today, the biggest market for H.323 applications is Voice over IP. Why?
  Most Internet connections today are still low-speed dial-up, making video and data intensive applications less appealing
  It’s a young industry, and with all such industries, it takes time to mature good products
  Companies can provide VoIP services today at a low cost and provide new competition to the incumbent carriers

## Slide 68: The Changing Market
Tomorrow, expect to see video and data conferencing to become more pervasive
  Broadband connectivity is making it possible
  Video and data are logically the next services customers expect to find in conference rooms and on their computer screens

## Slide 69: Beyond Voice over IP
Voice over IP opens the door to the next generation of communication products
It will take some time to migrate the world from PSTN to IP networks
  H.323 provides excellent interworking between IP networks and the PSTN
  H.323 provides a strong, proven foundation for new multimedia products and services

## Slide 70: IP Telephony
IP Telephony with H.323 truly means Multimedia over IP

## Slide 71: H.323 Makes It All Possible
H.323 makes it possible to create and deploy new services quickly and to take advantage of multimedia capabilities
These services can embrace audio, video, and data conferencing
- Application Sharing | - Electronic Whiteboard | - File Transfer
- Instant Messaging | - Click to Dial | - Internet Call Waiting
- Web Call Parking | - URL Redirection | - Ad-Hoc Conferencing
- Voicemail Anywhere | - Unified Messaging | - Service Portability
- Services! | - Services! | - Services!
Notes: T.120 provides H.323 systems with the capability of participating in, not only audio and video conferences, but also data conferencing. One interesting service that H.323 provides is Instant Messaging. Never thought about that? It’s possible– and the protocol specification has already been approved. Of course, the biggest benefit to H.323 is the fact that all of the equipment being deployed today and all of the networks running H.323 today and in the future allows for more services and new services that have not yet been imagined.

## Slide 72: Why H.323 for the Service Provider?
H.323 is a proven technology that is utilized in many large networks
Excellent integration with the PSTN
Gateways and residential devices are in use today
Notes: H.323 products for the residential customer come in a variety of forms, from wireless phones to single-line “gateway” devices with an RJ-11 to ADSL and cable modem devices to PC desktop IP phones

## Slide 73: Why H.323 in the Enterprise?
Multimedia conferencing devices show the real potential of H.323 and multimedia communication
With H.323 in the service provider network, H.323 is a logical choice for the enterprise
The enterprise customer wants voice, video, and data conferencing capabilities

## Slide 74: Contacts for H.323 Information
For further information, please feel free to contact:
Author of H.323 Content: Paul Jones
paulej@packetizer.com
Tel: +1-919-392-6948 Fax: +1-919-392-6801
Also see:
http://www.packetizer.com
Presenter: Simão Ferraz de Campos Neto
simao.campos@itu.int
Tel: +41-22-730-6805 Fax: +41-22-730-4345
Also see:
http://www.itu.int/ITU-T/studygroups/com16

## Slide 75: Part B: Multimedia Security within Study Group 16 Past, Presence and Future
Author: Martin Euchner
Rapporteur ITU-T Q.G/16

## Slide 76: Question G/16 “Security of MM Systems & Services”

## Slide 77: Study Group 16 - Security-related Questions in the MediaCom2004 project
Q.C - MM Applications & Services F.706
Q.D - Interoperability of MM Systems & Services
Q.G - Security of MM Systems & Services H.233, H.234, H.235
Q.1
MM Systems, Terminals & Data Conferencing
H.320
H.324
T.120
Q.2
MM over Packet Networks using H.323 systems
H.225.0
H.323
H.450
H.460
Q.3
Infrastructure & Interoperability for MM over Packet Network Systems
H.245
H.246
H.248
Q.4
Video and Data conferencing using Internet supported Services
Q.5
Mobility for MM Systems & Services
H.501
H.510
H.530
Q.F - MM Quality of Service & E-2-E Performance in MM Systems

## Slide 78: Question G/16 Security of MM Systems & Services
A horizontal question with broad focus
General Responsibilities:
  Perform threat analysis, analyze security requirements; recommend security services/mechanism for MM applications
  Build sound security architecture and interface with security infrastructure
  Realize multimedia communications security, engineer MM security protocols with real-time, group-communication, mobility and scalability constraints
  Address interdomain security and security interworking
  Maintain H.233, H.234; progress H.235
For further details on Q.G terms of reference, please see Annex G of the MediaCom2004 project description
http://www.itu.int/ITU-T/studygroups/com16/mediacom2004

## Slide 79: Multimedia Communications Security Some questions to address
Secure the signaling for MM applications
Secure data transport and MM streams
Protect MM content (authorship, IPR, copy-protection)
Efficiently integrate key management into MM protocols; interface with security infrastructures (e.g., PKI)
Negotiate security capabilities securely
Interact with security gateways and firewalls
Enable MM security across heterogeneous networks
Provide scalable security (small groups, medium sized enterprises, large carrier environments)
Build future-proof security (simple&sophisticated techniques)
Address the performance and system constraints (SW/HW crypto, smart-cards,...)
….

## Slide 80: Q.G Work and Study Items Some Highlights
Investigate confidentiality and privacy of all signaling
Address the concept of a centralized key management for MM systems
Security for MM Mobility, MM Presence, MM Instant Messaging
Optimize voice encryption, develop video encryption, consider sophisticated crypto algorithms
MM security support for emergency services
Consolidate or develop new security profiles
Clarify the impact due to lawful interception
Architect secure, de-composed systems
Security interworking H.323-SIP
Interaction with e-commerce and network security
...

## Slide 81: Target Multimedia Applications with Security Needs
Voice/Video Conferencing
Data Conferencing
IP Telephony (Voice over IP)
Media Gateway Decomposition
Instant Messaging and MM-Presence

## Slide 82: Threats to Multimedia Communication
Internet PC
PDA
Notebook
PC
Telephone
TV
Kiosk
Terminal
Online-Services
e.g. WWW,
Compuserve
Radio/Television Data
Telephone
Data
Video
WAN
Internet
Private
Network
LAN
Intranet
Public
Network
Unauthorized Access to Resources and Services
Intrusion
Repudiation (Data, Service)
Eavesdropping, Disclosure
Billing Fraud
Masquerade
Manipulation of Data
Replay
Misuse of Data
Misuse of Services
Denial of Service
Traffic Analysis
Insider Threats

## Slide 83: Secure IP Telephony
H.235 H.235 Annex D H.235 Annex E H.235 Annex F H.235 Version 3 H.530

## Slide 84: IP Telephony - Security Issues
User authentication:
  Who is using the service? (Who am I phoning with?)
Call authorization:
  Is the user/terminal permitted to use the service resources?
Terminal and server authentication:
  Am I talking with the proper server, MCU, provider? Mobility ...
Signaling security protection;
  Protection of signaling protocols against manipulation, misuse, confidentiality & privacy
Voice confidentiality:
  Encryption of the RTP voice payload
Key management:
  Secure key distribution and key management among the parties
Interdomain security:
  Security profile & capability negotiation, firewall traversal

## Slide 85: Specific IP Telephony Security Challenges
IP Telephony is real-time, point-2-point or multi-point
  secure fast setup/connect
  real-time security processing of media data
  real-time certificate processing
  IKE security handshakes take too long
Security measures must be integrated in proprietary platforms and in VoIP stacks
  security can best be added at application layer
  tight interaction with voice CODECs and DSPs
  low overhead for security: small code size, high performance,...
  “Windows 5000” is not the answer!
Secure management of the systems
  secure password update
  secure storage in databases
Scalable security from small enterprise to large Telco environments
Security should be firewall friendly

## Slide 86: “Historic” Evolution of H.235
1997
1998
1999
2000
1996
2001
2002
Initial Draft
Security Profiles
Annex D
Annex E
started
H.323V2
H.323V4
H.323V5?
H.235V2
Annex D
Annex E approved
Annex F
H.530
consent
H.235V1
approved
H.235V3 consent?
Core Security Framework Engineering
Consolidation
Improvement
1st Deployment

## Slide 87: H.235 – Security for H.323
“Security and Encryption for H.323 and other H.245-based multimedia terminals”
Builds upon ITU-T Rec. X.509
Provides cryptographic protection of control protocols (RAS, H.225.0 and H.245) and audio/video media stream data
Negotiation of cryptographic services, algorithms and capabilities
Integrated key management functions / secure point-to-point and multipoint communications
Interoperable security profiles
Sophisticated security techniques (Elliptic curves, anti-spamming & AES)
May use existing Internet security packages and standards (IPSec, SSL/TLS)

## Slide 88: H.235 – “H.323 Security” Security Protocol Architecture
AV
Applications
Audio
G.711
G.722
G.723.1
G.729
Video
H.261
H.263
Encryption
RTCP
H.225.0
Terminal
to
Gatekeeper
Signaling
(RAS)
Terminal Control and Management
Data
Applications
Security
Capabilities
Security
Capabilities
T.124
T.125
Unreliable Transport / UDP, IPX
Reliable Transport / TCP, SPX
Network Layer / IP / IPSec
Link Layer /......
Physical Layer / .....
T.123
Scope of H.323
Scope of H.235
TLS/SSL
Multimedia Applications, User Interface
TLS/SSL
Authenti-
cation
RTP
Scope of T.120
H.225.0
Call
Signaling
(Q.931)
H.245
System
Control
Notes: This slide illustrates the work on security and encryption for H.323 (IP-based network) multimedia systems.
Rec H.235 covers authentication and privacy of all real-time media streams exchanged during a conference.
-the dotted areas shows the terminal part addressed in H.323 and the red parts the security features defined in H.235.
-->You can find a complete presentation of the SG16 work on security in the workshop which was held two months ago in Seoul!

## Slide 89: H.530 The Security Problem of H.323 Mobility
Provide secure user and terminal mobility in distributed H.323 environments beyond interdomain interconnection and limited GK-zone mobility
Security issues:
  Mobile Terminal/User authentication and authorization in foreign visited domains
  Authentication of visited domain
  Secure key management
  Protection of signaling data between MT and visited domain
Notes: H.530: Symmetric security procedures for H.323 mobility in H.510

## Slide 90: Media Gateway Decomposition and H.248.1 Security

## Slide 91: H.248.1 Security in decomposed Gateways
(interim AH) IPSEC AH/ESP
H.225.0/ H.245/ H.235
SCN/SS7
RTP/ H.235
TDM voice trunk
IKE
H.248
H.245 OLC/ H.235
H.235 RTP payload security
Media Gateway MG
IPSEC
IKE
H.235 Key Management
IPSEC
IKE
Media Gateway Controller MGC
Notes: H.235 provides plenty of options, with no mandatory settings
RAS: 11, Call Signaling: 12, Call Control: 10, Media Stream Encryption: 4
SET, zBsp. IP Phone

## Slide 92: H.320 Audio/Video Security

## Slide 93: Security for Multimedia Terminals on circuit-switched networks
H.233: “Confidentiality System for Audiovisual Services”
  point-to-point encryption of H.320 A/V payload data by ISO 9979 registered algorithms: FEAL, DES, IDEA, B-CRYPT or BARAS stream ciphers
H.234: “Key Management and Authentication System for Audiovisual Services”
  uses ISO 8732 manual key management
  uses extended Diffie-Hellman key distribution protocol
  RSA based user authentication with X.509-like certificates by 3-way X.509 protocol variant

## Slide 94: Security Aspects of Data Conferencing

## Slide 95: Security for Computer Supported Collaborative Work (CSCW)
CSCW scenarios:
  Users work in a virtual office (Teleworking/Telecommuting from home)
  collaboration of users in a tele-conference through a conference system
Security aspects:
  user authentication for granting access to the corporate environment
  telecommuting server can protect out-bound/VPN application data
  secure remote access and management to home office PC
  home office PCs deserve special security protection:
    against intruders, viruses
    against misuse of corporate services
    unauthorized access to local information though application sharing
  point-to-point security may not be optimal in a decentralized multi-party conference

## Slide 96: Security for Multimedia Conferencing T.120 and Security
T.120 has very weak information security available (unprotected passwords), common state of the art cryptographic mechanisms are not supported.
OS security features do not prevent against typical T.120 threats (especially T.128 application sharing vulnerabilities); this problem already arises in simple pt-2-pt scenarios.
Additional threats exist for group-based multipoint scenarios: insider threats, lack of access control, “write token” not protected, unsecured conference management ,…
  The T.120 “virtual conference room” needs integral and user friendly security protection: for authentication & role-based authorization, for confidentiality, for integrity, and security policy negotiation capabilities.

## Slide 97: Security for MM Applications and Systems in Emergency & Disaster Relief
Security objectives:
  prevent theft of service and denial of service by unauthorized user
  support access control and authorization of ETS users
  ensure the confidentiality and integrity of calls
  provide rapid and user-friendly authentication of ETS users
H.SETS is the provisional title for a new work item under study within Q.G with the focus on the multimedia security aspects of ETS
Relationship identified with QoS, network issues, robustness and reliability,...

## Slide 98: Security in other study groups
SG 17: Lead SG on Communication System Security
  X.509 “The Directory: Public-key and attribute certificate frameworks”
  X.800 “Security architecture for Open Systems Interconnection for CCITT applications”
  Q.9/17: related to X.509 issues
  Q.10/17: Question for security, coordination with other study groups involved: SG 2, 4, 9,11, 13, 16 & SSG
  ITU-T Security Project
As SG 16, other study groups address security issues as needed on the course of production of Recommendations under their mandate; e.g.:
  J.170 “IPCablecom security specification” (SG 9)
  M.3016 “TMN security overview” (SG 4)
  M.3210.1 “TMN services for IMT-2000 sec. management”
  T.36 “Security capabilities for use with Group 3 facsimile terminals” (SG 8SG 16)
New!
Notes: List of Security-related recommendations in ITU-T (as of May 2002)
ITU-T SG 16
H.233, Confidentiality system for audiovisual services,
H.234, Encryption key management and authentication system for audiovisual services,
H.235, Security and encryption for H-Series (H.323 and other H.245-based) multimedia terminals,
H.323, Annex J, Packet based multimedia communications systems - Security for simple endpoint types
H.510, Mobility for H.323 multimedia systems,
T.30, Annex G, Procedures for secure G3 document facsimile transmission using the HKM and HFX system
T.30, Annex H, Procedures for security in facsimile G3 based on the RSA algorithm,
T.36, Security capabilities for use with Group 3 facsimile terminals,
T.503, A document application profile for the interchange of Group 4 facsimile documents,
T.563, Terminal characteristics for Group 4 facsimile apparatus.
Coming Soon
H.530 Symmetric Security Procedures for H.510 (Mobility for H.323 Multimedia Systems and Services
Revision to H.235 Annex C H.324 Security Enhancements
Revision to H.235 Annex C H. SETS Security for Emergency Telecommunication Services
List of Recommendations dealing with Security in SG 9,ITU-T
ITU-T Recommendation J.170 - Part 1 IPCablecom security specification
List of Recommendations dealing with security in SG 4, ITU-T
M.3016, TMN security overview
M.3210.1, TMN management services for IMT-2000 security management
M.3320, Management requirements framework for the TMN X-Interface
M.3400, TMN Management Functions
Q.813, Security Transformations Application Service Element for Remote Operations Service Element (STASE-ROSE)
Q.815, Specification of a security model for whole message protection
X.736, Information technology - Open Systems Interconnection - Systems Management: Security alarm reporting function
X.740, Information technology - Open Systems Interconnection - Systems Management: Security audit trail function
X.741, Information technology - Open Systems Interconnection - Systems management: Objects and attributes for access control
List of Recommendations dealing with security in SG 2, ITU-T
Under development, see Contribution COM 2-20
List of Recommendations dealing with security in SG 17, ITU-T
X.509, Information technology - Open Systems Interconnection - The Directory: Public-key and attribute certificate frameworks
X.800, Security architecture for Open Systems Interconnection for CCITT applications
X.802, Information technology - Lower layers security model
X.803, Information technology - Open Systems Interconnection - Upper layers security model
X.810, Information technology - Open Systems Interconnection - Security frameworks for open systems: Overview
X.811, Information technology - Open Systems Interconnection - Security frameworks for open systems: Authentication framework
X.812, Information technology - Open Systems Interconnection - Security frameworks for open systems: Access control framework
X.813, Information technology - Open Systems Interconnection - Security frameworks for open systems: Non-repudiation framework
X.814, Information technology - Open Systems Interconnection - Security frameworks for open systems: Confidentiality framework
X.815, Information technology - Open Systems Interconnection - Security frameworks for open systems: Integrity framework
X.816, Information technology - Open Systems Interconnection - Security frameworks for open systems: Security audit and alarms framework
X.830, Information technology - Open Systems Interconnection - Generic upper layers security: Overview, models and notation
X.831, Information technology - Open Systems Interconnection - Generic upper layers security: Security Exchange Service Element (SESE) service definition
X.832, Information technology - Open Systems Interconnection - Generic upper layers security: Security Exchange Service Element (SESE) protocol specification
X.833, Information technology - Open Systems Interconnection - Generic upper layers security: Protecting transfer syntax specification
X.834, Information technology - Open Systems Interconnection - Generic Upper Layers Security: Security Exchange Service Element (SESE) Protocol Implementation Conformance Statement (PICS) proforma
X.835, Information technology - Open Systems Interconnection - Generic Upper Layers Security: Protecting transfer syntax Protocol Implementation Conformance Statement (PICS) proforma
X.841, Information technology - Security techniques - Security information objects for access control
X.842, Information technology - Security techniques - Guidelines for the use and management of trusted third party services
X.843, Information technology - Security techniques - Specification of TTP services to support the application of digital signatures
Under development,
X.ism, information security management,
X.css, communication systems security,
X.ms, mobile security,
X.tb, telebiometrics.

## Slide 99: Summary of Security work in SG 16
In Study Group 16, Security issues coordinated under umbrella Question G/16, “Multimedia Security”
Several recommendations for security in MM terminals and services
Examples of past, present and future MM-security in SG16
  Secure H.323-based IP Telephony
  H.235 and associated security profiles
  H.248.1 Media Gateway Decomposition Security
  Secure H.320 Audio/Video and T.120 Data Conferencing
  Security for Emergency Telecommunications

## Slide 100: Contacts for Security in MM Terminals
For further information, please feel free to contact:
Author of Security in MM Terminals: Martin Euchner
martin.euchner@icn.siemens.de
Tel: +49-89-7-22-55790 Fax: +49-89-7-22-46841
Presenter: Simão Ferraz de Campos Neto
simao.campos@itu.int
Tel: +41-22-730-6805 Fax: +41-22-730-4345
Also see:
http://www.itu.int/ITU-T/studygroups/com16

## Slide 101: Thank you for your attention!
For further contact, please feel free to contact:
Simão Ferraz de Campos Neto
Counsellor, ITU-T Study Group 16
simao.campos@itu.int
Tel: +41-22-730-6805
Fax: +41-22-730-4345
http://www.itu.int/ITU-T