## Slide 1: Optical and xDSL Access work in ITU-T Study Group 15
Presented by:
Simão Ferraz de Campos Neto
Counsellor – ITU-T Study Group 16
Multimedia Services, Systems and Terminals

## Slide 2: Contents
About ITU-T SG 15
Optical Access
xDSL Access
Other access technologies

## Slide 3: About Study Group 15

## Slide 4: ITU-T Study Group 15
Responsible for studies relating to:
optical and other transport networks, systems and equipment including transmission layer related standards for access, metropolitan and long haul sections of communication networks
Lead Study Group on
Access Network Transport (ANT)
Optical Technology
(www.itu.int/ITU-T/studygroups/com15)
Responsible for the development of Recs. in the G-series that support xDSL and optical accesses.

## Slide 5: Many a type of access
F.O.
Copper or F.O.
Copper
Broadcast
SAT
Longhaul
Distribution Network
Access Network
Cable
Home Network
UNI
SNI

## Slide 6: ITU-T Study Group 15 Structure http://www.itu.int/ITU-T/studygroups/com15/index.asp
Study Group 15
Optical and other transport networks
Peter Wery
Working Party 3
OTN Structure
Stephen Trowbridge
Working Party 4
OTN Technology
Gastone Bonaventura
ITU-TSB
Counsellor
Paolo Rosa
Working Party 2
Network Signal Proc.
Yushi Naito
Working Party 1
Network Access
Andrew Nunn
Working Party 5
Projects and Promotion
Haruo Okamura

## Slide 7: ITU-T Study Group 15 WPs (1)
Working Party 1/15 - Network Access
2/15 Optical systems for access networks
3/15 Support for Systems based on ISDN Physical Layers
4/15 Transceivers for customer access and in-premises phone line networking systems on metallic pairs
Working Party 2/15 - Network Signal Processing
5/15 Compression and classification in signal processing network equipment
6/15 Speech enhancement in signal processing network equipment
7/15 Voice gateway equipment
8/15 Interaction aspects of signal processing network equipment

## Slide 8: ITU-T Study Group 15 WPs (2)
Working Party 3/15 – Optical Network Transmission Structure
9/15 Transport equipment and network protection/restoration
10/15 ATM and Internet Protocol (IP) equipment
11/15 Signal structures, I/F and I/W for transport networks
12/15 Technology Specific Transport Network Architectures
13/15 Network Synch. and Time Distribution Performance
14/15 Network management for transport systems and equipment
Working Party 4/15 – Optical Network Transmission Technology
15/15 Chars. and test methods of optical fibres and cables
16/15 Chars. of optical systems for terrestrial transport networks
17/15 Characteristics of optical components and subsystems
18/15 Characteristics of optical fibre submarine cable systems
Working Party 5/15 – Projects and Promotion
1/15 Access network transport
19/15 General characteristics of optical transport networks

## Slide 9: Overview of Access Technologies

## Slide 10: Typical Access Network Construction
Central Office
(Exchange)
Feeder Network
Street Cabinet
Distribution Network
Overhead
Feed
Underground
Feed

## Slide 11: Access technological evolution
Year
9.6 kbit/s
28.8 kbit/s
56.6 kbit/s
128 kbit/s
2 Mbit/s
640 kbit/s
8 Mbit/s
25 Mbit/s
50 Mbit/s
1989
1997
2000
Analog
modems
ISDN
HDSL/
ADSL
VDSL
OPTICAL
ACCESS
622 Mbit/s
G-PON
2003

## Slide 12: Capacity, technologies & availability
Source Siemens
There will never be enough! The bandwidth demand will continue to grow.
Fiber to the home will be necessary sooner or later.
ISDN
100
1k
10k
100k
1M
10M
100M
1G
1980
1990
2000
2010
2020
Year
Bit rate per user (
bit/s)
PSTN / Modem
ADSL
SDSL
FTTH
double in 18
mon
.
double in 24
mon
.
N.B. The technology bars show
the introduction, not the end of
the technology
VDSL,
FTTCab

## Slide 13: Optical access network architecture (G.983.1)
O
N
U
O
N
U
O
N
U
O
L
T
N
T
N
T
Fibre
Fibre
Fibre
Copper
Copper
HOME
Access network
SNI
FTTB/C
FTTCab
FTTH
Optical Distribution Network

## Slide 14: Characteristics of different access technologies
Technology
Definition
Bandwidth
Advantages
Disadvantages
ADSL
Asymmetric Digital Subscriber Line
Transmission of voice and data over copper
 Up to 8 Mbit/s downstream
 Up to 1.5 Mbit/s upstream
 Makes full use of existing copper
 Ideal for web-browsing
 Good platform for voice
 Limited video capability
 Distance limitation
 Limited upstream bandwidth
VDSL Very High Rate Digital Subscriber Line
Transmission of video, voice and data over copper
 Up to 52 Mbit/s downstream
 Up to 26 Mbit/s symmetrical
 Supports broadcast video, Video-on-demand, Internet TV, and interactive TV
 Offers always-on network for voice, video, and data
 Requires short distance
 Non-standard products and technology
 Limited scalability
µwave multipoint fixed services
Microwave transmission of video and data
Point-to-point or point-to-multipoint
 Up to 1 Gbit/s downstream and downstream
 Fast time-to-market
 Point-to-multipoint cells have limited geographical area
 Needs line of sight to complete transmission
HFC Hybrid Fibre/Coax
Transmission of video, voice, and data over coaxial and fibre cable
 10 to 42 Mbit/s downstream
 2 Mbit/s upstream
 Supports broadcast video, Video-on-demand, Internet TV, and interactive TV
 Offers always-on network for voice, video, and data
 Voice requires special engineering
 Difficult to guarantee speed
 High cost of upgrades and build-outs

## Slide 15: How hungry an application?
2
1
0.5
Upstream Mbit/s
0.5
1
2
8
4
Downstream Mbit/s
Business TV
Voice
e-commerce
Video conference
Internet access

## Slide 16: Optical Access

## Slide 17: Optical Systems for Access Networks Market & Business Drivers (1)
Getting PSTN, data and cable TV together on one system at competitive prices
Fibre To The Home (FTTH) is the next step for many operators
The major change is driven by the explosive growth of the Internet usage
Public and private networks evolve from multiple overlay networks to a unified network platform able to carry multiple applications

## Slide 18: Optical Systems for Access Networks Market & Business Drivers (2)
IP routers and ATM switches are providing higher and higher speed optical interfaces
Major carriers are realizing that services at STM-16 (2.5 Gbit/s) optical pipes may well represent more than 50% of the bulk bandwidth entering networks in the near future
The new high speed data requirements are requiring a new category of Wavelength Services
These new services will require new networking functions (performance monitoring, fault localization, network restoration, etc)

## Slide 19: Key aspects for optical technologies
IP over optical, business and market aspects
Switched optical networks
Optics in access and metropolitan networks
Optical interfaces
Optical/IP network OAM and protection and restoration
WDM and C&D-WDM
Signalling and routing
Optical fibres, cables and components
Optical network management
Optical switching equipment
Network performance (IP/Optical)
Optical network clients and services
Services and network evaluation
 Making fully-optical networks viable

## Slide 20: OTN Structure and Technology
Optical Transport Network (OTN) structure
  Automatic Switched Optical Network (ASON)
  Architecture and interfaces for the OTN
  Optical Cross-Connect and Switch functions
  Network management and control
OTN technology (terrestrial and submarine)
  Coarse and Dense WDM, 40 Gbit/s signal channels
  Optical components & amplifiers (e.g. tunable filters)
  Fiber characteristics, more channels/fiber
  Transmission technology (Soliton/RZ), long reach

## Slide 21: Evolution of Standardization – Fibres
TDM Systems
@ 1310 nm
TDM systems
@ 1550 nm
DWDM Systems
CWDM Systems
Fibre G.652
(zero-dispersion @ 1310 nm)
[1984]
[1988]
[1996]
[2000]
Fibre G.653
(zero-dispersion @ 1550 nm)
Fibre G.655
(low dispersion @ 1550 nm)
Fibre G.652.C
(zero dispersion @ 1310 nm)
(flat attenuation loss
from 1260 to 1625 nm)
TDM Systems
@ 850 / 1310 nm
Fibre G.651
multimode
[1980]

## Slide 22: Evolution of Standardization – Systems (1)
Recs. | Bit rate | Content | Date
G.955 | 140 Mbit/s | Single channel PDH Long. Compat. | 1984
G.957 | STM-16 | Single channel SDH transv. Compat. | 1998
G.691 | STM-4 up to STM-256 | Single channel Transv compat. Terminal OAs | 1994-2000

## Slide 23: Evolution of Standardization – Systems (2)
G.692 | 622 Mbit/s – 10 Gbit/s (STM-4 to STM-16) | WDM 4 to 32 ch Long. Compat. Line amplifiers mono/bidirect. | 1996 / 1998
G.959.1 | 2.5 and 10 Gbit/s Up to 16 channels WDM | Pre-OTN Single /WDM Transv Compat. Term. OAs Id Interfaces | 2000
G.693 | 10 – 40 Gbit/s (STM-64 to STM-256) | Single channel Transv. Compat. Intra office | 2001
G.694.1 G.694.2 | ≥ 80 Ch/10 Gbit/s Up to 18 Ch/2.5 Gbit/s | Dense WDM Coarse WDM | 2002

## Slide 24: OTN Standardization Work Plan
Global Optical Transport Network
Supporting Today's and Future Services
OTN
IrDI
OTN
IaDI
Carrier Domain A
Carrier Domain B
SDH
STM-N
USER
NE
USER
NE
OTN
IaDI
OTN
IaDI
OTN
IrDI
OTN
NE
OTN
NE
OTN
NE
User/carrier may originate/terminate the OTN framing for any digital payload
(IP, ATM, SDH,,,)
IaDI = Intra-Domain Interface
IrDI = Inter-Domain Interface
NE = Network Element
Interfaces:For single/multichannels with performance monitoring

## Slide 25: Single channel systems (G.957 and G.691)
G.957:
  only with electrical regenerators
  short distances, small capacities
G.691:
  Uses optical amplifiers only as Booster or Pre-amplifiers
  transversal compatibility
  bit rates up to STM-64 (10 Gbit/s)
  target distances (up to 160 km) based on 11dB/40km at 1550 nm and 11dB/20 km at 1310 nm
WAVELENGHT
1310
1550
1550
1310
1550
1550
1310
1550
1550
1550
1550
Fibre Type
G.652
G.652
G.653
G.652
G.652
G.653
G.652
G.652
G.653
G.652
G.653
Target Dist. (Km)
20
40
40
40
80
80
80
120
120
160
160
STM-1
-
-
-
-
-
STM-4
G.957
V-4.1
V-4.2
V-4.3
U-4.2
U-4.3
STM-16
V-16.1
V-16.2
V-16.3
U-16.2
U-16.3
STM-64
S-64.1
S-64.2
S-64.3
L-64.1
L-64.2
L-64.3
V-64.1
V-64.2
V-64.3
-
-

## Slide 26: Optical systems for access networks Broadband PON: G.983.x-series Recs.
Passive Optical Network up to 622 Mbit/s symmetrical / asymmetrical
Supports wide range of narrow- & broadband services like:
  PSTN / ISDN / Multiple Line
  Data / LAN interconnection / High speed Internet (~100 Mbit/s)
  Cable TV / Video on demand (up to 400 TV channels on single wavelength)
  Videoconferencing
Independent from bit rates, signal formats (digital or analogue, SONET/SDH etc.) and protocols (IP, Ethernet, ATM etc.)
Need to deploy only the equipment needed for specific services needs to be added at the ends of the network as needed to add new services to existing customers or to add new customers.
Notes: Summary of G.983 sub-series of B-PON Recommendations:
G.983.1: Broadband optical access systems based on Passive Optical Networks Specifies an optical access system with symmetrical line rates of 155.520 or 622.080 Mbit/s and asymmetrical line rates of 155.520 Mbit/s upstream and 622.080 Mbit/s downstream.
G.983.2: ONT management and control interface specification for B-PON Specifies requirements for the OMCI, managed entities of a protocol-independent Management Information Base and protocol/detailed messages for the ONT management and control channel.
G.983.3: A broadband optical access system with increased service capability by wavelength allocation Adds an additional wavelength band to a G.983.1 B-PON to enable the distribution of unidirectional or bidirectional video broadcast or data services.
G.983.4: A broadband optical access system with increased service capability using dynamic bandwidth assignment Specifies the enhancements to a G.983.1 B-PON to allow the use of dynamic bandwidth assignment.
G.983.5: A broadband optical access system with enhanced survivability Specifies protection features for a G.983.1 B-PON.
G.983.6: ONT management and control interface specifications for B-PON system with protection features Specifies the OMCI for a B-PON system with protection features.
G.983.7: ONT management and control interface specification for dynamic bandwidth assignment (DBA) B-PON system Specifies the OMCI for a B-PON system using dynamic bandwidth assignment.

## Slide 27: Optical systems for access networks G.984.x -series Recs (G-PON) – (01-2003)
Gbit/s capable PON systems
Symmetrical/Asymmetrical
1.244 and 2.488 Gbit/s downstream
155 Mbit/s up to 2.488 Gbit/s upstream
Business and residential users
Convenient support of IP and Ethernet
Same wavelength plan and full-network design principles as in G.983.x-series (B-PON)
New!
Notes: A passive optical network (PON) is a system that brings optical fibre cabling and signals all or most of the way to the end user in residential and new small/medium business networks. Gigabit-capable PONs will offer customers unprecedented data rates enabling applications such as video-on-demand, streaming video, on-line games, voice over IP and other high bandwidth capabilities.
The draft new standard G.gpon.gsr describes the general characteristics of a Gigabit-capable PON system such as architecture, bit rates, reach, signal transfer delay, split ratio, protection and security.
The second draft new standard G.gpon.pmd describes a flexible optical fibre access network capable of supporting the bandwidth requirements of business and residential services. It covers systems with nominal line rates of 1244.160 Mbit/s and 2488.320 Mbit/s in the downstream (Central Office to customer) direction and 155.520 Mbit/s, 622.080 Mbit/s, 1244.160 Mbit/s and 2488.320 Mbit/s in the upstream (customer to Central Office) direction. Both symmetrical and asymmetrical (upstream/downstream) systems are described.
Both draft new standards enhance the existing set of standards (G.983 series) on Passive Optical Network based access systems by providing unprecedented access network capacities that should satisfy any currently foreseeable customer demands.
A further GPON standard will describe the Transmission Convergence (TC) layer and the ranging protocol.

## Slide 28: Automatic Switched Optical Network (ASON)  G.8080
Architecture components and interactions between control plane, management plane and transport plane for switched wavelength & sub-wavelength connection services.
Functions:
  Facilitate fast & efficient configuration of connections within a transport layer network
  Re-configure connections to maintain calls
  Restoring functionCost-effective and survivable architectures
Adds dynamic capability to new optical networks or already established SDH networks
Fast turn-up and rapid provisioning; as well as wavelength-on-demand services to increase capacity and flexibility
Reduced operations cost: more accurate inventory & topology information, resource optimization and automated processes
Notes: ITU Press Release (http://www.itu.int/newsarchive/press_releases/2001.html)
The 40Gigabit per Second Phone Call: Global Standards for Automatically Switched Optical Networks Enable New Market Services
Geneva, 5 December 2001 — New global standards for Automatically Switched Optical Networks (ASON) and their control mechanisms have been adopted as a result of an aggressive work programme initiated by ITU to support bandwidth-on-demand applications. The standards, which add switching capability to the installed optical fibre infrastructure, were developed and agreed upon in less than a year.
"The ASON family of standards build on Optical Transport Network (OTN) standards completed earlier this year and move us towards the Optical Internet" said Peter Wery, Chairman of ITU-T Study Group 15. "They can create tremendous business opportunities for network operators and service providers, giving them the means to deliver end-to-end, managed bandwidth services efficiently, expediently and at reduced operational cost," Wery added. ASON standards can also be implemented to add dynamic capabilities to new optical networks or established SDH networks.
The expected business benefits include:
Increased revenue generating capabilities through fast turn-up and rapid provisioning; as well as wavelength-on-demand services to increase capacity and flexibility
 Increased return on capital from cost-effective and survivable architectures that help protect current and future network investments from forecast uncertainties
Reduced operations cost through more accurate inventory and topology information, resource optimization and automated processes that eliminate manual steps
ASON control mechanisms provide support for both switched wavelength and sub-wavelength connection services in transport networks to provide bandwidth on-demand. Wavelength connection services make use of an entire wavelength of light while sub-wavelength services use a channel within a wavelength.
The ASON control mechanisms also enable fast optical restoration. Traditionally, transport networks have used protection rather than restoration to provide reliability for connections. With protection, connections are moved to dedicated or shared routes in the event of a failure of a fibre or network equipment. With restoration, the endpoints can "redial" to re-establish the connection through an alternative route as soon as a loss of the original connection is detected. Restoration is a defined advantage for carriers as it makes better use of the network capacity and, with this new standard, it can be performed much faster than with most proprietary restoration systems available today.
These recommendations are an important step towards the completion of the ASON series of standards. Work ahead includes the addition of detailed protocol specifications and the expansion of features for interoperable network restoration.

## Slide 29: G.8080 Control Plane and Optical Layer
OCC
OCC
OCC
OCC
ASON Control Plane
Optical Layer
OS
OS
OS
OS
λs, STM-N granularity
OS = Optical Switch
OCC = Optical Connection Controller
Clients, e.g.
IP, ATM, TDM
Clients, e.g.
IP, ATM, TDM
NNI
CCI
UNI
IrDI NNI
IrDI
UNI = User Network I/F
NNI = ASON control Node-Node I/F
Optical Layer topology, status, control
CCI = Connection Control I/F
IrDI = Inter Domain I/F

## Slide 30: SDOs cooperating with ITU-T
Coperation:
ITU-T
IEC
ETSI
Competition:
IEC
IETF
IEEE
Fora, Consortia, etc
Relationships:
ATM Forum [traffic and networks management]
DSL Forum [Access network]
TM Forum [network management]
ATIS T1 [Access, SDH, OTN]
IETF [optical transport network]
IEEE [Ethernet, optical interfaces]
TIA [optical networks and technology]
OIF [optical networks and technology]

## Slide 31: Work in progress
Ethernet – PON combination for high bit rate
End-to-end wavelength services
OTN management Information Model (Protocol neutral and specific)
Terabyte/s in metropolitan and long haul transport
  Optical Internet
  Dense & Coarse WDM, PONs
Multi-Megabit/s and Gigabit/s network access
  Internet
  TV distribution and interactive

## Slide 32: xDSL Access

## Slide 33: xDSL Market & Business Drivers
xDSL technology allows the provision of high-speed Internet access and other broadband services over existing copper access lines
Incumbent operators need to exploit their large installed base of copper access lines for broadband deployment
Competing operators can exploit incumbent operators access lines via ‘unbundling’ agreements
Competition:
  Digital Cable / Cable Modem
  Bi-directional Satellite

## Slide 34: Typical components of an xDSL system
audio/video/data
POTS
Splitter
xDT
=
SN = Service Node
xDSL
xDT
xDSL
Transceiver
DTU-R =
Transceiver Unit- Remote
DTU-C =
xDSL
Transceiver Unit- Central office
U-R
T
CUSTOMER PREMISES
CENTRAL OFFICE
POTS
Splitter
xDT
U-C
SNI
• PSTN/ISDN
SN
• B-ISDN SN
• Non-ATM based SN
(e.g. - video server
- IP router)
(Subscriber line)
xDTU-R
xDTU-C
ADSL
ADSL lite
HDSL
SHDSL
VDSL

## Slide 35: Typical rates & loop lengths for xDSL

## Slide 36: ITU-T Recommendations on DSL
G.995.1 – Overview of Digital Subscriber Line (DSL) Recommendations
G.991.1 (HDSL) – High-bit rate Digital Subscriber Line (HDSL) transmission system on metallic local lines
G.991.2 (G.SHDSL) – Single-pair High bit rate speed Digital Subscriber Line
G.993.1 (G.VDSL) – Very high bit-rate Digital Subscriber Line
G.994.1, G.996.1 and G.997.1 for tests, management and handshake
ADSL  next slide

## Slide 37: ITU-T Recommendations on ADSL
G.992.1 (G.DMT) – Asymmetrical Digital Subscriber Line (ADSL) Transceivers
G.992.2 (G.LITE) – Splitterless Asymmetrical Digital Subscriber Line (ADSL) Transceivers
G.992.3 – Asymmetric digital subscriber line transceivers - 2 (ADSL2.DMT)
G.992.4 – Splitterless asymmetric digital subscriber line transceivers - 2 (ADSL2.LITE)

## Slide 38: ADSL versus ADSL2 (G.992.1 x G.992.3)
2nd generation of ADSL with improvements on:
  data rate versus loop reach performance
  loop diagnostics
  deployment from remote cabinets
  spectrum control
  power control
  robustness against loop impairments and RFI
  operations and maintenance
Improved application support for an all digital mode of operation and voice over ADSL operation;
Fallback compatibility (?) (if manufacturer opts)

## Slide 39: ADSL+ (01/2003)
G.adslplus  G.992.5?
A delta regarding ADSL2 (G.992.3)  DMT
Performance
Compatibility (but requires ADSL2)
Data rate on long distances
ADSL+ doubles the bandwidth and therefore can significantly increase data rates on short loops (extra bandwidth can only be used if the loop attenuation is low enough up to ~ 2.5–3 km).
Soon-to-be!

## Slide 40: Other Access Technologies

## Slide 41: Home Phone-line Networking Market & Business Drivers
Redeployment of existing infrastructure facilitates penetration
Potentially a large market as many homes now have more than one computer and need to share an internet connection and printer etc.
Network Operators see this as a stimulus for broadband deployment
Competition:
  Powerline networking
  WiFi (IEEE 802.11x)

## Slide 42: Relevant Recommendations
Done: G.989.1/G.989.2 – Home Phoneline Networking Transceivers
In progress: G.pnt.if – Phone-line Networking - Isolation Filter

## Slide 43: Things in progress in SG15
Network access
  Home networking (data on in-premises wiring)
  Refinements & enhancements xDSL
  Web-based ANT standardization plan
Optical Transport Network (OTN)
x-WDM and 40Gbit/s signal channels
  Optical Cross-Connect and Switch
  Fiber characteristics, more channels/fiber
  Transmission technology (Soliton/RZ)
  Network Node Interface for OTN
Continue as Lead Study Group on
  Access Network Transport
  Optical Technology

## Slide 44: Thank you for your attention!
For further contact, please feel free to contact:
Presenter: Simão Ferraz de Campos Neto
simao.campos@itu.int
Tel: +41-22-730-6805 Fax: +41-22-730-4345
Counsellor for SG 15: Paolo Rosa
Paolo.rosa@itu.int
Tel: +41-22-730-5235 Fax: +41-22-730-4345
http://www.itu.int/ITU-T

## Slide 45: Supplemental Slides

## Slide 46
Q.2/15 - Optical systems for access networks
Recommendations
G.983.1 + Amendment 1 - High speed optical access systems based on Passive Optical Network (PON) techniques
G.983.2 - ONT Management and Control Interface specification for ATM PON

## Slide 47
Q.2/15 - Optical systems for access networks
Recommendations (continued)
G.983.3 - A broadband optical access system with increased service capability by wavelength allocation
G.983.4 - A broadband optical access system with increased service capability using Dynamic Bandwidth Assignment

## Slide 48
Q.2/15 - Optical systems for access networks
Recommendations (continued)
G.983.5 - A broadband optical access system with enhanced survivability
G.983.7 - ONT Management and Control Interface specification for Dynamic Bandwidth Assignment

## Slide 49
G.983.1 + Amendment 1 - High speed optical access systems based on Passive Optical Network (PON) techniques
ATM-PON
155.520/155.520 Mbit/s, 622.080/155.520 Mbit/s or 622.080/622.080 Mbit/s downstream/upstream
Single or two fibre working
Maximum range of at least 20 Km

## Slide 50
G.983.3 - A broadband optical access system with increased service capability by wavelength allocation
Defines new wavelength allocations to distribute ATM-PON signals and additional service signals simultaneously
Allows distribution of video broadcast services or data services without disturbing basic ATM-PON system

## Slide 51
Q.2/15 - Optical systems for access networks
Current/future work
Enhancement of G.983.2 to support survivability (G.983.5) and new services
Enhancement of G.983.3 to include 622.080 Mbit/s upstream rate
Gigabit PON (2.48832 Gbit/s ?)

## Slide 52
Q.3/15 - Support for Recommendations Specifying Systems Based on ISDN Physical Layers
Currently working on:
Possible revision of of I.414 (Overview of Access Recommendations) as necessary to incorporate VB5 interface, and other recent new Recommendations in the area of access

## Slide 53
Q.4/15 - Transceivers for customer access and
in-premises phone line networking systems on metallic pairs
Recommendations
G.991.1 - High bit-rate Digital Subscriber Line (HDSL)
G.991.2 - Single-pair High-speed DSL (SHDSL)
G.992.1 - Asymmetrical DSL (ADSL)
G.992.2 - ‘Splitterless’ or ‘lite’ ADSL
G.992.3 - ASDL 2 (2nd generation ADSL)
G.992.4 - Splitterless or ‘lite’ ADSL 2

## Slide 54
Q.4/15 - Transceivers for customer access and
in-premises phone line networking systems on metallic pairs
Recommendations (continued)
G.993.1 - Very high bit rate DSL (VDSL) – Foundation
G.994.1 - DSL Handshaking procedures
G.995.1 - Overview of DSL Recommendations

## Slide 55
Q.4/15 - Transceivers for customer access and
in-premises phone line networking systems on metallic pairs
Recommendations (continued)
G.996.1 - DSL Testing procedures
G.997.1 - DSL Physical Layer management
G.989.1 - Phone-line Networking - Foundation
G.989.2 - Phone-line Networking - Payload format and Link Layer requirements

## Slide 56
G.991.1 - High bit-rate Digital Subscriber Line transceivers
Two wire bidirectional transceiver, three systems:
Two or three pairs, each 748 kbit/s
Two pairs, each 1168 kbit/s
One pair, 2320 kbit/s
Line Code - 2B1Q or CAP (Carrierless Amplitude and Phase modulation)

## Slide 57
G.991.2 - Single pair High-speed Digital Subscriber Line transceivers
Duplex (bidirectional) operation on one copper pair
Payload 192 kbit/s up to 2.312 Mbit/s
Optional 2 pairs: Payload 384 kbit/s up to 4.624 Mbit/s
Line Code - TC-PAM (Trellis Coded Pulse Amplitude Modulation)

## Slide 58
G.992.1 - Asymmetric Digital Subscriber Line transceivers
One twisted pair
Payload upstream up to 640 kbit/s
Downstream up to 6.144 Mbit/s
Simultaneous Voiceband and N-ISDN possible
Line Code - DMT (Discrete MultiTone)

## Slide 59
G.992.2 - Splitterless asymmetric digital subscriber line transceivers
One twisted pair
Payload downstream up to 1.536 Mbit/s
Upstream up to 512 kbit/s
Line Code - DMT (Discrete MultiTone)

## Slide 60
G.993.1 - Very high bit-rate Digital Subscriber Line transceivers
One twisted pair
Asymmetric and symmetric data rates up to tens of Mbit/s
Frequency Division Duplexing to separate upstream & downstream traffic
Three band plans defined occupying 138kHz up to 12 MHz

## Slide 61
G.989.1/G.989.2 – Home Phoneline Networking Transceivers
In-premises distribution of data over existing phoneline wiring
Nominal effective throughput equal to 10BASE-T Ethernet
Compatibility with other phoneline services such as POTS, V.90/V.92, ISDN and G.992.2
Spectrum notching for compatibility with Amateur Radio services

## Slide 62
Q.4/15 - Transceivers for customer access and in-premises phone line networking systems on metallic pairs
Current/future work
Revision of Single-pair High-speed DSL (SHDSL) - G.991.2
Second Generation ADSL
Second Generation‘Splitterless’ ADSL

## Slide 63
Q.4/15 - Transceivers for customer access and in-premises phone line networking systems on metallic pairs
Current/future work (continued)
Very high bit rate DSL (VDSL) – G.vdsl.l
Phone-line Networking - Isolation Filter – G.pnt.if
Voice over DSL
Bonding of DSL systems
Power Line Transmission (in-premises only)?

## Slide 64: G.991.2 (SHDSL) transceivers
  Multi-rate transmission technology
    duplex operation over only two-wire twisted metallic pairs. (G.991.1 is for 1-3 pairs).
  Symmetric data rates (scalable):
    One pair mode: 192 kbit/s to 2312 Kbit/s (single pair mode), in increments of 8 kbit/s, distance from 1.8 up to 6.5 km.
    Two-pair mode: 384 kbps to 4.624 Mbps
  Many Manufacturer’s options
    4-wire operation
    Repeaters, etc.

## Slide 65: G.993.1 (VDSL) transceivers
  Symmetric and asymmetric data rates
    Downstream as high as 5 to 20 Mbit/s
    Upstream 1.6, 2.3, 19 Mbit/s or equal to downstream in case of symmetric tx.
  American/Japanese/European Service Types (Annexes)
  300 – 1 500 m. reach