## Slide 1: JCTVC-G315 Unification of picture partitioning schemes
Muhammed Coban, Ye-Kui Wang, Marta Karczewicz, Ying Chen, In Suk Chong

## Slide 2: Proposal
A unification design for the different picture partitioning schemes
  Entropy slices
  Tiles
  Wavefront parallel processing (WPP)
Unification in the following senses
  Picture partitions contained in coded slices in the same way
  Cross-partition dependency control by a slice header flag in the same way
  Signaling of partition entry byte offsets, if needed, in the same way
  Association to the parent slice by slice ID in the same way

## Slide 3: The current picture partitioning schemes (1/2)
Four types of picture partitioning schemes
  Slices, entropy slices, tiles, WPP
All may be used for one or more of the following purposes
  Packetization or MTU size matching
  Parallel processing
  ME memory reduction
The designs
  One slice in one NAL unit, cross-partition in-picture prediction always disallowed
  One entropy slice in one NAL unit, cross-partition in-picture prediction always allowed
  One tile can be in 1) one NAL unit, 2) a part of a NAL unit, 3) multiple NAL units, or 4) a subset of multiple NAL units; cross-partition in-picture prediction can be either allowed or disallowed by a tile specific control parameter; byte offsets may be signaled by two alternative, tile specific methods
  One WPP wave (one LCU row within a tile/picture) can be in one NAL unit, 2) a part of a NAL unit, 3) multiple NAL units, or 4) a subset of multiple NAL units; cross-partition in-picture prediction always allowed; byte offsets may be signaled by a WPP specific method

## Slide 4: The current picture partitioning schemes (2/2)
Feature | Slices | Entropy Slices | Tiles | WPP
Independent parsing (of a partition) |  |  | (independent) x (dependent) |  (with some LCU delay)
Independent decoding |  | x | (independent) x (dependent) |  (with some LCU delay)
LCU order changing | x | x |  | x
Overhead | Slice header | Short Slice header | Byte offsets | Byte offsets

## Slide 5: Problems (1/3): non-unified designs
One slice in one NAL unit, cross-partition in-picture prediction always disallowed
One entropy slice in one NAL unit, cross-partition in-picture prediction always allowed
One tile can be in 1) one NAL unit, 2) a part of a NAL unit, 3) multiple NAL units, or 4) a subset of multiple NAL units; cross-partition in-picture prediction can be either allowed or disallowed by a tile specific control parameter; byte offsets may be signaled by two alternative, tile specific methods
One WPP wave (one LCU row within a tile/picture) can be in one NAL unit, 2) a part of a NAL unit, 3) multiple NAL units, or 4) a subset of multiple NAL units; cross-partition in-picture prediction always allowed; byte offsets may be signaled by a WPP specific method

## Slide 6: Problems (2/3)
The presence of cabac_init_idc depends on slice_type, which is not present in a short slice header. Thus, the short slice header itself cannot be parsed independently
A short slice header cannot be used for tiles and/or WPP, while it can be used for entropy slices
When the number of WPP sub-streams is greater than one, the bitstream causality (i.e., no earlier data depends on data coming later in bitstream/decoding order) is broken
The slice starting address is deeply buried in the slice header, not the first in slice header as in AVC

## Slide 7: Problems (3/3)
The slice address signaling consists of one flag and then optionally the slice address itself. This saves a few bits for the slice covering the top-left coding block, but wastes a bit for every other slice
When multiple byte-aligned coded tiles or WPP waves are included in a coded slice NAL unit to enable parallel processing, it may be ideal to send the same slice header to the different parallel decoding cores. However, currently the slice header is likely not byte aligned (i.e., it does not end at a byte-aligned position), which requires a transcoding process to make the slice header byte aligned, and each of the individual decoder cores to be able to handle transcoded non-standard compliant slice header
Byte alignment syntax is missing for multiple byte-aligned coded tiles or WPP waves included in a coded slice NAL unit

## Slide 8: Summary of the overall design of the proposal
Typically
  Each coded slice NAL unit contains only one entropy slice, coded tile or WPP wave.
  Tiles only determine LCU decoding order, cross-tile dependency is controlled by a new flag in the slice header.
  No signaling of entry points for tiles or WPP waves is needed.
Occasionally (when coded tiles or WPP waves are too small in size such that the overhead of NAL unit headers and short slice headers become non-trivial)
  Multiple byte-aligned coded tiles or WPP waves are included into one coded slice NAL unit.
  Byte offsets of the multiple entries are signaled using the slice-level entry offset SEI message.
Entropy slices are supported simply by allowing in-picture prediction across slices.
WPP waves must be ordered in the bitstream based on the starting LCU address.

## Slide 9: More details of the proposal (1/3)
SPS and PPS
  Same syntax as in JCTVC-F335 for tile
  Only the PPS syntax element entropy_coding_synchro as in JCTVC-F274 for WPP, and the semantics is the same but applies within each tile column
  Three new PPS syntax elements: short_slice_header_enabled_flag, dependent_slice_enabled_flag and slice_header_byte_aligned_flag

## Slide 10: More details of the proposal (2/3)
Slice header
  Short slice header may be applied regardless of which picture partitioning schemes are in use
  Cross-slice in-picture prediction control may be applied regardless of which picture partitioning schemes are in use
  When either short slice header or cross-slice in-picture prediction is possible, a slice ID is included in the slice header
    In this case, all slice NAL units of one coded picture with the same slice ID are collectively referred to as a parent slice
    This is in spirit the same as slice ID association of slice data partitions in AVC
  Slice header may be always byte-aligned
  slice_address is the first syntax element in slice headers, and first_slice_in_pic_flag is removed
  The presence of the cabac_init_idc syntax element no longer depends on the value of slice_type
  Signaling of entry point byte offsets, for either tiles or WPP sub-streams, is not included

## Slide 11: More details of the proposal (3/3)
Byte alignment syntax added to the slice_data( ) syntax structure
Syntax and semantics for the slice-level entry offset SEI message added, to convey the byte offsets of multiple coded tiles or WPP waves included in one coded slice NAL unit