## Slide 1: JCTVC-G319: Conforming bitstreams starting with CRA pictures
Ying Chen, Ye-Kui Wang, and Marta Karczewicz

## Slide 2: Introduction
In broadcasting, streaming, and multi-party video conferencing, random access points are frequently inserted
  Herein CRA outperforms IDR in coding efficiency
  Performing random access at CRA pictures is common, e.g., the recently finalized MPEG Dynamic Adaptive Streaming over HTTP (DASH) explicitly allows signaling of open-GOP random access points, which are effectively CRA pictures
  However, decoding from a CRA picture is not confirming
    It is not guaranteed that a conforming decoder may be able to handle random accessing from CRA pictures
    A practical problem: when the leading pictures are not present, is that the CPB may overflow, because the coded bits of pictures after the leading pictures in decoding order flow into the CPB earlier than when the leading pictures are not present, while the decoding times of these pictures are unchanged
Proposal
  To make a bitstream staring from a CRA picture conforming
  Convenient for decoder implementers
    Normative behaviors are clearly specified for random access from CRA pictures
    No unexpected decoding behaviors

## Slide 3: Examples of CRA picture and the corresponding leading pictures
CRA pictures: picture 8 (POC) and 16
Leading pictures
  Picture 1~7 for the CRA picture with POC 8
  Picture 9~15 for the CRA picture with POC 16

## Slide 4: More details of the proposal (1/2)
Definition of leading pictures
  leading picture: a coded picture associated with a CRA picture, that follows the CRA picture in decoding order but precedes the CRA picture in output order
Leading pictures may or may not be present in the bitstream starting with a CRA picture. When present, a leading picture is ignored in the decoding process
The CPB overflow problem and the solution
  When the leading pictures are not present, the CPB may overflow
    Bits of the pictures following the starting CRA picture in decoding order flow into the CPB earlier (than when the leading pictures are present)
    If the CPB removal times of these pictures are kept unchanged, the CPB may overflow
  Solution to this problem
    To shift earlier the decoding time of pictures following the starting CRA picture
    The time shift is signaled in the buffering period SEI message

## Slide 5: More details of the proposal (2/2)
Bitstream conformance requirement
  The first coded picture, in decoding order, of a conforming bitstream may be an IDR picture or a CRA picture
  For a conforming bitstream starting with a CRA picture, the bitstream subset generated by discarding the access units that contain any leading picture associated with the starting CRA picture, when present, shall still be a conforming bitstream (i.e. fulfill all the bitstream requirements)