## Slide 1
JCTVC-J0272: Simplifications of HRD parameters for Temporal Scalability
M. Haque, K. Sato, A. Tabatabai, T. Suzuki
July 10, 2012

## Slide 2: HEVC VUI with Extension Hooks – J0270, Option-1
vui_parameters( ) { | Descriptor
..... edited out .... | .......
vui_max_temporal_layers_minus1 | u(3)
for (i=0; i<=vui_max_temporal_layers_minus1; i++ ) { // iterative loop starts | 
temporal_id[i] | u(3)
field_seq_flag[i] | u(1)
timing_info_present_flag[i] | u(1)
if( timing_info_present_flag[i] ) { | 
num_units_in_tick[i] | u(32)
time_scale[i] | u(32)
fixed_pic_rate_flag[i] | u(1)
} | 
nal_hrd_parameters_present_flag[i] | u(1)
if( nal_hrd_parameters_present_flag[i] ) | 
hrd_parameters( ) | 
vcl_hrd_parameters_present_flag[i] | u(1)
if( vcl_hrd_parameters_present_flag[i] ) | 
hrd_parameters( ) | 
if( nal_hrd_parameters_present_flag[i] ¦ ¦ vcl_hrd_parameters_present_flag[i] ) { // ed - missing ? | 
low_delay_hrd_flag[i] | u(1)
sub_pic_cpb_params_present_flag[i] | u(1)
if( sub_pic_cpb_params_present_flag[i] ) | 
num_units_in_sub_tick[i] | u(32)
} | 
} // iterative loop ends for temporal layers | 
bitstream_restriction_flag | u(1)
if( bitstream_restriction_flag ) { | 
tiles_fixed_structure_flag | u(1)
motion_vectors_over_pic_boundaries_flag | u(1)
max_bytes_per_pic_denom | ue(v)
max_bits_per_mincu_denom | ue(v)
log2_max_mv_length_horizontal | ue(v)
log2_max_mv_length_vertical | ue(v)
} | 
vui_extension_flag | u(1)
if( vui_extension_flag ) { | 
while( more_rbsp_data() ) | 
vui_extension_data_flag | u(1)
} | 
rbsp_trailing_bits() | 
} | 

## Slide 3: Review of HRD syntax-parameters and Semantics
In SVC and MVC VUI syntax-structures,
  hrd_parameters() exist for each scalability (spatial/temproal/snr or view) layer
As HEVC, version -1 addresses temporal scalability, some common HRD parameters may exist among various temporal layers
  Variable length (1 parameter): cpb_cnt_minus1
    specifies number of alternative delivery schedules from the SchedSelIdx (HSS delivery Schedules Selected Idx) Subset values with restricted bit rate and CPB size
    So this parameter cannot be considered as a constant parameter for all temporal layers.
    Note: HSS - Hypothetical Stream Scheduler (HSS) operates for output timing decoder conformance
  Fixed length, 4-bit HRD parameters (2)
    bit_rate_scale: BitRate[ SchedSelIdx ] = ( bit_rate_value_minus1[ SchedSelIdx ] + 1 ) * 2(6 + bit_rate_scale)
    cpb_size_scale: CpbSize[ SchedSelIdx ] = ( cpb_size_value_minus1[ SchedSelIdx ] + 1 ) * 2(4 + cpb_size_scale)
    So both bit_rate_scale and cpb_size _scale can be made constant
hrd_parameters( ) { | Descriptor
cpb_cnt_minus1 | ue(v)
bit_rate_scale | u(4)
cpb_size_scale | u(4)
for( SchedSelIdx = 0; SchedSelIdx <= cpb_cnt_minus1; SchedSelIdx++ ) { | 
bit_rate_value_minus1[ SchedSelIdx ] | ue(v)
cpb_size_value_minus1[ SchedSelIdx ] | ue(v)
cbr_flag[ SchedSelIdx ] | u(1)
} | 
initial_cpb_removal_delay_length_minus1 | u(5)
cpb_removal_delay_length_minus1 | u(5)
dpb_output_delay_length_minus1 | u(5)
time_offset_length | u(5)
} | 

## Slide 4: From VUI HRD parameters Semantics Definition
Fixed length, 5-bit HRD parameters (4)
  initial_cpb_removal_delay_length_minus1
  cpb_removal_delay_length_minus1
  dpb_output_delay_length_minus1
  time_offset_length
From Semantics definition:
  "When the '*'_delay_length_minus1 (or, time_offset_length) syntax element is present in more than one hrd_parameters( ) syntax structure within the VUI parameters syntax structure, the value of the '*'_delay_length_minus1 (or, time_offset_length) parameters shall be equal in both hrd_parameters( ) syntax structures. When the '*'_delay_length_minus1 (or, time_offset_length) syntax element is not present, it is inferred to be equal to 23 (24 for time_offset_length)."
  When the SEs not present, all of them = 23, except time_offset_length = 24
Given the above semantics definition, we may consider all these four syntax parameters of “*_delaay_length_minus1* and “time_offset_length” to remain constant for all temporal-layers (similar buffer properties for all layers)

## Slide 5: hrd_parameters() modifications
hrd_parameters_var( ) { | Descriptor
cpb_cnt_minus1 | ue(v)
for( SchedSelIdx = 0; SchedSelIdx <= cpb_cnt_minus1; SchedSelIdx++ ) { | 
bit_rate_value_minus1[ SchedSelIdx ] | ue(v)
cpb_size_value_minus1[ SchedSelIdx ] | ue(v)
cbr_flag[ SchedSelIdx ] | u(1)
} | 
} | 
hrd_parameters_fixed( ) { | Descriptor
bit_rate_scale | u(4)
cpb_size_scale | u(4)
initial_cpb_removal_delay_length_minus1 | u(5)
cpb_removal_delay_length_minus1 | u(5)
dpb_output_delay_length_minus1 | u(5)
time_offset_length | u(5)
} | 
HRD parameters syntax structure can be split up into two parts:
hrd_parameters_fixed()
  the same for all temporal layers with constant parameters
  There could be 2 options for this hrd_parameters_fixed() structure:
    Option-1: A single hrd_parameters_fixed() structure for both NAL and VCL HRD cases
    Option-2: Two separate hrd_parameters_fixed() structures for NAL and VCL HRD cases – hrd_parameters_fixed_nal() and hrd_parameters_fixed_vcl().
      Both these syntax structures contain identical syntax parameters as in hrd_parameters_fixed(), but with different values perhaps.
b) hrd_parameters_var() - it will be changing according to each temporal layer requirements.

## Slide 6: Modified VUI Extension – Option 1
vui_parameters( ) { | Descriptor
..... edited out .... | .......
vui_max_temporal_layers_minus1 | u(3)
hrd_parameters_fixed( ) // Fixed HRD parameters for all temporal layers | 
for (i=0; i<=vui_max_temporal_layers_minus1; i++ ) { // iterative loop starts | 
temporal_id[i] | u(3)
field_seq_flag[i] | u(1)
timing_info_present_flag[i] | u(1)
if( timing_info_present_flag[i] ) { | 
num_units_in_tick[i] | u(32)
time_scale[i] | u(32)
fixed_pic_rate_flag[i] | u(1)
} | 
nal_hrd_parameters_present_flag[i] | u(1)
if( nal_hrd_parameters_present_flag[i] ) | 
hrd_parameters_var( ) | 
vcl_hrd_parameters_present_flag[i] | u(1)
if( vcl_hrd_parameters_present_flag[i] ) | 
hrd_parameters_var( ) | 
if( nal_hrd_parameters_present_flag[i] ¦ ¦ vcl_hrd_parameters_present_flag[i] ) { // ed - missing ? | 
low_delay_hrd_flag[i] | u(1)
sub_pic_cpb_params_present_flag[i] | u(1)
if( sub_pic_cpb_params_present_flag[i] ) | 
num_units_in_sub_tick[i] | u(32)
} | 
} // iterative loop ends for temporal layers | 
bitstream_restriction_flag | u(1)
if( bitstream_restriction_flag ) { | 
tiles_fixed_structure_flag | u(1)
motion_vectors_over_pic_boundaries_flag | u(1)
max_bytes_per_pic_denom | ue(v)
max_bits_per_mincu_denom | ue(v)
log2_max_mv_length_horizontal | ue(v)
log2_max_mv_length_vertical | ue(v)
} | 
vui_extension_flag | u(1)
if( vui_extension_flag ) { | 
while( more_rbsp_data() ) | 
vui_extension_data_flag | u(1)
} | 
rbsp_trailing_bits() | 
} | 

## Slide 7: Modified VUI Extension – Option 2
vui_parameters( ) { | Descriptor
..... edited out .... | .......
vui_max_temporal_layers_minus1 | u(3)
hrd_parameters_fixed_nal( ) // Fixed HRD parameters for all temporal layers | 
hrd_parameters_fixed_vcl( ) // Fixed HRD parameters for all temporal layers | 
for (i=0; i<=vui_max_temporal_layers_minus1; i++ ) { // iterative loop starts | 
temporal_id[i] | u(3)
field_seq_flag[i] | u(1)
timing_info_present_flag[i] | u(1)
if( timing_info_present_flag[i] ) { | 
num_units_in_tick[i] | u(32)
time_scale[i] | u(32)
fixed_pic_rate_flag[i] | u(1)
} | 
nal_hrd_parameters_present_flag[i] | u(1)
if( nal_hrd_parameters_present_flag[i] ) | 
hrd_parameters_var( ) | 
vcl_hrd_parameters_present_flag[i] | u(1)
if( vcl_hrd_parameters_present_flag[i] ) | 
hrd_parameters_var( ) | 
if( nal_hrd_parameters_present_flag[i] ¦ ¦ vcl_hrd_parameters_present_flag[i] ) { // ed - missing ? | 
low_delay_hrd_flag[i] | u(1)
sub_pic_cpb_params_present_flag[i] | u(1)
if( sub_pic_cpb_params_present_flag[i] ) | 
num_units_in_sub_tick[i] | u(32)
} | 
} // iterative loop ends for temporal layers | 
bitstream_restriction_flag | u(1)
if( bitstream_restriction_flag ) { | 
tiles_fixed_structure_flag | u(1)
motion_vectors_over_pic_boundaries_flag | u(1)
max_bytes_per_pic_denom | ue(v)
max_bits_per_mincu_denom | ue(v)
log2_max_mv_length_horizontal | ue(v)
log2_max_mv_length_vertical | ue(v)
} | 
vui_extension_flag | u(1)
if( vui_extension_flag ) { | 
while( more_rbsp_data() ) | 
vui_extension_data_flag | u(1)
} | 
rbsp_trailing_bits() | 
} | 
Two separate hrd_parameters_fixed( )
structures for NAL and VCL HRD parameters