## Slide 1
Cheung Auyeung
Teruhiko Suzuki
Sony Electronics Inc
July 1, 2012
Request to establish an AHG to reduce computation in residual coding
Notes: 1

## Slide 2: Complexity Reduction of Residual Coding
Based on Sony software team analysis, the residual coding is one of the more computational intensive component in the HEVC decoder.
We would like to request JCTVC to establish an AHG to reduce software complexity in residual coding.
This is an attempt to initiate work to reduce the amount of software computation in residual coding.

## Slide 3: Software Complexity in Residual Coding
The HM7 residual coding consists of four loops:
  significant_coeff_flag loop
  coeff_abs_level_greater1_flag loop
  coeff_sign_flag loop
  coeff_abs_level_remaining loop
It is a challenge to speedup or parallelize the residual coding loop by software in the decoder for the following reasons:
  There are multiple branches within the loop in (1), (2), and (3).
  There are data dependency among adjacent data within the loop in (2) and (4).
  The loop counts in the four loops could be all different.

## Slide 4: Software Execution Time Reduction in Residual Coding
Software execution time reduction in residual coding can be achieved by the following approaches
  Merge the four coding loops into fewer coding loops.
  Change the algorithms in residual coding to reduce the branches within each loop.
  Change the algorithms in residual coding to reduce data dependency on previously process data within each loop.
This contribution is an attempt to speedup execution time by merging some of the coding loops in residual coding.

## Slide 5: Loop Reduction in residual_coding
HM7
Propose to merge the two loops to prepare for more efficient software implementation.
significant_coeff_flag
coeff_abs_level_greater1_flag
significant_coeff_flag
coeff_abs_level_greater1_flag

## Slide 6: BDR of Merged Loop
Merged the significant_coeff_flag and coeff_abs_level_greater1_flag loops into one loop in HM7.
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class B | 0.00% | 0.00% | 0.00% | 0.01% | 0.01% | 0.01%
Class C | 0.01% | 0.01% | 0.01% | 0.01% | 0.01% | 0.01%
Class D | 0.01% | 0.01% | 0.01% | 0.01% | 0.01% | 0.01%
Class E | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Overall | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.01%
 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
Enc Time[%] |  |  |  |  |  | 
Dec Time[%] |  |  |  |  |  | 
Execution time is not accurate and it is not reported here.

## Slide 7: Appendix

## Slide 8: JCTVC-I1003_d4 Syntax
residual_coding( x0, y0, log2TrafoWidth, log2TrafoHeight, scanIdx, cIdx ) { | Descriptor
… | 
… | 
for( n = 15; n >= 0; n− − ) { | 
xC = ScanOrder[ log2TrafoWidth ][ log2TrafoHeight ][ scanIdx ][ n + offset ][ 0 ] | 
yC = ScanOrder[ log2TrafoWidth ][ log2TrafoHeight ][ scanIdx ][ n + offset ][ 1 ] | 
if( (n + offset) < (numCoeff − 1) && significant_coeff_group_flag[ xCG ][ yCG ] && ( n > 0 ¦ ¦ implicitNonZeroCoeff = = 0 ) ) { | 
significant_coeff_flag[ xC ][ yC ] | ae(v)
if( significant_coeff_flag[ xC ][ yC ] = = 1 ) | 
implicitNonZeroCoeff = 0 | 
} | 
} | 
firstNZPosInCG = 16 | 
lastNZPosInCG = −1 | 
numSigCoeff = 0 | 
firstGreater1CoeffIdx = −1 | 
for( n = 15; n >= 0; n− − ) { | 
xC = ScanOrder[ log2TrafoWidth ][ log2TrafoHeight ][ scanIdx ][ n + offset ][ 0 ] | 
yC = ScanOrder[ log2TrafoWidth ][ log2TrafoHeight ][ scanIdx ][ n + offset ][ 1 ] | 
if( significant_coeff_flag[ xC ][ yC ] ) { | 
if( numSigCoeff < 8 ) { | 
coeff_abs_level_greater1_flag[ n ] | ae(v)
numSigCoeff++ | 
if( coeff_abs_level_greater1_flag[ n ] && firstGreater1CoeffIdx = = −1 ) | 
firstGreater1CoeffIdx = n | 
} | 
if( lastNZPosInCG = = −1) | 
lastNZPosInCG = n | 
firstNZPosInCG = n | 
} | 
} | 
… | 
… | 

## Slide 9: Proposed Syntax
The proposed text changes from JCTVC-I1003_d4 is highlighted in yellow.
residual_coding( x0, y0, log2TrafoWidth, log2TrafoHeight, scanIdx, cIdx ) { | Descriptor
… | 
… | 
firstNZPosInCG = 16 | 
lastNZPosInCG = −1 | 
numSigCoeff = 0 | 
firstGreater1CoeffIdx = −1 | 
for( n = 15; n >= 0; n− − ) { | 
xC = ScanOrder[ log2TrafoWidth ][ log2TrafoHeight ][ scanIdx ][ n + offset ][ 0 ] | 
yC = ScanOrder[ log2TrafoWidth ][ log2TrafoHeight ][ scanIdx ][ n + offset ][ 1 ] | 
if( (n + offset) < (numCoeff − 1) && significant_coeff_group_flag[ xCG ][ yCG ] && ( n > 0 ¦ ¦ implicitNonZeroCoeff = = 0 ) ) { | 
significant_coeff_flag[ xC ][ yC ] | ae(v)
if( significant_coeff_flag[ xC ][ yC ] = = 1 ) | 
implicitNonZeroCoeff = 0 | 
} | 
if( significant_coeff_flag[ xC ][ yC ] ) { | 
if( numSigCoeff < 8 ) { | 
coeff_abs_level_greater1_flag[ n ] | ae(v)
numSigCoeff++ | 
if( coeff_abs_level_greater1_flag[ n ] && firstGreater1CoeffIdx = = −1 ) | 
firstGreater1CoeffIdx = n | 
} | 
if( lastNZPosInCG = = −1) | 
lastNZPosInCG = n | 
firstNZPosInCG = n | 
} | 
} | 
… | 
… |