## Slide 1: Non-TE5: Inter-layer Intra MPM derivation for EL in SHVC
Jun Xu, Ali Tabatabai
SONY

## Slide 2: Proposal
SMuC 0.1.1
  SVC_BL_CAND_INTRA enables BL co-located intra mode for MPM derivation.
  MPMs are derived from BL co-located CU and neighboring CUs. But sometimes neighbors are not available including Inter or IntraBL.
    SMuC sets unavailable neighbors as DC mode.
Proposed solution
  SVC_BL_CAND_INTRA is enabled to use BL co-located intra mode for MPM derivation.
  When deriving MPMs, each neighboring CU
    If neighboring CU is IntraBL
      If neighboring CU co-located BL is intra coded,
        use neighboring CU co-located BL intra mode
      Otherwise,
        use DC mode
    Otherwise,
      use intra mode of neighboring CU in EL

## Slide 3: Diagram
Intra
IntraBL
EL
BL
Intra
IntraBL
MPMs
derivation
DC
Proposed solution
SMuC0.1.1
+ SVC_BL_CAND_INTRA
co-located
co-located
co-located
Intra: intra mode
Inter: DC
Intra: intra mode
Inter: DC
Intra: intra mode
Inter: DC

## Slide 4: Performance
Thanks to Canon for cross-checking.
  MDCS on
  MDCS off
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.23% | -0.04% | 0.06% |  |  | 
Class B | -0.34% | -0.16% | -0.17% | -0.13% | 0.11% | 0.09%
Overall (EL+BL) | -0.31% | -0.12% | -0.10% | -0.13% | 0.11% | 0.09%
Overall (EL) | -0.55% | -0.16% | -0.12% | -0.32% | 0.33% | 0.29%
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.17% | 0.09% | 0.16% |  |  | 
Class B | -0.18% | 0.05% | 0.13% | -0.12% | 0.13% | 0.14%
Overall (EL+BL) | -0.18% | 0.06% | 0.14% | -0.12% | 0.13% | 0.14%
Overall (EL) | -0.33% | 0.13% | 0.26% | -0.30% | 0.37% | 0.40%

## Slide 5: Conclusion
New MPM derivation is proposed to use BL intra mode for both current and neighboring CU.
Coding efficiency is improved.
Recommend to adopt this solution.