## Slide 1: JCTVC-N0150: AHG-17: AhG17: complexity analysis of SHM2.0
Elena Alshina
Alexander Alshin
Samsung Electronics, Ltd

## Slide 2: SHM2.0 performance
BD-rate relative to HM10.1 single layer |  |  |  |  |  |  |  | 
Y | U | V | Y | U | V | Y | U | V
AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
12,8% | 14,9% | 14,6% | 10,5% | 9,8% | 9,3% |  |  | 
RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
19,2% | 33,3% | 32,0% | 16,2% | 28,8% | 29,1% | 14,4% | 32,1% | 34,1%
LD-B HEVC 2x |  |  | LD-B HEVC 1.5x |  |  | LD-B HEVC SNR |  | 
28,5% | 39,0% | 39,7% | 24,8% | 33,0% | 35,9% | 24,3% | 34,7% | 39,5%
LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
26,6% | 38,0% | 39,1% | 22,8% | 32,8% | 35,6% | 23,4% | 34,6% | 39,4%
There is 12…28% BD-rate drop of scalable system compare to single layer codec
Drop for Luma typically smaller than for Chroma
Smallest drop in All-Intra, biggest in LD-B scenario

## Slide 3: Processes with memory access
---------HEVC------------------
MC:
  Reading from reference frame (random place access)
Out-put:
  Writing of reconstructed data
---------SHVC------------------
PU-based inter-layer processing ( “on a fly”):
  Reading reconstructed BL frame (random place access)
PU-based inter-layer processing (“true RefIdx”):
  Reading reconstructed BL frame (regular access)
  Writing to the additional reference frame
MV mapping
  Reading of MV data (very low)
---------Block extension----------------
Regular access
  only vertical block extension is needed
Random access
  both vertical and horizontal block extension are needed
Writing
  No extension is needed

## Slide 4: Two possible implementations
Picture-based inter-layer processing
PU-based inter-layer processing
The worst case is illustrated on this slide

## Slide 5: Complexity assessment in SNR test (picture based inter-layer processing)
Open issue since last meeting
  Scaling ratio between BL and EL pictures is 1
    No re-scaling is needed
  But BL and EL picture sizes could be different (“scaled reference layer offset” adopted from JCTVC-M0309 )
    Cannot just redirect the pointer to reconstructed BL and create inter-layer reference
Solution so far
  Assume that reconstructed BL picture is copied (==1taps filtering)  overestimated
  Keep complexity assessment of “BL pointer” in a template  under estimated

## Slide 6: The worst case memory access
Relatively to HEVC single layer |  |  |  | 
spatial scalability ×1,5 |  | SNR scalability |  | 
PU-based processing | Picture processing | PU-based processing | Picture processing (copy) | Picture processing (pointer)
145% | 160% | 200% | 218% | 200%
2 layers scalable SHM2.0 complexity in the worst case equivalent to 2 layers simulcast HEVC decoding (assuming PU-based inter-layer processing)
Picture based inter-layer processing implementation requires 15…18% higher memory access in a worst case compare to PU-based inter-layer processing

## Slide 7: Average memory access
Relatively to HEVC single layer |  |  |  |  |  | 
Scalability | SPATIAL |  |  | SNR |  | 
 | Pure | DDR2 | DDR3 | Pure | DDR2 | DDR3
PU-based | 111% | 106% | 106% | 97% | 98% | 98%
Picture-based | 163% | 152% | 158% | 161% | 158% | 161%
2 layers scalable SHM2.0 complexity in average equivalent (103%) to single layer HEVC decoding (assuming PU-based inter-layer processing)
Picture based inter-layer processing implementation requires ×1,5 higher memory access in average compare to a worst case compare to single layer HEVC decoding
Picture based relatively to PU-based | SPATIAL |  |  | SNR |  | 
 | Pure | DDR2 | DDR3 | Pure | DDR2 | DDR3
 | 148% | 146% | 152% | 166% | 161% | 164%

## Slide 8: Comments on SCE3 tools
Test | spatial |  |  |  |  |  | SNR |  |  |  |  | 
 | BD-rate |  | Memory Avg |  | Worst |  | BD-rate |  | Memory Avg |  | Worst | 
 | Luma | Chroma | PU | Pic | PU | Pic | Luma | Chroma | PU | Pic | PU | Pic
SHM2.0 | 0,00 | 0,00 | 108% | 157% | 145% | 160% | 0,00 | 0,00 | 98% | 160% | 200% | 218%
3.1 fixed |  |  |  |  |  |  | -1,29 | -0,85 | 98% | 161% | 200% | 219%
3.1Pic | -0,14 | -0,02 | 107% | 157% | 145% | 160% | -1,47 | -0,25 | 98% | 161% | 200% | 219%
3.1PU | -0,18 | 0,01 | 106% | 218% | 145% | 204% | -1,85 | -0,12 | 97% | 220% | 200% | 237%
3.1PicLn0 | -0,30 | -0,03 | 107% | 161% | 145% | 160% | -1,47 | -0,25 | 98% | 161% | 200% | 219%
3.1PULn0 | -0,50 | 0,27 | 106% | 218% | 145% | 204% | -1,85 | -0,12 | 97% | 220% | 200% | 237%
3.2AUF | -0,27 | -0,49 | 107% | 157% | 145% | 160% | -1,98 | -1,40 | 97% | 163% | 200% | 220%
3.3ILSAO | -0,50 | -0,51 | 110% | 157% | 145% | 160% | -1,64 | -1,26 | 101% | 159% | 200% | 220%
3.4.1 | -0,40 | -8,44 | 108% | 158% | 145% | 160% | -0,29 | -6,55 | 99% | 160% | 200% | 219%
3.4.2 | -0,40 | -8,23 | 109% | 159% | 145% | 160% | -0,29 | -6,54 | 99% | 164% | 200% | 219%
3.5.1BLF | -0,43 | -0,02 | 108% | 228% | 145% | 204% |  |  |  |  |  | 
2 inter-layer references in picture-based inter-layer processing implementation

## Slide 9: Conclusions
Memory access assessment results are reported for scalable 2 layers SHM2.0 system relatively to single layer HEVC decoder.
In the worst case memory usage by scalable codec
  is twice higher compare to single layer decoder (assuming PU-based inter-layer processing)  equivalent 2 layers simulcast decoding;
  is ×2,2 higher compare to single layer decoder (assuming Picture-based inter-layer processing)  noticeable exceed 2 layers simulcast decoding.
Actual memory access estimated using SHM2.0 bit-streams
  is ~3% higher compare to single layer decoder if PU-based inter-layer processing is implemented;
  is ~50% higher compare to single layer decoder if Picture-based inter-layer processing is implemented.