## Slide 1: Non-RCE4: Refinement of the palette in RCE4 Test 2 Wei Pu, Feng Zou, Joel Sole, Marta Karczewicz, Rajan Joshi

## Slide 2: TABLE OF CONTENT
Overview
Technical Description

## Slide 3: Overview
RCE4 Test 2
  Stage 1:
    Derive palette;
  Stage 2:
    “Run mode”;
    “Copy above mode”;
    “Pixel mode” (escape mode)

## Slide 4: Technical Description
Skip the Index Coding when Palette has One Entry
  If palette has only one color,
    All Index = 0;
    Skip Index Coding.
Skip the Index Coding when Palette has One Entry

## Slide 5
Skip the Coding of Escape Flag (I)
for (each pixel x in the CU)
{
Code a flag indicating whether x is escape;
if (x is escape)
{
code x with ‘pixel mode’;
}
else
{
code x with ‘run mode’ or ‘copy above mode’;
}
}

## Slide 6
Skip the Coding of Escape Flag (II)
if (palette size < 32)
 No escape pixel exists
 Don’t need to code escape flag

## Slide 7
Escape Pixel Coding in ‘Pixel Mode’
  MSB coded using single context
  Other bits coded bypass
  Removal of the Escape Pixel Prediction
  Escape pixel prediction is disabled in ‘pixel mode’
  Reducing the Fixed Length Coding Bit-Depth
  According to QP

## Slide 8: Results (Lossy, RCE4 Test 2 as Anchor)
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.9% | -1.8% | -1.7% | -0.6% | -1.0% | -1.1% | -0.5% | -0.5% | -0.5%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -3.6% | -2.6% | -2.7% | -3.2% | -2.7% | -2.6% | -2.7% | -2.3% | -2.4%
RGB 4:4:4 Animation | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0%
YCbCr 4:4:4 SC | -2.4% | -3.5% | -4.0% | -2.7% | -3.6% | -4.1% | -2.6% | -3.3% | -3.7%
YCbCr 4:4:4 Animation | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -3.5% | -3.5% | -3.7% | -4.1% | -4.2% | -4.2% | -4.4% | -4.4% | -4.5%
YCbCr 4:4:4 SC (Optional) | -1.6% | -1.0% | -0.8% | -1.2% | -0.7% | -1.0% | -1.1% | -0.9% | -1.2%

## Slide 9: Results (Lossy, RCE4 Test 2 as Anchor)
 | Random Access Main-tier |  |  | Random Access High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.5% | -1.2% | -1.1% | -0.4% | -0.6% | -0.6%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -2.5% | -1.7% | -1.7% | -1.5% | -1.1% | -1.1%
RGB 4:4:4 Animation | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0%
YCbCr 4:4:4 SC | -1.9% | -2.6% | -3.1% | -1.8% | -2.4% | -2.9%
YCbCr 4:4:4 Animation | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -0.5% | -0.4% | -0.8% | -0.6% | -0.6% | -0.6%
YCbCr 4:4:4 SC (Optional) | 0.1% | 2.1% | 2.2% | 0.1% | 1.6% | 1.0%

## Slide 10: Results (Lossy, RCE4 Test 2 as Anchor)
 | Low delay B Main-tier |  |  | Low delay B High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.1% | -1.0% | -0.3% | 0.0% | -0.3% | -0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -0.6% | -0.5% | -0.6% | -0.5% | -0.5% | -0.5%
RGB 4:4:4 Animation | -0.1% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -0.7% | -0.7% | -1.1% | -0.6% | -0.6% | -1.0%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 0.0% | -0.1% | -0.2% | -0.4% | -0.4% | -0.3%
YCbCr 4:4:4 SC (Optional) | -0.6% | 0.1% | 0.0% | -0.4% | 0.2% | -0.2%

## Slide 11
Thanks