## Slide 1: JCTVC-T0061 Non-CE: Efficient Coding for Static CTUs of Screen Content
Weinong Huang, Yong Yan

## Slide 2: Introduction
Static CTU:
  A CTU has no change from its reference frame and its reconstruction is just a copy from its co-located area in reference frames.
Static Slice:
  All CTUs in one slice are static CTUs and all CTUs have same reference frame.
Redundancy in CABAC bins for static CTU and static slice
  In H.265 SCC, a static CTU is always coded as skip mode, which needs one split flag, one skip flag and one merge index. So one static CTU needs to code at least 3 bins in CABAC process, and it could code up to 6 bins if multiple merge candidates are available. If a CTU is on the edge of the picture and only part of CTU is within that picture, more bins are needed to code the edge CTU.
  It could be more efficient to represent the static CTU with one flag and use 1 bin to code the flag.
  If one slice is a static slice and all CTUs have same bin-pattern, that slice can be coded as 1-bit flag in slice segment header.

## Slide 3: The Proposal: Static CTU
A CTU can be coded as a Static CTU when that CTU meet all the following conditions:
  For non-edge CTU, the split depth of CTU is 0. For edge CTU, no further split for all CUs within that edge CTU.
  The prediction mode is MODE_INTER.
  The prediction residual is 0 for both Luma and Chroma.
  All motion vectors are 0.
  The prediction partition size is 2Nx2N.
  The reference frame index is always 0 for both P slice and B slice.
  The prediction direction is always 0 (Uni_Direction_0) for P slice and 2 (Bi_Direction) for B slice.
Detection of static CTU can be in the R-D searching process or after the R-D searching process.
If done after the R-D searching process, no extra memory bandwidth or PSNR change.

## Slide 4: The Proposal: Static Slice
If all CTUs in one slice can be coded as static CTUs, that slice is one static slice.
Static slice will disable the de-blocking filter and SAO filter within the slice because these operations have been done for each CTU in the reference frame. It’s not necessary to repeat these operations in static slice.

## Slide 5: Proposed Syntax Change
In SPS SCC extension section, one flag, static_ctu_coding_enabled_flag, is added to indicate if Static CTU coding is enabled for current sequence.
In PPS SCC extension section, one flag, static_ctu_coding_enabled_flag, can be added to indicate if Static CTU coding is enabled for current frame if needed.
In CTU syntax, one extra flag, static_ctu_flag, is added to indicate if current CTU is one static CTU.
In slice segment header, a few more flags are added in order to represent one static slice properly. One flag (static_slice_flag) is used to indicate if current slice is a static slice. If that flag is true, another flag, slice_is_full_frame_flag, is used to indicate if current slice is also a full frame. If that flag is false, one variable is used to indicate the size of current slice.

## Slide 6: Advantages
Improved compression efficiency for static CTU and static slice.
Provided an efficient way to compress a skipped frame or slice.
Could be used to improve the encoding and decoding time for the static CTU and static Slice.

## Slide 7: Test Results for lossy Low-Delay
Data Source: Placeholder
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.1% | -0.2% | -0.2%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.2% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.3% | -0.4% | -0.4%
YUV, mixed content, 1440p & 1080p | -0.4% | -0.5% | -0.5%
YUV, Animation, 720p | 0.1% | 0.1% | 0.1%
YUV, camera captured, 1080p | 0.1% | 0.1% | 0.1%
Enc Time[%] | 99% |  | 
Dec Time[%] | 99% |  | 

## Slide 8: Questions ?

## Slide 9: Thank You