## Slide 1
1. Summary
2. Proposed Method
3. Experimental Results
4. Conclusion
Contents
3D-CE6.h related: Rate Distortion Optimized Selection between Non-Zero Residual and All-Zero Residual in Intra Coding of Depth (JCT2-A0087)
2012-07-16
China TV Lab. / Media Part
Hongbin Liu, Jie Jia, Sehoon Yea, Jin Heo, Eunyong Son
(LG Electronics)

## Slide 2: Summary
Proposed method
  Perform rate distortion optimized selection between non-zero residual and all-zero residual in intra mode coding of depth
  No syntax is changed
Performance
  -0.1% BD-rate gain on “coded and synthesized view” on average
  Negligible influence on encoding/decoding time
Crosscheck
  JCT2-A0127 (by MediaTek)
JCT2-A0087

## Slide 3: Proposed Method
Motivation
  If residual of depth has small impact or no impact on quality of synthesized view, bits spent on it can be saved
Proposed
  Perform rate distortion optimized selection between non-zero residual and all-zero residual for each PU in intra mode coding of depth
  Only applied to the first picture of each intra period
  No syntax is changed
JCT2-A0087

## Slide 4: Experimental Results
Table 1. Results of 3 view-case
Simulation
 | synthesized only | coded & synthesized | enc time | dec time
Balloons | -0.1% | -0.1% | 97.0% | 100.4%
Kendo | -0.1% | -0.2% | 98.7% | 100.5%
Newspapercc | 0.0% | -0.1% | 99.2% | 99.7%
GhostTownFly | -0.6% | -0.5% | 100.9% | 100.5%
PoznanHall2 | 0.0% | 0.0% | 100.5% | 101.4%
PoznanStreet | -0.1% | -0.1% | 101.0% | 102.9%
UndoDancer | -0.1% | -0.1% | 100.8% | 100.8%
1024x768 | -0.1% | -0.1% | 98.3% | 100.2%
1920x1088 | -0.2% | -0.2% | 100.8% | 101.4%
average | -0.1% | -0.1% | 99.7% | 100.9%
JCT2-A0087

## Slide 5: Experimental Results
Table 2. Results of 2 view-case
Simulation
 | synthesized only | coded & synthesized
Balloons | 0.0% | 0.0%
Kendo | -0.2% | -0.3%
Newspapercc | -0.1% | -0.1%
GhostTownFly | -0.6% | -0.5%
PoznanHall2 | 0.1% | 0.0%
PoznanStreet | -0.1% | -0.1%
UndoDancer | -0.1% | -0.1%
1024x768 | -0.1% | -0.1%
1920x1088 | -0.2% | -0.2%
average | -0.2% | -0.2%
JCT2-A0087

## Slide 6: Conclusion
Propose method
  Perform rate distortion optimized selection between non-zero residual and all-zero residual in intra mode coding of depth
  No syntax is changed
Performance
  -0.1% BD-rate gain on average
  Negligible influence on encoding/decoding time
It is recommended to adopt proposed method into 3DV-HTM
JCT2-A0087