## Slide 1
CE4.h Results on depth distortion metric
with a weighted depth fidelity term (JCT3V-B0131)
10. 13. 2012
Jiwook Jung, Sehoon Yea (LG)

## Slide 2
Problems of the current depth-coding metric (HHI_VSO)
  Cares only about view synthesis quality
  Assume a specific view renderer (VSO) and synthesis view
  Biased coded-depth quality to specific view synthesis conditions
  Often lead to undesirable synthesis artifacts under different conditions
  Suggest to also consider the fidelity of coded-depth itself
Introduction

## Slide 3
Depth distortion metric with a weighted depth fidelity term
  The depth distortion metric function is modified as follows:
: total depth distortion (for mode decision)
: distortions in synthesis and depth domains, respectively
: weights for distortions in synthesis and depth domains, respectively
  The weight of depth distortion is determined heuristically
  The weighting factors are squared where the distortion metric is SSE.
Proposed Method

## Slide 4
Objective result using VSRS 1D Fast
Anchor : HTM-4.1 WVSO Off
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.7% | 1.1% | 101.3% | 101.4%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 1.4% | 2.3% | 102.6% | 101.4%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.6% | 99.7% | 100.9%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | -0.6% | -0.4% | 98.5% | 103.1%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.5% | 0.7% | 101.0% | 106.0%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.3% | 101.6% | 100.1%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | -1.0% | -0.7% | 101.2% | 100.5%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.7% | 1.3% | 101.2% | 101.2%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | 0.0% | 100.6% | 102.4%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.6% | 100.8% | 101.9%

## Slide 5
Objective result using VSRS 3.5
Anchor : HTM-4.1 WVSO Off
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.3% | 0.9% | 101.3% | 101.4%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | -0.5% | 1.1% | 102.6% | 101.4%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | -3.7% | -1.9% | 99.7% | 100.9%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | -5.8% | -3.8% | 98.5% | 103.1%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.5% | 0.7% | 101.0% | 106.0%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.2% | 101.6% | 100.1%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | -10.4% | -7.3% | 101.2% | 100.5%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | -1.3% | 0.0% | 101.2% | 101.2%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | -3.9% | -2.5% | 100.6% | 102.4%
average | 0.0% | 0.0% | 0.0% | 0.0% | -2.8% | -1.4% | 100.8% | 101.9%

## Slide 6
Objective result – Depth PSNR (cubic)
Anchor : HTM-4.1 WVSO Off
 | depth 0 | depth 1 | depth 2 | Depth average
Balloons | -60.1% | -71.4% | -69.1% | -66.9%
Kendo | -73.2% | -86.0% | -91.9% | -83.7%
Newspapercc | -45.0% | -79.1% | -70.4% | -64.8%
GhostTownFly | -100.0% | -91.7% | -91.2% | -94.3%
PoznanHall2 | -48.8% | -69.0% | -72.5% | -63.4%
PoznanStreet | -34.9% | -48.4% | -50.8% | -44.7%
UndoDancer | -85.1% | -68.5% | -87.0% | -80.2%
1024x768 | -59.4% | -78.8% | -77.1% | -71.8%
1920x1088 | -67.2% | -69.4% | -75.4% | -70.7%
average | -63.3% | -74.1% | -76.3% | -71.2%

## Slide 7
Subjective result – QP 25, synth_view_pos = 0.25
 | HTM-4.1 WVSO Off | HTM-4.1 WVSO On
Left Coded Depth |  | 
VSRS3.5 |  | 

## Slide 8
Conclusion
Under the CTC, depth distortion metric (VSO) can cause undesirable artifacts in various synthesis scenarios.
Undesirable depth distortion and severe artifact on synthesis video can be removed by adding a weighted depth fidelity term into depth metric function explicitly.
The average synthesis BD-rate changes of proposed method were 0.2% and -2.8% when the renderer is VSRS1DFast and VSRS3.5, respectively
It is recommended that WVSO be adopted into the CTC