## Slide 1: Comments on MV-HEVC WD6 and SHVC WD4 (JCTVC-P0079 / JCT3V-G0092)
Hahyun Lee
Jan., 2014

## Slide 2: Introduction
The following issues are proposed
  Derivation of the variable NumActiveRefLayerPics
  Clean-up of profile, tier and level information
  Semantics of “vps_number_layer_sets_minus1” in the VPS extension.

## Slide 3: The derivation of the variable NumActiveRefLayerPics
The variable NumActiveRefLayerPics is derived as follows in the current text
The variable NumActiveRefLayerPics is derived as follows:
if( nuh_layer_id = = 0 | | NumDirectRefLayers[ nuh_layer_id ] = = 0 ) NumActiveRefLayerPics = 0 else if( all_ref_layers_active_flag ) NumActiveRefLayerPics = numRefLayerPics else if( !inter_layer_pred_enabled_flag ) NumActiveRefLayerPics = 0 else if( max_one_active_ref_layer_flag | | NumDirectRefLayers[ nuh_layer_id ] = = 1 ) NumActiveRefLayerPics = refLayerPicFlag[ 0 ] ? 1 : 0 else NumActiveRefLayerPics = num_inter_layer_ref_pics_minus1 + 1
All slices of a coded picture shall have the same value of NumActiveRefLayerPics.
The variables numRefLayerPics and refLayerPicFlag[i] and refLayerPicIdc[j] are derived as follows:
for( i = 0, j = 0; i < NumDirectRefLayers[ nuh_layer_id ]; i++ ) { refLayerIdx = LayerIdxInVps[ RefLayerId[ nuh_layer_id ][ i ] ] refLayerPicFlag[ i ] = ( sub_layers_vps_max_minus1[ refLayerIdx ] >= TemporalId ) && ( max_tid_il_ref_pics_plus1[ refLayerIdx ][ LayerIdxInVps[ nuh_layer_id ] ] > TemporalId ) if( refLayerPicFlag[ i ] ) refLayerPicIdc[ j++ ] = i }
numRefLayerPics = j

## Slide 4: The derivation of the variable NumActiveRefLayerPics
Problem
  When “max_one_active_ref_layer_flag” is equal to 1 or NumDirectRefLayers[nuh_layer_id] is equal to 1, the value of NumActiveRefLayerPics depends on the value of refLayerPicFlag[0]
  However, when “max_one_active_ref_layer_flag” is equal to 1, it specifies that at most one picture is used for inter-layer prediction for each picture in the CVS but does not guarantee that NumDirectRefLayers is always equal to 1.
  When “max_one_active_ref_layer_flag” is equal to 1, the following case is possible
    NumDirectRefLayerPics[nuh_layer_id] == 2
    refLayerPicFlag[0] == 0 and refLayerPicFlag[1] == 1
  In this case, even though there is an actual reference picture that can be used in decoding of the current picture for inter-layer prediction, the variable NumActiveRefLayerPics is equal to be 0 by current derivation process

## Slide 5: The derivation of the variable NumActiveRefLayerPics
Proposals
  Alternative 1
  Alternative 2
The variable NumActiveRefLayerPics is derived as follows:
if( nuh_layer_id = = 0 | | NumDirectRefLayers[ nuh_layer_id ] = = 0) NumActiveRefLayerPics = 0 else if( all_ref_layers_active_flag ) NumActiveRefLayerPics = numRefLayerPics else if( !inter_layer_pred_enabled_flag ) NumActiveRefLayerPics = 0 else if( max_one_active_ref_layer_flag | | NumDirectRefLayers[ nuh_layer_id ] = = 1 ) NumActiveRefLayerPics = numRefLayerPics > 0 ? 1: 0 else NumActiveRefLayerPics = num_inter_layer_ref_pics_minus1 + 1
All slices of a coded picture shall have the same value of NumActiveRefLayerPics.
Or, the variable NumActiveRefLayerPics is derived as follows:
if( nuh_layer_id = = 0 | | numRefLayerPics = = 0) NumActiveRefLayerPics = 0 else if( all_ref_layers_active_flag ) NumActiveRefLayerPics = numRefLayerPics else if( !inter_layer_pred_enabled_flag ) NumActiveRefLayerPics = 0 else if( max_one_active_ref_layer_flag | | NumDirectRefLayers[ nuh_layer_id ] = = 1 ) NumActiveRefLayerPics = 1 else NumActiveRefLayerPics = num_inter_layer_ref_pics_minus1 + 1
All slices of a coded picture shall have the same value of NumActiveRefLayerPics.

## Slide 6: Clean-up of profile, tier and level information
Problem
  In the previous meeting, JCTVC-O0109 indicated that the syntax element “profile_ref_minus1[i]” is broken when i is equal to 1 and the syntax element “vps_profile_present_flag[1]” is equal to 0.
  From BoG discussion, modification of the semantics of “profile_ref_minus[i]” to replace “shall be less than i” with “shall be less than or equal to i”.
  However, the syntax element “profile_ref_minus1[i]” is broken as ever, when i is equal to 1 and “vps_profile_present_flag[1]” is equal to 0.
    Modified semantics of “profile_ref_minus1[i]” makes that profile and tier information for the 1st profile_tier_level() syntax structure is inferred to be equal to the profile and tier information for 1st profile_tier_level() syntax structure.
    Also, since no other layer in the same bitstream can conform to any version 1 profile, profile and tier information for the 1st profile_tier_level() syntax structure can not be inferred to be equal to the profile and tier information for the 0th profile_tier_level() syntax structure.
  Therefore, the constraint is needed for semantics of “vps_profile_present_flag[i]”
profile_ref_minus1[ i ] specifies that the profile and tier information for the i-th profile_tier_level( ) syntax structure is inferred to be equal to the profile and tier information for the ( profile _ref_minus1[ i ] + 1 )-th layer set. The value of profile_ref_minus1[i] + 1 shall be less than or equal to i.

## Slide 7: Clean-up of profile, tier and level information
Proposal
vps_profile_present_flag[i] equal to 1 specifies that the profile and tier information is present in the i-th profile_tier_level( ) syntax structure. vps_profile_present_flag[i] equal to 0 specifies that profile and tier information is not present in the i-th profile_tier_level( ) syntax structure and is inferred. The value of vps_profile_present_flag[1] for 1st profile_tier_level() syntax structure shall be equal to 1.
profile_ref_minus1[i] specifies that the profile and tier information for the i-th profile_tier_level( ) syntax structure is inferred to be equal to the profile and tier information for the ( profile _ref_minus1[i] + 1 )-th profile_tier_level() syntax structure. The value of profile_ref_minus1[i] + 1 shall be less than or equal to i.

## Slide 8: Semantics of vps_number_layer_sets_minus1
Current semantics
Motivation
  A layer set 0 consists of a layer with nuh_layer_id equal to 0 (i.e., the value of numLayersInIdList[0] is set equal to 1 and the value of layerSetLayerIdList[0][0] is set equal to 0)
  MV-HEVC/SHVC bitstream has to have more than two layers
  Therefore, in MV-HEVC or SHVC profile, it is clear that there should be more than two layer sets
Proposal
  The value of vps_number_layer_sets_minus1 shall be in the range of 1 to 1023
vps_number_layer_sets_minus1 plus 1 specifies the number of layer sets that are specified by the VPS. The value of vps_number_layer_sets_minus1 shall be in the range of 0 to 1023, inclusive, and shall be equal to vps_num_layer_sets_minus1.
vps_number_layer_sets_minus1 plus 1 specifies the number of layer sets that are specified by the VPS. The value of vps_number_layer_sets_minus1 shall be in the range of 1 to 1023, inclusive, and shall be equal to vps_num_layer_sets_minus1.

## Slide 9
Thank you !