## Slide 1: JCTVC-G264: Adaptive Resolution Coding (ARC)
Thomas Davies (Cisco)
Pankaj Topiwala (FastVDO)

## Slide 2: Summary
Simple resolution adaption proposed in JCTVC-F158 by reference frame resampling
Changing resolution is valuable
  - for reducing complexity
  - matching resolution to a display
  - bandwidth reduction
Implemented here with matched up- and down-sampling filters
Performance results for ARC
  Compared with QP increase with and without prefiltering
Gains in HE configurations for classes A, B, E

## Slide 3: Proposal

## Slide 4: Proposal
Temporal MV prediction
disabled when resolutions
are different

## Slide 5: Inserted IDRs are bad with low delay ...

## Slide 6: ... Predicting at lower resolution is better

## Slide 7: Filters and prediction
Use matched pair of separable FIRs for up- and down-scaling by factor 2:
  Down-scaling: (1 0 -3 0 10 16 10 0 -3 1)/32
  Up-scaling: (-1 0 5 8 5 0 -1)/8
These filters are just for prediction: any filters can be used for up- and down-sampling the current picture (including adaptive)
Signal a Picture Resolution Index (PRI) in the PPS
When a reference picture has a different PRI to the current picture, re-scale the reference
  Turn off temporal MV prediction in this case

## Slide 8: Q: Is reducing resolution the best way to reduce bandwidth?
The experiment:
  Code at moderate to high QP
  Lose some frames (5) due to network congestion
  Reduce bandwidth by
    reducing resolution
    increasing QP
    half-band prefiltering and increasing QP
  Compare
Issue: value of resolution change is dependent on content, tools and prediction structure

## Slide 9: Q: Is reducing resolution the best way to reduce bandwidth?
The experiment:
  Code at moderate to high QP (32, 35, 39, 42)
  Lose some frames (5) due to network congestion
  Reduce bandwidth by
    adaptively reducing resolution
    increasing QP
    half-band prefiltering and increasing QP
  Compare
Threshold method for selecting resolution

## Slide 10: Threshold-based resolution selection
Not proposing an algorithm for selecting resolution
Rough heuristic for predicting a cross-over point of the low- and high- resolution R-D curves
  Luma PSNR is computed at high (PSNR[0]) and low (PSNR[1]) resolution
  A threshold T is computed by T= 0.7 + H/900
  Resolution will be switched when consistently
    PSNR[1] – PSNR[0] < T

## Slide 11: Results: ARC versus QP+6
BD-rate (%) | High Efficiency |  | 
Class | RA | LB | LP
Class A | -6.9 | - | -
Class B | -4.5 | -3.6 | -3.6
Class C | 0.0 | 0.0 | 0.0
Class D | 0.0 | 0.0 | 0.0
Class E |  | -1.7 | -2.1
Average | -2.9 | -1.5 | -1.5
BD-Rate at high resolution
Best: -24.6% (SteamLocomotive, RA); -11.7% (Kimono, LB), -12.1% (Kimono, LP)
Chroma loss of around 0.5-1.0dB for low resolution case
Run-times reduced by 14-31% on average (70/60% when low res)

## Slide 12: Results: forced resolution change versus prefiltering
BD-rate (%) | High Efficiency |  | 
Class | RA | LB | LP
Class A | -8.6 | - | -
Class B | -4.7 | -1.4 | 0.3
Class C | -6.9 | -3.7 | -3.3
Class D | 0.5 | 5.0 | 7.1
Class E |  | -2.1 | -3.5
Average | -4.9 | -0.5 | 0.4
BD-Rate at high resolution
Best: -25.2% (SteamLocomotive, RA); -10.0% (Kimono, LB), -10.6% (Kimono, LP)

## Slide 13: Results ARC versus prefiltering and QP+6
BD-rate (%) | High Efficiency |  | 
Class | RA | LB | LP
Class A | -8.6 |  | 
Class B | -12.7 | -12.4 | -12.8
Class C | -13.4 | -15.4 | -16.0
Class D | -12.6 | -10.0 | -12.5
Class E |  | -9.8 | -11.1
Average | -11.9 | -12.0 | -13.2
BD-Rate at high resolution
NB: these gains include gains of QP increase over prefiltering