## Slide 1: Complexity analysis of high throughput CABAC Entropy codecs JCTVC-H0489
Alberto Dueñas, Prashant Arora , Oscar Patino and Francisco Javier Roncero

## Slide 2: Background
The need for a high throughput CABAC entropy codec scheme was identified at the 7th JCT-VC meeting
It has been traditionally challenging to identify a reliable method to analyze the implementation complexity
This contribution outlines a method that analyzes the implementation complexity of different entropy codec methods

## Slide 3: Steps to create a method to analyze the implementation complexity
A reliable scheme to analyze the implementation complexity of different entropy codec methods needs to focus on the worst case scenarios
An implementation of an entropy codec method will need to operate satisfactory in all cases
Current common conditions and software reference configurations may suitable to analyze the implementation complexity of different entropy codec methods

## Slide 4: Example: analysis of HM5
In the current design the syntax elements of a residual block are as follows:
These syntax elements will be the most commonly used in the worst case scenarios
The highlighted ones use coded bins. The coeff_abs_level has two codec bins and one codec bin per coefficient for significant_coeff_flag
This indicates that the worst case scenarios for the current WD5 entropy codec method happens when we have 3 coded bins per coefficient
last_significant_coeff_x, last_significant_coeff_y | 
significant_coeff_flag | 
coeff_abs_level_greater1_flag | 
coeff_abs_level_greater2_flag | 
coeff_abs_level_minus3 | 
coeff_sign_flag | 

## Slide 5: Example of the analysis of HM5 (2)
The following assumptions have been used in this analysis:
  Traditionally there are 1.5 bins per coded bit
  Traditionally 1 bin can be processed per clock cycle on the decoding process
  16x16 TU size is used for simplification
  4:2:0 Chrominance format is used, therefore 1.5 coefficients per pixel
  A video sequence with 1200*1920 resolution is used for simplification

## Slide 6: Example of the analysis of HM5 (3)
The worst case for 1920 by 1200 high resolution sequence is 622 080 000 bins per second
  3*16*16*1.5*9000*60 = 622 080 000 bins per second
Using our assumption of 1.5 bins per processed bit
For any bit rate that is lower than 414.7 megabits per second, all the coefficient bins could actually be codec bins and no by-pass bins are used
We use the assumption that 1 coded bin can be processed per cycle on the decoding process
The current entropy codec method on the worst case scenarios under analysis for bit rates below 414.7 megabits per second will need 1.5 cycles per bit
At the worst case bit-rate of 414.7 Mbps, this implies a clock frequency of 622 MHz, that is 1.5 cycle per bit
At a nominal frequency of 250 MHz, the maximum bitrate would be limited to 166 Mbps

## Slide 7: Conclusions and recommendations
It is most important to take into account the worst case scenario
This contribution suggests the need to create a reliable methodology
This contribution recommends enhancing the common conditions and software reference configurations
This contribution suggests the creation of a breakout group (BoG) in order to discuss technical analysis of the complexity of different high throughput CABAC Entropy codec

## Slide 8: Thank You