## Slide 1
Extension of HEVC VUI Syntax Structure
Munsi Haque
April 17, 2012

## Slide 2: On VUI Extension - Proposal
Motivation
  High level syntax merging for the “base” HEVC VUI parameters to include its future extensions for Scalability, Multi-view Coding and others
  As “base” VUI syntaxes are borrowed from AVC, SVC and MVC VUI extension parameters are also considered for this extension
  Efficient VUI syntax structure design in a unified fashion
Highlights in Extension VUI parameters
  A Generic type of extension to include HEVC VUI-extension parameters
  A single1-bit-flag to differentiate the extension part from “base”
  Address various combinations of scalability and multi-view coding

## Slide 3: Current HEVC VUI (CD)
timing_info_present_flag | u(1)
if( timing_info_present_flag ) { | 
num_units_in_tick | u(32)
time_scale | u(32)
fixed_pic_rate_flag | u(1)
} | 
nal_hrd_parameters_present_flag | u(1)
if( nal_hrd_parameters_present_flag ) | 
hrd_parameters( ) | 
vcl_hrd_parameters_present_flag | u(1)
if( vcl_hrd_parameters_present_flag ) | 
hrd_parameters( ) | 
if( nal_hrd_parameters_present_flag ¦ ¦ vcl_hrd_parameters_present_flag ) | 
low_delay_hrd_flag | u(1)
bitstream_restriction_flag | u(1)
if( bitstream_restriction_flag ) { | 
motion_vectors_over_pic_boundaries_flag | u(1)
max_bytes_per_pic_denom | ue(v)
max_bits_per_mincu_denom | ue(v)
log2_max_mv_length_horizontal | ue(v)
log2_max_mv_length_vertical | ue(v)
} | 

## Slide 4: Comparison between HEVC VUI & AVC-SVC and MVC VUI-extension parameters
Comparison between HEVC VUI & AVC-SVC and MVC VUI-extension parameters (Annexes E, G.14, H.14) |  |  |  | 
On Syntaxes | HEVC | SVC | MVC | Comment
Additional syntax | x | vui_ext_num_entries_minus1 : ue(v) | vui_mvc_num_ops_minus1 : ue(v) | # of iterations
Iterative Loop, i | i = 0 | i = 0 to vui_ext_num_entries_minus1 | i = 0 to vui_mvc_num_ops_minus1 | 
New syntaxes | x | vui_ext_temporal_id[ i ] : u(3) | vui_mvc_temporal_id[ i ] : u(3) | 
 | x | vui_ext_dependency_id[ i ] : u(3) | vui_mvc_num_target_output_views_minus1[ i ] : ue(v) | # of next syntax view_id in MVC case
 | x | vui_ext_quality_id[ i ] : u(4) | vui_mvc_view_id[ i ][ j ] : ue(v) | j=0 to vui_mvc_num_target_output_views_minus1[ i ]
Common syntaxes | timing_info_present_flag | vui_ext_timing_info_present_flag[ i ] | vui_mvc_timing_info_present_flag[ i ] | 
 | num_units_in_tick | vui_ext_num_units_in_tick[ i ] | vui_mvc_num_units_in_tick[ i ] | 
 | time_scale | vui_ext_time_scale[ i ] | vui_mvc_time_scale[ i ] | 
 | fixed_frame_rate_flag | vui_ext_fixed_frame_rate_flag[ i ] | vui_mvc_fixed_frame_rate_flag[ i ] | For HEVC, frame->pic
 | nal_hrd_parameters_present_flag | vui_ext_nal_hrd_parameters_present_flag[ i ] | vui_mvc_nal_hrd_parameters_present_flag[ i ] | 
 | vcl_hrd_parameters_present_flag | vui_ext_vcl_hrd_parameters_present_flag[ i ] | vui_mvc_vcl_hrd_parameters_present_flag[ i ] | 
 | low_delay_hrd_flag | vui_ext_low_delay_hrd_flag[ i ] | vui_mvc_low_delay_hrd_flag[ i ] | 
 | pic_struct_present_flag | vui_ext_pic_struct_present_flag[ i ] | vui_mvc_pic_struct_present_flag[ i ] | For HEVC, discard this syntax

## Slide 5: New HEVC VUI with Extensions
vui_flags_byte[0] | u(8)
if((vui_flags_byte[0] & 0x1) == 0) // no vui_extension | 
vui_num_entries = 1 | 
else // vui_extensions | 
vui_num_entries | ue(v)
for (i=0; i< vui_num_entries; i++) { // iterative loop starts | 
if((vui_flags_byte[i] & 0x01) > 0) { // vui_extensions - ID cases | 
vui_ temporal_id[ i ] | u(3)
if( i >0) vui_flags_byte[i] | u(8)
if((vui_flags_byte[i] & 0x06) == 0x02) { // Scalable video only | 
vui_dependency_id[ i ] | u(3)
vui_quality_id[ i ] | u(4)
} | 
if((vui_flags_byte[i] & 0x06) == 0x04) { // Multi-view video only | 
vui_ num_target_output_views_minus1[ i ] | ue(v)
for( j = 0; j <= vui_num_target_output_views_minus1[ i ]; j++ ) | 
vui_view_id[ i ][ j ] | ue(v)
} | 
if((vui_flags_byte[i] & 0x06) == 0x06) { // 3DV: Combined MVC/SVC | 
<< Undefined >> | 
} | 
} // end of vui-extension - ID cases | 
if((vui_flags_byte[i] & 0x08) > 0) { // timing_info_present_flag | u(3)
vui_num_units_in_tick[ i ] | u(32)
vui_time_scale[ i ] | u(32)
} | 
if((vui_flags_byte[i] & 0x20) > 0) // nal_hrd_parameters_present_flag | 
hrd_parameters( ) | 
if((vui_flags_byte[i] & 0x40) > 0) // vcl_hrd_parameters_present_flag | 
hrd_parameters( ) | 
} // iterative loop ends | 
if((vui_flags_byte[0] & 0x05) == 0x04) { // bitstream_restriction_flag: Base only | 
motion_vectors_over_pic_boundaries_flag | u(1)
max_bytes_per_pic_denom | ue(v)
max_bits_per_mincu_denom | ue(v)
log2_max_mv_length_horizontal | ue(v)
log2_max_mv_length_vertical | ue(v)
} | 

## Slide 6: Addition of a new syntax
vui_flags_byte[i], a 1-byte long syntax parameter
  Combines common flags in HEVC VUI and its possible extensions
  One 1-bit flag (vui_ext_flag) to differentiate: 0 (base), 1 (extension)
  Distribution of other 7-bits
    For “base”
      5 bits for common 1-bit flags
      1-bit for “bitstream_restriction_flag”
      1-bit “reserved”
    For “extension”
      2-bits (vui_ext_flags2bits) for “extension-types” (Scalability, MVC, 3DV, etc.)
      5-bits for common 1-bit flags
  vui_flags_byte[i], an Array?
    For “base”, a single parameter (i=0)
    For “extension”, an array (i = 0 to vui_num_entries-1)
      1st choice for 2-bits of vui_ext_flags2bits
        For 1st element (i=0), may be enough for “extension-types”
        For other elements (i=1 to vui_num_entries-1), can be “reserved”
        For simplified choice, same values for all elements
      Other choice for2-bits of vui_ext_flags2bits
        Allow varied “extension types” or “combinations” from one iteration to next for VUI-parameters extension

## Slide 7: vui_flags_byte Example : VUI flags Grouping & Extension hooks
vui_flags_byte[i], p=assigned bit | HEVC (Base), i=0 | HEVC (Scalability Extension), i=0 to vui_num_entries-1 | HEVC (Multi-view Extension), i=0 to vui_num_entries-1 | Conditional logics
0000 000p | vui_ext_flag (p=0) | vui_ext_flag (p=1) | vui_ext_flag (p=1) | (vui_flags_byte & 0x01) > 0
0000 00p0 | reserved | vui_ext_flag2bits - 1st bit | vui_ext_flag2bits - 1st bit | (vui_flags_byte & 0x02) > 0
0000 0p00 | bitstream_restriction_flag | vui_ext_flag2bits - 2nd bit | vui_ext_flag2bits - 2nd bit | Base: (vui_flags_byte & 0x05) == 0x04; Ext: (vui_flags_byte & 0x04) == 0x04;
0000 p000 | timing_info_present_flag | timing_info_present_flag | timing_info_present_flag | (vui_flags_byte & 0x08) > 0
000p 0000 | fixed_pic_rate_flag | fixed_pic_rate_flag | fixed_pic_rate_flag | (vui_flags_byte & 0x18) == 0x18
00p0 0000 | nal_hrd_parameters_present_flag | nal_hrd_parameters_present_flag | nal_hrd_parameters_present_flag | (vui_flags_byte & 0x20) > 0
0p00 0000 | vcl_hrd_parameters_present _flag | vcl_hrd_parameters_present _flag | vcl_hrd_parameters_present _flag | (vui_flags_byte & 0x40) > 0
p000 0000 | pic_struct_present_flag | pic_struct_present_flag | pic_struct_present_flag | (vui_flags_byte & 0x80) > 0
 | low_delay_hrd_flag | low_delay_hrd_flag | low_delay_hrd_flag | (vui_flags_byte & 0x60) > 0
An interim parameter, vui_ext_flag2bits = ((vui_flags_byte >> 1) & 0x03), not a syntax parameter |  |  | 
vui_ext_flag2bits |  | HEVC Extension type | Conditional logics
0 | 0 | reserved | (vui_flags_byte & 0x06) == 0x00
0 | 1 | svc extension | (vui_flags_byte & 0x06) == 0x02
1 | 0 | mvc extension | (vui_flags_byte & 0x06) == 0x04
1 | 1 | combined svc & mvc (3DV) | (vui_flags_byte & 0x06) == 0x06