## Slide 1: AHG6: Comparison of block adatpive (BA) and region adaptive (RA) ALF (JCTVC-I0363)

## Slide 2: AHG6/CE2 activity on ALF
Option 2 ALF
  Picture level coefficients in APS
    Using previous frame
    Block adaptive (BA) vs. region adaptive (RA) mode
      BA: 4x4 block based, direction and activity
      RA: divide picture into 16 regions
  LCU level on/off flag in Slice data
  Low delay application support

## Slide 3: Comparison of BA vs. RA
Block adaptive (BA)/ region adaptive (RA) mode
  BA: 4x4 block based, direction and activity
  RA: divide picture into 16 regions
BA vs. RA
  Difference in coding performance especially in Class A
  Subjective quality difference
  Complexity difference
  Coding performance of BA with smaller number of filters in BA

## Slide 4: Coding performance difference
BA vs. RA mode with 16 filters
  RA with 64 filters: no gain
BA with 8 filters (encoder only): no loss
BA with 10 filters (normative): no loss
Replace BA with RA |  |  |  | 
 | AI10 | RA10 | LB10 | LP10
Class A | 0.5% | 0.9% | 0.7% | 1.0%
Class B | 0.2% | 0.4% | 0.1% | 0.4%
Class C | 0.1% | 0.1% | 0.0% | 0.2%
Class D | 0.1% | 0.0% | 0.1% | 0.1%
Class E | 0.2% |  | 0.1% | 0.1%
Average | 0.2% | 0.4% | 0.1% | 0.2%
Enc Time | 100% | 100% | 100% | 100%
Dec Time | 99% | 98% | 99% | 100%

## Slide 5: Complexity analysis
Additional complexity of BA
  block activity computation
  more filter storage (i.e., on chip cache) may be required due to faster filter switching (up to 16 filters)
Block activity computation
  For each 4x4 block,
    25 additions, 1 table look up
  1.56 additions/pixel
Filter storage requirements
  RA
    16 filters (picture level filter loading)
    8 filters (row by row filter loading is done)
    4 filters (LCU by LCU filter loading is done)
  BA
    8 filters (picture level filter loading )

## Slide 6: Visual test of BA vs. RA (Test 1)
Basic condition
  Spine Calendar, QP37, LP-Main
Comparison
  ALF ON Option2 BA
  ALF ON Option2 RA
Result
  ALF ON (BA and RA) is better visual quality than OFF.
  BA is better than RA because lines are preserved and ringing artifacts around lines are removed.

## Slide 7: Option 2 OFF

## Slide 8: Option 2 BA

## Slide 9: Option 2 RA

## Slide 10: Option 2 with RA

## Slide 11: Option 2 with BA

## Slide 12: Visual test of BA vs. RA (Test 2)
Basic condition
  A.PeopoleOnStreet, QP37, RA-HE10
Comparison
  ALF OFF
  ALF ON Option2 BA
  ALF ON Option2 RA
Result
  ALF ON (BA and RA) is better visual quality than OFF.
  BA is better than RA because block noises around objects are removed.
    In RA, block noises often remains as ALF OFF.

## Slide 13: ALF_OFF

## Slide 14: Option2 BA

## Slide 15: Option2 RA
Degradation point compared to BA

## Slide 16: Visual test of BA vs. RA (Test 3)
Basic condition
  Kimono, QP42, LP-HE10
Comparison
  ALF OFF
  ALF ON Option2 BA
  ALF ON Option2 RA
Result
  ALF ON (BA and RA) is better visual quality than OFF.
  BA is better than RA because block noises around objects are removed.
    In RA, block noises often remains as ALF OFF.

## Slide 17: ALF_OFF

## Slide 18: Option2 BA

## Slide 19: Option2 RA