## Slide 1: Inclusion of ALF in Main profile and additional test results
Tomohior Ikai
Yukinobu Yasugi
Tomoyuki Yamamoto
Takeshi Tsukuba
Tomoko Aono
SHARP Corporation
10th Meeting: Stockholm, SE, 11–20 July 2012

## Slide 2: Motivation
To provide good experience of streaming / download service in TV, recorder and cellular phone
Our users desire High quality video at streaming and Fast download
4K display and its service is almost there
High coding performance at HD / over-HD is quite necessary at codec level
One of the promising tools, ALF, is tested in a various range of HD sequences

## Slide 3: Test
Material
  Twenty HD video
    a wide variety test sequences (not necessarily typical video)
    not trained in the HEVC development
    not intentionally selected (our normally used material)
  Duration
    first 300 frames (5 sec) of each video
Encoder
    JCTVC-J0048 “AHG6: ALF with non-normative encoder-only improvements” (adopted in this meeting)
Condition
  QP 22, 27, 32, 37
  RA, LB, LP, RA10, LB10, LP10
The test materials are provided by ITE [The Institute of Image Information and Television Engineers ] and widely used in broadcasting and video products related companies in Japan
*original duration is 15 sec.

## Slide 4: Results
 |  | Random Access Main |  |  | Random Access HE10 |  | 
 |  | Y | U | V | Y | U | V
 | s201-s204 | -2.9% | -0.9% | -2.1% | -3.2% | -1.3% | -2.6%
 | s205-s208 | -2.7% | -0.8% | -3.2% | -3.0% | -1.2% | -3.8%
 | s209-s212 | -2.1% | -1.1% | -1.8% | -2.4% | -1.5% | -1.6%
 | s213-s216 | -2.5% | -1.9% | -1.9% | -2.8% | -2.7% | -2.2%
 | s217-s265 | -3.7% | -5.6% | -1.5% | -3.9% | -8.6% | -2.0%
 | Overall | -2.8% | -2.1% | -2.1% | -3.1% | -3.1% | -2.4%
 |  | -2.8% | -2.0% | -2.1% | -3.1% | -3.1% | -2.5%
 | Enc Time[%] | 100% |  |  | 101% |  | 
 | Dec Time[%] | 118% |  |  | 116% |  | 
 |  | Low delay B Main |  |  | Low delay B HE10 |  | 
 |  | Y | U | V | Y | U | V
 | s201-s204 | -2.9% | -0.8% | -2.1% | -3.6% | -2.3% | -3.9%
 | s205-s208 | -2.4% | -1.4% | -3.0% | -2.8% | -2.5% | -3.8%
 | s209-s212 | -2.0% | -1.1% | -1.7% | -2.3% | -5.5% | -1.8%
 | s213-s216 | -3.2% | -2.7% | -1.9% | -3.6% | -2.8% | -2.4%
 | s217-s265 | -3.7% | -2.8% | -1.7% | -4.1% | -6.8% | -2.8%
 | Overall | -2.8% | -1.8% | -2.1% | -3.3% | -4.0% | -2.9%
 |  | -2.8% | -1.8% | -2.3% | -3.3% | -4.0% | -2.9%
 | Enc Time[%] | 100% |  |  | 101% |  | 
 | Dec Time[%] | 113% |  |  | 116% |  | 
 |  | Low delay P Main |  |  | Low delay P HE10 |  | 
 |  | Y | U | V | Y | U | V
 | s201-s204 | -5.4% | -1.6% | -2.3% | -6.7% | -3.4% | -4.1%
 | s205-s208 | -6.1% | -3.2% | -3.5% | -7.6% | -4.3% | -4.8%
 | s209-s212 | -3.5% | -1.5% | -1.9% | -4.6% | -7.0% | -3.0%
 | s213-s216 | -4.4% | -4.3% | -2.2% | -5.1% | -5.2% | -3.4%
 | s217-s265 | -5.0% | -4.6% | -2.9% | -6.3% | -11.2% | -4.9%
 | Overall | -4.9% | -3.0% | -2.6% | -6.1% | -6.2% | -4.0%
 |  | -4.9% | -3.1% | -2.8% | -6.1% | -6.4% | -4.0%
 | Enc Time[%] | 102% |  |  | 101% |  | 
 | Dec Time[%] | 120% |  |  | 116% |  | 

## Slide 5: Results (cont.)
2.8 % at RA case (highest coding efficiency case)
4.9 % at LP case (relatively easy encoder case)
 | Random Access Main |  | 
 | Y | U | V
s201 | -2.5% | -1.2% | -2.9%
s202 | -2.0% | -0.6% | -1.5%
s203 | -4.6% | -0.7% | -2.6%
s204 | -2.4% | -1.0% | -1.3%
s205 | -2.9% | -1.0% | -2.0%
s206 | -4.7% | -0.3% | -6.1%
s207 | -1.2% | -1.6% | -1.4%
s208 | -1.9% | -0.4% | -3.1%
s209 | -2.0% | -2.3% | -2.6%
s210 | -2.4% | -0.5% | -1.6%
s211 | -2.4% | 0.1% | -2.4%
s212 | -1.8% | -1.6% | -0.8%
s213 | -2.4% | -3.3% | -1.6%
s214 | -3.3% | -3.4% | -2.9%
s215 | -1.9% | 0.1% | -2.8%
s216 | -2.3% | -1.2% | -0.3%
s217 | -2.2% | -0.7% | -0.3%
s218 | -2.0% | -3.0% | -1.9%
s264 | -2.3% | -1.6% | -0.9%
s265 | -8.6% | -17.0% | -2.8%
Overall | -2.8% | -2.1% | -2.1%
 | -2.8% | -2.0% | -2.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 118% |  | 
 | Low delay P Main |  | 
 | Y | U | V
s201 | -2.2% | -1.2% | -1.6%
s202 | -10.2% | -2.8% | -4.1%
s203 | -6.3% | -1.3% | -1.9%
s204 | -2.9% | -1.0% | -1.8%
s205 | -4.3% | -1.9% | -2.0%
s206 | -11.4% | -2.3% | -5.9%
s207 | -3.1% | -3.9% | -2.1%
s208 | -5.5% | -4.6% | -3.9%
s209 | -2.9% | 2.4% | -2.3%
s210 | -3.2% | -2.2% | -1.2%
s211 | -4.7% | -2.8% | -2.3%
s212 | -3.1% | -3.4% | -2.1%
s213 | -4.7% | -5.8% | -2.2%
s214 | -5.2% | -6.2% | -4.3%
s215 | -1.8% | -0.8% | 0.0%
s216 | -5.9% | -4.2% | -2.4%
s217 | -2.7% | -1.8% | -0.9%
s218 | -5.2% | -6.9% | -5.2%
s264 | -3.5% | -2.7% | -2.1%
s265 | -8.5% | -6.9% | -3.5%
Overall | -4.9% | -3.0% | -2.6%
 | -4.9% | -3.1% | -2.8%
Enc Time[%] | 102% |  | 
Dec Time[%] | 120% |  | 

## Slide 6: Benefit and complexity of ALF
Benefit
  Decrease download time and provide high quality streaming video
  Save communication channel
  Relatively easy encoder
Complex?
  Prevent HD service?
    With ALF, decoder can meet HD@60p. Complexity is not an issue for providing service
    TV, recorder and cellular phone can use hardware and PC is ok with software
  Increase power consumption?
    LP mode with ALF can decrease power consumption on encoder side
    ALF may increase power consumption, however Main Profile do not force encoder to use ALF, thus product can choose the usage of ALF if it is not desirable and power consumption issue will disappear with time
  Increase cost?
    Area size of operation is not an issue with the current chip process
    Minor increase of register / SRAM size
This is the “User Benefit”

## Slide 7: Conclution
Main profile should support effective coding gain tools for HD or over-HD sequences
Twenty HD sequences are tested
  Significant coding gain is observed
    2.8 % at RA
    4.9 % at LP
We request to include ALF in Main profile