## Slide 1: JCTVC-K0217 On Coding Tree Unit Syntax and Sequence parameter set RBSP syntax
Xue Fang and Limin Wang
Motorola Mobility

## Slide 2: Summary
Proposals consisting of two parts
Part 1
  Fix InverseRasterScan for Coding Tree Unit Syntax
Part 2
  Clean up related to PCM parameters in Sequence Parameter Set

## Slide 3: Part 1: Coding Tree Unit Syntax
( xCtb, yCtb ) top-left luma position for the coding tree unit
( xCtb, yCtb ) is calculated based on InverseRasterScan()
coding_tree_unit( xCtb, yCtb ) { | Descriptor
NumPCMBlock = 0 | 
xCtb = InverseRasterScan( CtbAddrRS, CtbSize, CtbSize, pic_width_in_luma_samples, 0 ) | 
yCtb = InverseRasterScan( CtbAddrRS, CtbSize, CtbSize, pic_width_in_luma_samples, 1 ) | 
CtbAddrInSlice = CtbAddrRS − slice_address | 
if( slice_sao_luma_flag ¦ ¦ slice_sao_chroma_flag ) | 
sao( xCtb >> Log2CtbSizeY, yCtb >> Log2CtbSizeY ) | 
coding_quadtree( xCtb, yCtb, Log2CtbSizeY, 0 ) | 
} | 

## Slide 4: Part 1: Coding Tree Unit Syntax
InverseRasterScan( a, b, c, d, e ) =
  InverseRasterScan( CtbAddrRS, CtbSize, CtbSize, pic_width_in_luma_samples, 0/1 )
  Incorrect ( xCtb, yCtb ) when pic_width_in_luma_samples is not dividable by CtbSize
  Example: 416x240 picture, CtbSize 64 => 7x4 CTU Array
  CtbAddrRS = 6
  (xCtb, yCtb) = (0,64)
  (6%(416/64))*64, 6/(416/64))*64)
 |  |  |  |  |  | 6
7 |  |  |  |  |  | 

## Slide 5: Part 1: Coding Tree Unit Syntax
Proposed Editorial Change:
coding_tree_unit( xCtb, yCtb ) { | Descriptor
NumPCMBlock = 0 | 
xCtb = (CtbAddrRS %PicWidthInCtbsY)<< Log2CtbSizeY | 
yCtb = (CtbAddrRS / PicHeightInCtbsY) << Log2CtbSizeY | 
CtbAddrInSlice = CtbAddrRS − slice_address | 
if( slice_sao_luma_flag ¦ ¦ slice_sao_chroma_flag ) | 
sao( xCtb >> Log2CtbSizeY, yCtb >> Log2CtbSizeY ) | 
coding_quadtree( xCtb, yCtb, Log2CtbSizeY, 0 ) | 
} | 
PicWidthInCtbsY = Ceil( pic_width_in_luma_samples ÷ CtbSizeY ) (7-20)
PicHeightInCtbsY = Ceil( pic_height_in_luma_samples ÷ CtbSizeY ) (7-22)

## Slide 6: Part 2: PCM parameters in Sequence Parameter Set
seq_parameter_set_rbsp( ) { | Descriptor
. . . . | 
bit_depth_chroma_minus8 | ue(v)
pcm_enabled_flag | u(1)
if( pcm_enabled_flag ) { | 
pcm_sample_bit_depth_luma_minus1 | u(4)
pcm_sample_bit_depth_chroma_minus1 | u(4)
} | 
. . . . | 
log2_diff_max_min_transform_block_size | ue(v)
if( pcm_enabled_flag ) { | 
log2_min_pcm_luma_coding_block_size_minus3 | ue(v)
log2_diff_max_min_pcm_luma_coding_block_size | ue(v)
} | 
. . . . | 
sample_adaptive_offset_enabled_flag | u(1)
if( pcm_enabled_flag ) | 
pcm_loop_filter_disable_flag | u(1)
. . . . | 

## Slide 7: Part 2: PCM parameters in Sequence Parameter Set
PCM Parameters spread in three locations
Each PCM group need check if pcm_enabled_flag is on
Other parameters have no dependency on PCM parameters

## Slide 8: Part 2: PCM parameters in Sequence Parameter Set Proposal 1
Suggest group all the PCM parameters together
seq_parameter_set_rbsp( ) { | Descriptor
….. | 
pcm_enabled_flag | u(1)
if( pcm_enabled_flag ) { | 
pcm_sample_bit_depth_luma_minus1 | u(4)
pcm_sample_bit_depth_chroma_minus1 | u(4)
log2_min_pcm_luma_coding_block_size_minus3 | ue(v)
log2_diff_max_min_pcm_luma_coding_block_size | ue(v)
pcm_loop_filter_disable_flag | u(1)
} | 
…….. | 

## Slide 9: Part 2: PCM parameters in Sequence Parameter Set
log2_min_pcm_coding_block_size_minus3 + 3 specifies the minimum size of I_PCM coding blocks.
The variable Log2MinIPCMCUSize is set equal to log2_min_pcm_coding_block_size_minus3 + 3. The variable Log2MinIPCMCUSize shall be in the range of Log2MinCbSize to Min( Log2CtbSizeY, 5 ), inclusive.
Ticket 777 points to the defect when Log2MinIPCMCUSize = 6 is desired
log2_min_pcm_luma_coding_block_size_minu3 issue
seq_parameter_set_rbsp( ) { | Descriptor
….. | 
log2_min_luma_coding_block_size_minus3 | ue(v)
..... | .
if( pcm_enabled_flag ) { | 
log2_min_pcm_luma_coding_block_size_minus3 | ue(v)
log2_diff_max_min_pcm_luma_coding_block_size | ue(v)
} | 
..... | 

## Slide 10: Part 2: PCM parameters in Sequence Parameter Set Proposal 2
Change log2_min_pcm_luma_coding_block_size_minus3 to log2_diff_min_pcm_luma_coding_block_size = Log2MinIPCMCUSize - Log2MinCbSize
Save coding bits
The Log2MinIPCMCUSize is naturally bounded by Log2MinCbSize without semantic : “The variable Log2MinIpcmCbSizeY shall be in the range of Log2MinCbSizeY to Min( Log2CtbSizeY, 5 ), inclusive”.
Log2MinCbSize | Log2MinIPCMCUSize | DiffLog2MinIPCMCUSize
3 (code 0) | 3(0) | 3(code 0)
4(code 1 ) | 4(1) | 4(code 0)
5(code 2) | 5(2) | 5(code 0)

## Slide 11: Part 2: PCM parameters in Sequence Parameter Set Proposal 2
log2_diff_min_pcm_luma_coding_block_size + log2_min_luma_coding_block_size_minus3 + 3 specifies the minimum size of I_PCM coding blocks when pcm_enabled_flag equals to 1.
seq_parameter_set_rbsp( ) { | Descriptor
...... | 
log2_min_luma_coding_block_size_minus3 | ue(v)
..... | ue(v)
if( pcm_enabled_flag ) { | 
log2_diff_min_pcm_luma_coding_block_size | ue(v)
log2_diff_max_min_pcm_luma_coding_block_size | ue(v)
} | 
max_transform_hierarchy_depth_inter | ue(v)
max_transform_hierarchy_depth_intra | ue(v)
..... | 

## Slide 12: Conclusion
  Proposed fix on InverseRasterScan for Coding Tree Unit Syntax
  Suggest group all the PCM parameters together
  Change log2_min_pcm_luma_coding_block_size_minus3 to log2_diff_min_pcm_luma_coding_block_size
  Thank You !