## Slide 1: REMOVING A LEVEL RESTRICTION ON CODING TREE BLOCK SIZE
JCTVC-M0173
Eran Pinhasov, Shevach Riabtsev & Assaf Menachem
13th JCT-VC Meeting – Apr 2013

## Slide 2: Background
Current standard disallows 16x16 CTBs for level 5 and above (Annex A, section A.4.1)
This restriction was proposed in JCTVC-J0334, reporting 16x16 CTBs add overheads for decoders
  Up to 10% increase in worst-case decode time
  Add ~1KB storage for 4K wide video (for top-line SAO params)
However, this restriction imposes substantial complication and cost for encoders targeting HEVC 4K
  Especially for legacy AVC\H.264 encoders upgrading to HEVC, using 16x16 architectures
Notes: Wade Wan, Tim Hellman
Assuming 10% is reached when a clip is coded using 32x32 CTBs (i.e. no split) comparing to all CTBs are 16x16.

## Slide 3: CTB Size Restriction Impact on Encoders
Breaks legacy 16x16 AVC\H.264 implementations
Increases cost of HW solutions
  Affects typical on-chip memories (sensitive to CTB size):
    Target & Reference image data
    Buffers between pipeline stages (coefficients, predictors, reconstructed and filtered data)
  Usage of 32x32/64x64 CTBs increases memory by at least ~25KB/100KB compared to 16x16 CTB (by analyzing a basic pipelined encoder architecture)
  Line-buffer & memory increase in proprietary components such as:
    Pre or post video processing (e.g. scaler, de-interlacer, image-enhancement etc.)
    Reference image cache or memories

## Slide 4: Summary & Proposal
CTB size restriction has significant impact on encoders
  Limits implementation flexibility
  Imposes complication and adds significant cost
  Breaks legacy AVC\H.264 16x16 based architecture
Recommending the removal of the CTB size limitation in Annex A, allowing 16x16 CTBs in all levels