## Slide 1: JCTVC-N0163 AHG14: Wide Color Gamut Test Material
P.Bordes
14th JCT-VC Meeting: Vienna, July 25- August 2nd, 2013

## Slide 2: AHG14: Wide Color Gamut Test Material
  Acquisition
    Sony F65 cinema camera, 14-stop
    Chose scene with Wide Color Gamut: Parakeets, saturated birthday clothes as well as flashy party items under RGB flashlights
    4K resolution, no gamma (linear-light domain), S-gamut, 50 or 59.94Hz
  Post-production
  Color grading
    DCI-P3 projector (Reference white D65, unlike digital cinema that is normally D50).
    Rec.709 HDTV Display
    Colorist took care of giving a natural looking style to graded content as well as creating out-of-gamut Rec.709 colors for the P3 graded contents
    Colors and lightness are intentionally equally balanced between Rec.709 and DCI-P3 content to keep a consistent general Director’s artistic intent, however some items of interest may be more colorful or saturated

## Slide 3: AHG14: Wide Color Gamut Test Material
  Content format adaptation for distribution codecs
    R’G’B’ to Y’CbCr matrix conversion:
      Rec.709: ITU-R Recommendation BT.709
      DCI-P3: SMPTE RP 177 2003 guidelines
    Down-sampling
      3840x2160 =>1920x1080 => 1280x720 (1.5x) and 960x540 (2x)
      Zero phase shift down-sampling filter (SHVC CfP sequences) with 10-bit capabilities (kindly provided and updated by InterDigital)
      8-bit content generated from 10-bit by adding an offset rounding then two right shifts

## Slide 4: Test Material - Rec.709

## Slide 5: Test Material – DCI P3