## Slide 1: JCTVC-N0168 AHG14 Color Gamut Scalable Video Coding using 3D LUT New Results
P.Bordes
14th JCT-VC Meeting: Vienna, July 25- August 2nd, 2013

## Slide 2: AHG14: Color Gamut Scalable
  M24484 – “Requirements for the scalable enhancement of HEVC” (S-2.10)
  The scalability extension shall support :
    BL and EL with different color spaces
    Combination of color space scalability and spatial scalability.
    Tristimulus values in EL that can not be represented in the BL color space.
  Proposal: use of “Color Difference Predictor” function (see also L0334,K0241)

## Slide 3: Color Difference Predictor
  The determination of the color transfer function is not straightforward because the content creation workflows may include deterministic processing but also non-deterministic operations (ex: Color grading).

## Slide 4: Color Difference Predictor: 3D Color LUT
  Advantages
  Many Color processing tools uses 3D LUTs to represent and save their intermediate and final color grading operations. In these cases, the 3D LUT information can be made available to the encoder easily
  The 3D LUT size (number of vertices in one direction), is a parameter read in the bit-stream. In that way, the encoder may choose the best trade-off between “Color Difference Predictor” module accuracy and encoding cost
  3D color LUT interpolation module for color conversion is implemented in many STBs and display devices (graphics card).
  If size=1 (one single octant with 8 vertices), and the color components of the vertices are set appropriately (see 6-Annex), then the 3D LUT is equivalent to the Gain-Offset model previously proposed in JCTVC-L0334.

## Slide 5: Test Material - Rec.709

## Slide 6: Test Material – DCI P3

## Slide 7: Color Gamut Scalability Tests (8 bits)
  Use Color graded test sequences (8 bits)

## Slide 8: Color Gamut Scalability Tests (10 bits)
  Use Color graded test sequences (10 bits)

## Slide 9: Conclusions
  A generic model scalable in complexity and in accuracy:
    Allows addressing low complexity use cases (linear models)
    Allows addressing more general use cases where the Color mapping function in between the BL and EL is more complex (non linear, clamping…)
  Propose to include CGS in SHM
  Propose JCT-VC to precise Color Gamut Scalability inter-layer prediction test conditions
    Define common CGS test content:
      AHG14 Color-Graded sequences BT.709 vs BT.2020 (Color graded in P3)
    Config parameters to be precised:
      BL 8-bits, EL 8-bits
      BL 8-bits, EL 10-bits
      …