## Slide 1: Overview of our professional requirements
JCTVC-P0044
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background
Professional (high end content creation) targets significantly higher bit rates and low compression ratios than consumer.
The top-level industry benchmarks systems are:
  For 4:2:2 10-bit HD 60P compression, an 880 Mbps intra-only system.
  Or for 4:4:4 10/12-bit HD 30P compression, an 880 Mbps intra-only system.
When designing at these bit rates, the processing is not in terms of bins or bits per cycle, but in terms of cycles per sample.
  Low latency is a necessity, and the shortest period over which case the worst case is managed the simpler the design.
In addition, professional cameras are already 4K 16-bit GBR HDR.
  16-bit cameras have been available for several years.
  A working standard is required to compress this at the professional operating points, and 2:1 compression should be the target.

## Slide 3: Changes in RExt to support Professional
Professional should not impact the codec for consumer applications
  There is, of course, always going to be “prosumer” applications that bridge the divide.
For that reason, we have been targeting the 16-bit profile to be the home for the tools
  In Korea and the following 3 meetings we presented aspects on:
    Internal bit depth/accuracies,
    CABAC compression efficiency
    CABAC throughput
    Profiles / levels (and now also tiers)
  To date, the committee have accepted the proposal on internal bit depth.
    It may be interesting to note that the compression efficiency being offered in N0189 for lossless surpassed that observed in P0162 where the lossless bitstream was split into two 8-bit streams.

## Slide 4: Internal bit depth
The system that has been accepted into the standard (which would only be applicable in the 16-bit profiles) is scalable.
This means that professional can use the 16-bit profile to code 16, 12 or 10-bits, and the encoder would scale automatically.
  This means that professional has no necessity to use or influence Main 10 444, Main 12 444, for example (although of course prosumer could)
  Note that when Main 12 444 was discussed, it was indicated that it was only applicable to positive QPs, and therefore consumer operating points, since for negative QPs, the system’s internal accuracy caused all but 8x8 blocks and 4x4 blocks to be applicable:
    Eg for 8x8,
      12(input bit depth)+3(bit depth increase by transform)+1(sign) = 16 = MAX_TR_DYNAMIC_RANGE
      This leaves no sub-fractional precision
      At the lowest QPs, where the quantiser expands the data by a small amount, 8x8 blocks also become redundant due to clipping in the entropy coder.

## Slide 5: CABAC compression efficiency
The importance of compression efficiency is obvious.
Shortcomings in the performance at lower QPs was identified in Korea and subsequent meetings.
  Proposals (from others) have now been accepted that improve the performance at the professional operating points and also for consumer lossless.

## Slide 6: CABAC throughput
As stated before, when designing at the high bit rates, the processing is not in terms of bins or bits per cycle, but in terms of samples per cycle.
  Low latency is a necessity, and the shortest period over which case the worst case is managed the better.
Consider the current worst case for 16-bit over a CTB.
  1.5 CABAC bins per sample
  5/3*baseband=5/3*16=26 EP bins per sample.
A value of 2 CABAC bins or 4 EP bins per 200MHz clock cycle (assume ~pixel rate) has been used in previous discussions.
Therefore, the worst case (considering coefficient data only) is:
  1 cycle for CABAC bins.
  7 cycles for EP bins.
  => 8 cycles per sample, or 24 cycles per 444 pixel.
    => 24 parallel decoders are required for HD.
    => 96 parallel decoders are required for 4K.

## Slide 7: CABAC throughput (cont)
Consider the current worst case for 16-bit over one sample.
  1.5 CABAC bins per sample (this can be averaged over the sub-group)
  46 EP bins per sample.
A value of 2 CABAC bins or 4 EP bins per 200MHz clock cycle (assume ~pixel rate) has been used in previous illustrations.
Therefore, the worst case (considering coefficient data only) is:
  1 cycle for CABAC bins.
  12 cycles for EP bins.
  => 13 cycles per sample, or 39 cycles per pixel.
    => 39 parallel decoders are required for HD.
    => 156 parallel decoders are required for 4K.

## Slide 8: CABAC throughput (cont.)
Alignment is a professional operating point enabler.
  RAW bins can be decoded without effort.
  The problem moves to become a manageable bandwidth issue between CPB and entropy decoder.
  It is possible to decode the worst case 46 RAW bins for a coefficient in 1 cycle.
    In fact, it is even possible to decode the worst case 92 RAW bins for two coefficients in 1 cycle.
  The worst case is therefore reduced.
    1 cycle for CABAC bins per sample
    0.5 cycles for RAW bins per sample
    i.e. 1.5 cycles per sample, or 4.5 cycles per pixel.
      => 5 parallel decoders for HD
      => 20 parallel decoders for 4K.

## Slide 9: Profiles
As indicated before, we do not want to influence consumer profiles.
Professional may not need to use screen content tools, but we believe we could support these tools without any big issues.
The current text reduces MinCR to professional operating levels (and below!)
  However, the definitions of MinCR are academic given the other parameters defined in Annex A.
  For that reason, a super tier is also being requested.
  It is hoped that the committee would mandate our proposed alignment scheme based upon the super-tier being used.
    Again, this would then mean the tool would not affect the lower-bit rate main and high-tier consumer designs.

## Slide 10: Conclusion
The requirements of professional have been described.
They have been shown to not impact consumer profiles.
The modifications that we have proposed have been small changes to the text, keeping the professional design within the general design philosophy of HEVC.