## Slide 1: Modified Deblocking Filtering Process for Intra Block Copy (IBC) (JCTVC-R0118)
Ismail M, Hyunho Jo, Jonghyun Ma, Woong Lim, and Donggyu Sim
Kwangwoon University (KWU)

## Slide 2: Summary
Motivation
  The current deblocking filter is designed inappropriately for IBC-coded block
    The deblocking filter of SCM-1.0 is conducted with strong filtering for IBC-coded blocks without consideration of the block vector.
    When two adjacent blocks are coded with IBC mode having same block vector without residual coefficient (means no discontinuity), no blocking artifact exist at the boundary.
The proposed method
  Modified deblocking filter for IBC as similar to inter-coded blocks
    When two adjacent blocks are coded with IBC, boundary strength (Bs) for deblocking filtering is modified to be set to 0 or 1 rather than 2
Experimental results
  0.17% BD-rate gain for Low Delay
  0.09% BD-rate gain for Random Access
  0.1% BD-rate loss for All Intra

## Slide 3: The current DBF process for IBC (1/2)
Deblocking filter is a tool that is introduced in the previous video standards such as H.264/AVC and HEVC
  It’s designed to reduce blocking artifacts caused by:
    block-based prediction (intra and inter blocks), and
    quantization
In the Screen Content Coding (SCC), intra block copying (IBC) is introduced as a new tool of a prediction mode
  It provides a significant bitrate savings for SCC
Current status: no body touches the deblocking filter with special attention to the IBC cases for SCC

## Slide 4: The current DBF process for IBC (2/2)
  Fig.1: Current DBF Process Flowchart
boundary
HEVC Version1
SCC
Bs=2
Bs=2
Bs=2
Bs=2
Bs=2
Bs=2
Bs=2
Bs=2
Bs=0 or 1

## Slide 5: Problem statements
Current SCM-1.0, deblocking filter for IBC is regarded as intra-coded block:
  It means that boundary strength (Bs) of IBC-coded block is set to 2 (strong filtering) regardless of the block vectors of IBC-coded blocks
  However, when two blocks are encoded with IBC and they have same block vector and no residual coefficients:
    There is no discontinuity between two blocks
    Strong filtering is not required to be applied for this case

## Slide 6: The proposed modified DBF process for IBC
Proposed method
  Deblocking filter is modified with paying attention to IBC-coded blocks as similar to inter-coded blocks
  Considering the block vectors of two blocks coded with IBC:
    Bs=0 (no filtering) for two IBC-coded blocks having same block vector without residual coefficient
    Bs=1 (weak filtering) when two IBC-coded blocks have different block vector or residual coefficient
  When (PIBC and QInter) or (PInter and QIBC) :
    Bs=1 (weak filtering) since reference indices are always different regardless of residual coefficient
  When (PIBC and QIntra) or (PIntra and QIBC) :
    Bs=2 (strong filtering) as similar with the current deblocking filtering process

## Slide 7: Decision of the modified DBF boundary strength
P | Q | Motion | Residual | Boundary strength | 
 |  |  |  | SCM-1.0 | Proposed
Intra | Intra | - | - | 2 | 2
Intra (Inter) | Inter (Intra) | - | - | 2 | 2
Inter | Inter | Equal | None | 0 | 0
Inter | Inter | Not equal | - | 1 | 1
Intra (IBC) | IBC (Intra) | - | - | 2 | 2
Inter (IBC) | IBC (Inter) | - | - | 2 | 1
IBC | IBC | Equal | None | 2 | 0
IBC | IBC | Not equal | - | 2 | 1
  Table 1. The comparisons of the BS decision
  The comparisons of the boundary strength (BS) decision between the conventional DBF and the proposed modified DBF for IBC

## Slide 8: Flowchart of the proposed modified DBF
  Fig.2: The proposed modified DBF for IBC process flowchart

## Slide 9: Experimental results (1/3)
BD-rate results of modified DBF for IBC under Low Delay

## Slide 10: Experimental results (2/3)
BD-rate results of modified DBF for IBC under Random Access

## Slide 11: Experimental results (3/3)
BD-rate results of modified DBF for IBC under All Intra

## Slide 12: Conclusion
The modified deblocking filter for intra block copy (IBC) is proposed with consideration of coded modes of two neighboring blocks
The proposed method achieves:
  x.x% BD-rate gain for Low Delay
  0.09% BD-rate gain for Random Access
  0.1% BD-rate lost for All Intra
  Under the common test condition of SCC
It is recommended to adopt the proposed method into SCC