## Slide 1
Xingyu Zhang, Robert Cohen
Mitsubishi Electric Research Laboratories
July 2014
JCTVC-R0200
SCCE3 Test D.2: Independent Uniform Prediction (IUP) Mode

## Slide 2: Independent Uniform Prediction (IUP)
Screen content material, especially computer desktop videos, have large areas dominated by a very few colors, e.g. foreground and background theme colors.
Independent Uniform Prediction
  Basic concept: Combination of uniform prediction with a small global palette
  All pixels in a block are predicted using the same color, per component (i.e. 3-component color vector/triplet)
  Encoder selects and signals colors in slice header
  These colors are available for any CU in the slice; no dependencies on neighboring CUs.

## Slide 3: CU decoding with IUP
CU header
Generate a uniform predictor block with pixel value
uniform_colors[cIdx][uniform_color_index]
No
Yes
Get the prediction
block using other
prediction modes
Decoded CU
decode uniform_color_index
uniform_color_index=1
No
Yes
Reconstructed
residue block
independent_uniform_pred_flag==1
num_uniform_colors>1
+
For this proposal, num_uniform_colors = 2

## Slide 4: Example IUP usage maps
Desktop
WebBrowsing
Uncompressed

## Slide 5: IUP usage map for Desktop from JCTVC-Q0036
Two color IUP: Blocks with white or mostly black backgrounds tended to be selected
Palette
IBC
IUP

## Slide 6: IUP usage map for WebBrowsing
Two-color IUP: Blocks with white backgrounds tended to be selected
Palette
IBC
IUP

## Slide 7: Lossy compression performance (AI), without palette
Anchor: 2-CTU IBC, without palette | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -1.6% | -1.7% | -1.6%
RGB, text & graphics with motion,720p | -1.5% | -1.6% | -1.5%
RGB, mixed content, 1440p | -1.0% | -0.9% | -0.9%
RGB, mixed content, 1080p | -0.7% | -0.7% | -0.7%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -1.5% | -1.5% | -1.5%
YUV, text & graphics with motion,720p | -1.5% | -1.8% | -2.1%
YUV, mixed content, 1440p | -0.7% | -0.9% | -0.9%
YUV, mixed content, 1080p | -0.8% | -1.0% | -0.9%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 96% |  | 
Anchor: Full IBC, without palette | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -1.4% | -1.5% | -1.4%
RGB, text & graphics with motion,720p | -1.3% | -1.6% | -1.5%
RGB, mixed content, 1440p | -0.9% | -0.8% | -0.8%
RGB, mixed content, 1080p | -0.6% | -0.6% | -0.6%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -1.4% | -1.4% | -1.4%
YUV, text & graphics with motion,720p | -1.5% | -1.9% | -2.2%
YUV, mixed content, 1440p | -0.6% | -0.9% | -0.9%
YUV, mixed content, 1080p | -0.6% | -0.8% | -0.7%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% |  | 
Dec Time[%] | 96% |  | 
Anchor: 2-CTU IBC, without palette
Anchor: Full IBC, without palette

## Slide 8: Lossy compression performance (AI), with palette
Anchor: 2-CTU IBC, with palette | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.6% | -0.5% | -0.6%
RGB, text & graphics with motion,720p | -0.9% | -0.9% | -0.9%
RGB, mixed content, 1440p | -0.7% | -0.7% | -0.7%
RGB, mixed content, 1080p | -0.5% | -0.5% | -0.5%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.5% | -0.5% | -0.5%
YUV, text & graphics with motion,720p | -0.9% | -1.2% | -1.2%
YUV, mixed content, 1440p | -0.6% | -0.6% | -0.5%
YUV, mixed content, 1080p | -0.4% | -0.5% | -0.4%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 97% |  | 
Anchor: Full IBC, with palette | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.6% | -0.6% | -0.6%
RGB, text & graphics with motion,720p | -1.0% | -1.1% | -1.1%
RGB, mixed content, 1440p | -0.6% | -0.6% | -0.6%
RGB, mixed content, 1080p | -0.4% | -0.4% | -0.4%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.5% | -0.5% | -0.5%
YUV, text & graphics with motion,720p | -0.9% | -1.5% | -1.4%
YUV, mixed content, 1440p | -0.5% | -0.6% | -0.6%
YUV, mixed content, 1080p | -0.4% | -0.4% | -0.4%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 98% |  | 
Dec Time[%] | 97% |  | 
Anchor: 2-CTU IBC, with palette
Anchor: Full IBC, with palette

## Slide 9: Lossy compression performance (RA)
Anchor: 2-CTU IBC, without palette | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.6% | -0.6% | -0.5%
RGB, text & graphics with motion,720p | -0.8% | -0.9% | -0.9%
RGB, mixed content, 1440p | -0.5% | -0.4% | -0.5%
RGB, mixed content, 1080p | -0.2% | -0.3% | -0.3%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.6% | -0.7% | -0.7%
YUV, text & graphics with motion,720p | -0.9% | -1.4% | -1.4%
YUV, mixed content, 1440p | -0.4% | -0.6% | -0.5%
YUV, mixed content, 1080p | -0.5% | -0.6% | -0.6%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Anchor: Full IBC, without palette | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.5% | -0.5% | -0.5%
RGB, text & graphics with motion,720p | -0.7% | -0.8% | -0.9%
RGB, mixed content, 1440p | -0.4% | -0.3% | -0.3%
RGB, mixed content, 1080p | -0.3% | -0.3% | -0.4%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.6% | -0.7% | -0.6%
YUV, text & graphics with motion,720p | -0.8% | -1.2% | -1.2%
YUV, mixed content, 1440p | -0.2% | -0.6% | -0.6%
YUV, mixed content, 1080p | -0.3% | -0.8% | -0.6%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Anchor: 2-CTU IBC, with palette | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.1%
RGB, text & graphics with motion,720p | -0.3% | -0.4% | -0.4%
RGB, mixed content, 1440p | -0.2% | -0.2% | -0.2%
RGB, mixed content, 1080p | -0.2% | -0.2% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.1%
YUV, text & graphics with motion,720p | -0.5% | -0.7% | -0.8%
YUV, mixed content, 1440p | -0.2% | -0.3% | -0.3%
YUV, mixed content, 1080p | 0.0% | -0.3% | -0.2%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
Anchor: Full IBC, with palette | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.1%
RGB, text & graphics with motion,720p | -0.4% | -0.5% | -0.4%
RGB, mixed content, 1440p | -0.2% | -0.2% | -0.2%
RGB, mixed content, 1080p | -0.2% | -0.1% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.1%
YUV, text & graphics with motion,720p | -0.4% | -0.8% | -0.8%
YUV, mixed content, 1440p | -0.2% | -0.1% | -0.3%
YUV, mixed content, 1080p | 0.0% | -0.1% | -0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 98% |  | 
Dec Time[%] | 100% |  | 

## Slide 10: Lossy compression performance (LB)
Anchor: 2-CTU IBC, without palette | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.2% | -0.1% | 0.0%
RGB, text & graphics with motion,720p | -0.2% | -0.2% | -0.2%
RGB, mixed content, 1440p | -0.5% | -0.4% | -0.2%
RGB, mixed content, 1080p | 0.1% | -0.2% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.1% | -0.2% | 0.0%
YUV, text & graphics with motion,720p | -0.1% | -0.4% | -0.5%
YUV, mixed content, 1440p | -0.4% | -0.3% | -0.3%
YUV, mixed content, 1080p | 0.0% | 0.5% | 0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 101% |  | 
Anchor: Full IBC, without palette | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.1% | 0.0% | 0.0%
RGB, text & graphics with motion,720p | -0.1% | -0.3% | -0.2%
RGB, mixed content, 1440p | -0.4% | -0.5% | -0.3%
RGB, mixed content, 1080p | -0.3% | 0.0% | -0.6%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.2% | -0.2% | -0.1%
YUV, text & graphics with motion,720p | -0.1% | -0.1% | -0.2%
YUV, mixed content, 1440p | -0.2% | -0.5% | -0.4%
YUV, mixed content, 1080p | 0.2% | -0.7% | 0.4%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 101% |  | 
Anchor: 2-CTU IBC, with palette | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | 0.1% | 0.2% | 0.1%
RGB, text & graphics with motion,720p | 0.1% | 0.2% | 0.2%
RGB, mixed content, 1440p | -0.2% | 0.0% | -0.1%
RGB, mixed content, 1080p | 0.0% | -0.2% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.0% | 0.1% | 0.1%
YUV, text & graphics with motion,720p | 0.3% | -0.2% | 0.1%
YUV, mixed content, 1440p | -0.1% | 0.1% | -0.1%
YUV, mixed content, 1080p | 0.0% | -0.4% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 98% |  | 
Dec Time[%] | 100% |  | 
Anchor: Full IBC, with palette | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | 0.0% | 0.1% | 0.1%
RGB, text & graphics with motion,720p | 0.3% | 0.1% | 0.2%
RGB, mixed content, 1440p | -0.3% | -0.1% | -0.2%
RGB, mixed content, 1080p | -0.1% | 0.1% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.1% | 0.1% | 0.1%
YUV, text & graphics with motion,720p | 0.1% | 0.2% | -0.3%
YUV, mixed content, 1440p | -0.2% | -0.4% | -0.2%
YUV, mixed content, 1080p | 0.0% | -1.7% | -0.4%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 98% |  | 
Dec Time[%] | 100% |  | 

## Slide 11: Summary
Independent uniform prediction uses one or two uniform colors as a prediction for a block
Method for selecting color is non-normative – can be provided by encoder, or even provided by computer that is generating the graphics
All-intra BD-Rate improvement for RGB text & graphics with motion
  Without palette in anchor and tested configurations:
    SCM 2-CTU: 1.6% G, 1.5% Y for 1080p; 1.5% G, 1.5% Y for 720p
    SCM Full: 1.4% G, 1.4% Y for 1080p; 1.3% G, 1.5% Y for 720p
  With palette in anchor and tested configurations:
    SCCE3 2-CTU: 0.6% G, 0.5% Y for 1080p; 0.9% G, 0.9% Y for 720p
    SCCE3 Full: 0.6% G, 0.5% Y for 1080p; 1.0% G, 0.9% Y for 720p
IUP can be added to SCM with or without palette