## Slide 1: JCTVC-AB0023
Roll equations in omnidirectional projection indicator SEI message
(current draft: JCTVC-AA1005)

## Slide 2: Current state of roll equations:
JCTVC-AA1005 currently defines roll as a rotation about a vector projecting from the center of the sphere through the center of the coded cropped picture after yaw and pitch rotation have been defined.
[These equations do not reflect intent of the roll operation]
JVET defines rotations about X,Y,Z axis
ϕ = Cos( ω′ ) * α − Sin( ω′ ) * β
θ = Sin( ω′ ) * α + Cos( ω′ ) * β

## Slide 3: Counter-clockwise 2D rotation
x’ = x * cos(ω) - y * sin(ω)
y’ = x * sin(ω) + y * cos(ω)

## Slide 4
clockwise ( ω’ = ­­-ω ):
counter-clockwise:

## Slide 5
generalized rotation in 3D XYZ Cartesian space, where a clockwise rotation is performed of two axis (a,b) around a third axis ( c ) normal to the (a,b) plane

## Slide 7
Forward (pre-processing on encoder):
Inverse (post-processing “render” after decoder):
(Step 1)
(Step 2)
(Step 3)

## Slide 8
X = cos(θ) cos(ϕ)
Y = sin(θ)
Z = −cos(θ) sin(ϕ)
Convert spherical surface coordinates to Cartesian XYZ
ϕ = tan2−1(−Z,X)
θ = sin−1(Y/(X2+Y2+Z2)1/2)
Inverse:

## Slide 10: https://jvet.hhi.fraunhofer.de/svn/svn_360Lib/tags/360Lib-3.0rc1 /source/Lib/TLib360/TGeometry.cpp
Void TGeometry::invRotate3D(SPos& sPos, Int iRoll, Int iPitch, Int iYaw){
POSType x = sPos.x; POSType y = sPos.y; POSType z = sPos.z;
if(iYaw){
POSType rcos = scos((POSType)(iYaw*S_PI/(180.0*SVIDEO_ROT_PRECISION)));
POSType rsin = ssin((POSType)(iYaw*S_PI/(180.0*SVIDEO_ROT_PRECISION)));
POSType t1 = rcos*x + rsin*z;
POSType t2 = -rsin*x + rcos*z;
x = t1; z = t2;
}
if(iPitch){
POSType rcos = scos((POSType)(-iPitch*S_PI/(180.0*SVIDEO_ROT_PRECISION)));
POSType rsin = ssin((POSType)(-iPitch*S_PI/(180.0*SVIDEO_ROT_PRECISION)));
POSType t1 = rcos*x - rsin*y;
POSType t2 = rsin*x + rcos*y;
x = t1; y = t2;
}
if(iRoll){
POSType rcos = scos((POSType)(iRoll*S_PI/(180.0*SVIDEO_ROT_PRECISION)));
POSType rsin = ssin((POSType)(iRoll*S_PI/(180.0*SVIDEO_ROT_PRECISION)));
POSType t1 = rcos*y - rsin*z;
POSType t2 = rsin*y + rcos*z;
y = t1; z = t2;
}
sPos.x = x; sPos.y = y; sPos.z = z;
}
JVET-F0065 /
JCTVC-AA0033

## Slide 11: https://jvet.hhi.fraunhofer.de/svn/svn_360Lib/tags/360Lib-3.0rc1/source/Lib/TLib360/TGeometry.cpp
S_EPS = 1.0e-6
#define satan2(y, x) atan2((Double)(y), (Double)(x))
yaw = (-atan2(z, x)) * 180.0/ pi;
len = sqrt(x*x + y*y + z*z);
pitch = 90.0 -((len < S_EPS? 0.5 : acos(y/len)/pi)*180.0);

## Slide 12: Euler’s rotation: math reflecting intent of JCTVC-AA1005 roll…
u
Perform yaw, pitch rotations, then….

## Slide 13: Where to find more information on rotation…
https://en.wikipedia.org/wiki/Rotation_matrix