## Slide 1
NALU verification SEI
JCTVC-AJ0024

## Slide 2: Problem
Bitstream corruption and error-resilience/concealment:
  Transport or application level (FEC…)
  Codec: built-in tools
BUT…
Detected errors not pulled up to higher layers
  E.g. visible artefacts in DTV rendering (OTT…)
Corrupted bitstream may not be detected
  Undetected errors may apply to the global picture (SEI)
  E.g. corrupted value is in the syntax element range
Lots of places for undetected corruption of SEI…
  SMPTE ST 2108 (SDI)  HEVC  HDMI 2.1 (CTA-861.4)

## Slide 3
Proposition: verification SEI – coded data hash
Syntax | Descriptor
coded_data_hash( payloadSize ) { | 
cdh_type | u(8)
cdh_nalu_type | u(8)
if( cdh_type == 0 ) | 
for(i = 0 ; i < 16 ; i++ ) | 
cdh_md5[ i ] | b(8)
if( cdh_type == 1 ) | 
cdh_crc | u(16)
} | 
cdh_nalu_type | NALU type
0 | All NALU in the AU (precluding verification SEI message)
1 | All VCL NALU of the current AU
2 | All non-VCL NALU of the current AU
3 | Following SEI message