## Slide 1: Performance analysis of affine inter prediction in JEM 1.0
Author / Email:
Hong Zhang / summer.zhanghong@huawei.com
Huanbang Chen / chenhuanbang@Huawei.com
Xiang Ma / Maxiang6@Huawei.com
Haitao Yang / Haitao.yang@Huawei.com

## Slide 2: Evaluation of affine inter prediction in JEM 1.0
Class | RA10 | LDB10 | LDP10
Class A | 0.13% | -- | --
Class B | 0.66% | 1.10% | 1.26%
Class C | 0.31% | 0.88% | 0.80%
Class D | 0.56% | 1.99% | 1.66%
Class E | -- | 1.69% | 1.82%
Class F | 0.81% | 1.11% | 1.34%
Over all | 0.50% | 1.32% | 1.35%
Enc(%) | 97% | 93% | 94%
Dec(%) | 103% | 104% | 102%
Table 1 Affine tool off vs. JEM 1.0
Class | RA10 | LDB10 | LDP10
Class A | -0.44% | -- | --
Class B | -1.39% | -1.50% | -1.69%
Class C | -0.67% | -1.00% | -1.31%
Class D | -1.08% | -2.06% | -2.48%
Class E | -- | -1.81% | -2.05%
Class F | -1.38% | -1.66% | -1.63%
Over all | -1.01% | -1.59% | -1.81%
Enc(%) | 115% | 119% | 115%
Dec(%) | 95% | 100% | 105%
Table 2 Affine tool on vs. HM 16.6
Affine inter prediction integrated to JEM 1.0
RD performance almost the same as those in VCEG document COM16–C1016
  Tool off test shows 0.50%, 1.32% and 1.35% loss
  Tool on test shows 1.01%, 1.59% and 1.81% gain

## Slide 3: Response to the comments
Does affine prefer easier content?
The influence of high precision motion vector
The influence of high bit depth interpolation filter

## Slide 4: Coding performance under different conditions
Source | Sequence | Description | Frame
Netflix Chimera | Aerial | zoom, rotation | 0-599
 | DrivingPOV | zoom | 0-599
 | RollerCoaster | rotation | 300-899
Netflix E1 Fuente | VegetableMarket | Camera shakiness with zoom, rotation | 0-299
 | Tango | rotation | 0-293
 | Tunnel | zoom | 0-599
 | BoxingPractice | Camera shakiness with rotation | 0-253
Transformer 1080P | Transformer34 | rotation, zoom | 0-169
 | Transformer35 | zoom | 0-107
HEVC CTC | Cactus | rotation | 0-499
Affine vs. HM |  |  | 
Sequence | RA10 | LDB10 | LDP10
Cactus | -5.7% | -6.6% | -6.2%
Tunnel | -6.1% | -4.6% | -6.2%
BoxingPractice | -0.5% | -0.7% | -0.9%
Tango | -0.5% | -0.6% | -0.6%
VegetableMarket | -2.5% | -1.3% | -1.8%
Aerial | -3.8% | -6.2% | -3.9%
DrivingPOV | -3.0% | -2.6% | -2.5%
RollerCoaster | -2.7% | -3.2% | -2.7%
Transformer34 | -3.0% | -2.2% | -2.3%
Transformer35 | -3.6% | -2.2% | -2.5%

## Slide 5
Sequence | Tunnel | Aerial
POC | 0-390 | 0-170
BD Rate | -7.26% | -0.11%
Bit rate of HM | 4.8-42.4 | 2.2-38.6
POC | 391-600 | 171-320
BD Rate | -0.82 | -14.44%
Bit rate of HM | 1.5-11.6 | 3.3-47.1
Bit Rate of HM: range of bit rate with QP 22,27,32,37, measured by Mbps

## Slide 6: Motion vector accuracy test
Position | Luma Filter coefficients
1/8 | { -1, 2, -5, 62, 8, -3, 1, 0 }
2/8 | { -1, 4, -10, 58, 17, -5, 1, 0 }
3/8 | { -1, 3, -9, 47, 31, -10, 4, -1 }
4/8 | { -1, 4, -11, 40, 40, -11, 4, -1 }
5/8 | { -1, 4, -10, 31, 47, -9, 3, -1 }
6/8 | { 0, 1, -5, 17, 58, -10, 4, -1 }
7/8 | { 0, 1, -3, 8, 62, -5, 2, -1 }
Position | Chroma Filter coefficients | Position | Filter coefficients
1/16 | { -2, 62, 4, 0 } | 9/16 | { -4, 30, 42, -4 }
2/16 | { -2, 58, 10, -2 } | 10/16 | { -4, 28, 46, -6 }
3/16 | { -4, 56, 14, -2 } | 11/16 | { -2, 20, 52, -6 }
4/16 | { -4, 54, 16, -2 } | 12/16 | { -2, 16, 54, -4 }
5/16 | { -6, 52, 20, -2 } | 13/16 | { -2, 14, 56, -4 }
6/16 | { -6, 46, 28, -4 } | 14/16 | { -2, 10, 58, -2 }
7/16 | { -4, 42, 30, -4 } | 15/16 | { 0, 4, 62, -2 }
8/16 | { -4, 36, 36, -4 } |  | 
Motion vector precision up to 1/8
Use the same filter as FRUC
1/8 precision mv has little influence to coding gains
Sequence | RA10 |  | LDB10 |  | LDP10 | 
 | Affine | 1/8 mv | Affine | 1/8 mv | Affine | 1/8 mv
Tractor | -22.94% | 2.61% | -33.08% | 1.36% | -29.55% | 0.85%
Station | -23.56% | 1.99% | -39.57% | 1.34% | -37.16% | 1.76%
Shields | -12.65% | 1.42% | -18.50% | 1.10% | -18.10% | -0.76%
BlueSky | -6.80% | 0.63% | -9.98% | 0.79% | -10.23% | -2.27%
SpinCalendar | -14.95% | -0.39% | -33.27% | -0.71% | -27.27% | -7.36%
Jets | -6.46% | -0.13% | -24.19% | -0.36% | -21.04% | -2.99%

## Slide 7: Motion compensation filter bit depth test
Position | 8-tap Filter coefficients
1/4 | { -3, 13, -38, 228, 74, -24, 9,-3 }
2/4 | { -3, 13, -40, 158, 158, -40, 13, -3 }
3/4 | { -3, 9, -24, 74, 228, -38,13,-3 }
Position | 8-tap Filter coefficients
1/8 | { -12, 240, 36, -8 }
2/8 | { -20, 216, 74, -14 }
3/8 | { -20, 182, 112, -18 }
4/8 | { -20, 148, 148, -20 }
5/8 | { -18, 112, 182, -20 }
6/8 | { -14, 74, 216, -20 }
7/8 | { -8, 36, 240, -12 }
Sequence | RA10 |  | LDB10 |  | LDP10 | 
 | Affine | 8 bit | Affine | 8 bit | Affine | 8 bit
Tractor | -22.94% | -0.36% | -33.08% | -0.62% | -29.55% | -0.11%
Station | -23.56% | -0.42% | -39.57% | -0.85% | -37.16% | 0.55%
Shields | -12.65% | -0.56% | -18.50% | -0.44% | -18.10% | 0.18%
BlueSky | -6.80% | -0.50% | -9.98% | -0.19% | -10.23% | -0.39%
SpinCalendar | -14.95% | -0.09% | -33.27% | -0.08% | -27.27% | -0.56%
Jets | -6.46% | -0.24% | -24.19% | -0.42% | -21.04% | -0.11%
Use the same 8 bit filter as Affine
little influence to coding gains

## Slide 8: Conclusion
After being integrated in JEM1.0, the RD performance of affine prediction is kept
Affine transform prediction tool work well especially for video clip with complex motion which cause bitrate increase of an encoder
Most of the coding gain is from the simplified affine transformation model, simply enhancing precision of either mv or interpolation filter can barely get coding gain