## Slide 1: Further improvement of intra coding tools
Seung-Hwan Kim and Andrew Segall

## Slide 2
Overview
In JEM 1.0 NSST is enabled only if PDPC mode is disabled
  Proposal: Allow NSST and PDPC to be enabled simultaneously
In JEM 1.0 NSST index is binarized in two ways
  Proposal: Single unified binarization
In JEM 1.0 Non-MPM coding is coded fixed length coded
  Proposal: Non-MPM mode is divided into two sets and coded

## Slide 3
  Allowing NSST and PDPC to be enabled at same time
  In JEM 1.0, NSST is enabled only when PDPC index is equal to ‘0’
  In this proposal, NSST index coded independently from PDPC flag
Recover PDPC index
Recover NSST index
PDPC index ==0
YES
JEM 1.0
Proposed
…
No
Recover PDPC index
Recover NSST index
…
Condition to recover NSST index is modified
REASON: Probabilistically NSST is independent of PDPC

## Slide 4
Analysis : Distribution of PDPC index
 | PDPC_idx ==0 | PDPC_idx ==1
Racehorse | 0.643 | 0.357
Blowingbubble | 0.673 | 0.327
BQSquare | 0.764 | 0.236
BasketballDrill | 0.794 | 0.206
RacehorseC | 0.622 | 0.378
BQTerrace | 0.690 | 0.310
ParkScene | 0.405 | 0.595
Traffic | 0.518 | 0.482
PeopleOnStreet | 0.557 | 0.443
NebutaFestival | 0.312 | 0.688
AVG | 0.598 | 0.402

## Slide 5
Analysis : Distribution of NSST index
 | Nsst_idx ==0 | Nsst_idx ==1 | Nsst_idx ==2 | Nsst_idx ==3
Racehorse | 0.279 | 0.286 | 0.220 | 0.215
Blowingbubble | 0.304 | 0.268 | 0.244 | 0.184
BQSquare | 0.287 | 0.279 | 0.232 | 0.202
BasketballDrill | 0.216 | 0.292 | 0.271 | 0.221
RacehorseC | 0.309 | 0.256 | 0.221 | 0.215
BQTerrace | 0.403 | 0.214 | 0.203 | 0.181
ParkScene | 0.407 | 0.202 | 0.199 | 0.192
Traffic | 0.461 | 0.184 | 0.187 | 0.168
PeopleOnStreet | 0.418 | 0.215 | 0.191 | 0.177
NebutaFestival | 0.410 | 0.195 | 0.214 | 0.181
AVG | 0.349 | 0.239 | 0.218 | 0.193
Distribution of NSST index when PDPC_idx is equal to ‘0’

## Slide 6
 | Nsst_idx ==0 | Nsst_idx ==1 | Nsst_idx ==2 | Nsst_idx ==3
Racehorse | 0.319 | 0.261 | 0.216 | 0.205
Blowingbubble | 0.322 | 0.253 | 0.238 | 0.187
BQSquare | 0.349 | 0.245 | 0.213 | 0.192
BasketballDrill | 0.252 | 0.283 | 0.256 | 0.209
RacehorseC | 0.331 | 0.239 | 0.220 | 0.210
BQTerrace | 0.437 | 0.202 | 0.195 | 0.167
ParkScene | 0.434 | 0.197 | 0.188 | 0.180
Traffic | 0.482 | 0.176 | 0.184 | 0.158
PeopleOnStreet | 0.435 | 0.207 | 0.189 | 0.169
NebutaFestival | 0.382 | 0.199 | 0.227 | 0.192
AVG | 0.374 | 0.226 | 0.213 | 0.187
Analysis : Distribution of NSST index
Distribution of NSST index when PDPC_idx is equal to ‘1’

## Slide 7
Analysis : Distribution of NSST index
 | Nsst_idx ==0 | Nsst_idx ==1 | Nsst_idx ==2 | Nsst_idx ==3
Racehorse | 0.532 | 0.217 | 0.124 | 0.127
Blowingbubble | 0.565 | 0.201 | 0.133 | 0.101
BQSquare | 0.701 | 0.140 | 0.086 | 0.073
BasketballDrill | 0.679 | 0.168 | 0.083 | 0.070
RacehorseC | 0.512 | 0.201 | 0.151 | 0.135
BQTerrace | 0.634 | 0.138 | 0.125 | 0.103
ParkScene | 0.444 | 0.179 | 0.193 | 0.183
Traffic | 0.534 | 0.136 | 0.172 | 0.159
PeopleOnStreet | 0.574 | 0.146 | 0.147 | 0.134
NebutaFestival | 0.420 | 0.187 | 0.214 | 0.178
AVG | 0.560 | 0.171 | 0.143 | 0.126
Distribution of NSST index when
((IP == DC || IP == Planar) && Partition Size ==2Nx2N))

## Slide 8
Proposed: Single unified binarization
JEM1.0 | Proposed
If(Intra_pred_mode <= DC && partition size == 2Nx2N) { Code NSST index : // Truncated unary (1, 01, 00) // Available index range from 0 to 2 } else { Code NSST index : // fixed length (00, 01, 10, 11) } | Code NSST index; // truncated unary (1, 01, 001, 000)
REASON: - Conceptually more straight forward
- NSST index is derived in the same way all of the time
- Context reduction (7 5)
- Coding performance improvement

## Slide 9
Non-MPM Mode Coding
Current:
  If intra prediction mode is non-MPM mode, 61 mode index are arranged as follows:
  {0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15, 16, 17, 18, 19, 20, … 60}
  Signal index
Proposed:
  If intra prediction mode is non-MPM mode, sub-divide non-MPM modes into two sets
    Set X = { 0, 4, 8, 12, 16, 20, …60}
    Set Y = { 1, 2, 3, 5, 6, 7 , 9, 10, … 59}
    Signal Set, index within set

## Slide 10
Proposed non-MPM mode coding
JEM1.0 | Proposed
code Intra_pred_idx_flag If(Intra_pred_idx_flag == MPM mode) code MPM mode else code non-MPM mode | code Intra_pred_idx_flag If(Intra_pred_idx_flag == MPM mode) code MPM mode Else { code intra_selected_mode_idx_flag if (intra_selected_idx_flag) code selected mode else code non-selected mode }

## Slide 11
Results-AI
 | All Intra Main 10 |  | 
 | Y | U | V
Class A | -0.42% | -0.69% | -0.95%
Class B | -0.36% | -0.50% | -0.76%
Class C | -0.33% | -0.15% | -0.29%
Class D | -0.34% | -0.19% | -0.44%
Class E | -0.25% | 0.49% | -0.35%
Overall | -0.35% | -0.26% | -0.58%
Class F (option) | -0.29% | -0.11% | -0.43%
  Allowing PDPC and NSST together increased encoder run time about 60% ,
  And no changes in decoder run time. (AI)

## Slide 12
Results-RA
 | Random Access Main 10 |  | 
 | Y | U | V
Class A | -0.21% | -1.06% | -1.41%
Class B | -0.14% | -0.66% | -0.88%
Class C | -0.22% | -0.47% | -0.78%
Class D | -0.19% | -0.33% | -0.33%
Overall | -0.19% | -0.63% | -0.85%
Class F (option) | -0.12% | -0.30% | -0.35%

## Slide 13
Conclusions
NSST coding performance in JEM can be further improved by allowing NSST to be enabled independently from PDPC index
NSST binarization needs to be simplified so that it is coded with
  One binarization
  The number of NSST index defined is always the same
Current non-MPM intra coding mode can be further improved by allowing more mode sets
Recommendation is to adopt the above technologies in JEM.

## Slide 14
Backup slide 1
Class A | -0.46% | -0.66% | -1.15%
Class B | -0.35% | -0.71% | -0.85%
Class C | -0.36% | -0.34% | -0.52%
Class D | -0.41% | 0.01% | -0.52%
Class E | -0.24% | 0.59% | -0.30%
Class F | -1.11% | -0.58% | -0.27%
All w/o F | -0.37% | -0.29% | -0.70%
Class A | -0.38% | -0.19% | -0.49%
Class B | -0.31% | -0.39% | -0.66%
Class C | -0.31% | -0.39% | -0.40%
Class D | -0.34% | -0.36% | -0.51%
Class E | -0.26% | 0.40% | -0.39%
Class F | -0.85% | -0.03% | -0.02%
All w/o F | -0.32% | -0.23% | -0.50%
Class A | -0.03% | -0.12% | -0.18%
Class B | -0.02% | -0.09% | -0.12%
Class C | -0.05% | 0.04% | -0.11%
Class D | -0.09% | -0.23% | -0.18%
Class E | 0.01% | -0.94% | -1.09%
Class F | -0.97% | -0.13% | -0.05%
All w/o F | -0.04% | -0.22% | -0.29%
NSST enabling and index coding
Improvement on non-MPM mode coding
Combined Method
All Intra 30 frames tested

## Slide 15
Backup slide 2
  Non-Separable Secondary Transform (NSST)
  Independently applied for each 4×4 transform coefficient block in Intra CU
  There are 12 transform sets defined
    Each transform set includes 3 transform matrices
    NSST index is transmitted to indicate the corresponding transform matrix.
  The mapping from the intra prediction mode to the transform set is defined
Mapping from intra prediction mode to transform set index