## Slide 1: Simplification and improvements for BIO design in JEM2
E.Alshina, A.Alshin
Samsung Electronics

## Slide 2: 3 changes are proposed for BIO
Longer MV regiment in RA
=Clip3(-thBIO,thBIO, ); =Clip3(-thBIO,thBIO, ).
  Motivation: GOPsize 816
  Proposal: thBIO (thBIO<<1)
BIO application in LD cases
  Issue: Condition check per PU
    calculate RefPOC, MV no zero, proportion of MVs…
    always false in RA configuration
  Proposal: lose-less code modification
BIO extension to 1/16 MV resolution
  Issue: MV with precision 1/16 is rounded to ¼ precision inside BIO
  Proposal: extend BIO gradients filters ¼  1/16 eliminate MV rounding
Avg: 0,1%
Avg: 0,1%
Avg: 0,2%

## Slide 3: Longer MV regiment in RA
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,2% | 0,2% | 0,3% | 95% | 97%
Class A2 | -0,2% | 0,1% | 0,1% | 92% | 92%
Class B | -0,1% | 0,1% | 0,2% | 101% | 99%
Class C | 0,0% | 0,0% | 0,0% | 93% | 103%
Class D | 0,0% | 0,1% | -0,1% | 99% | 100%
Overall JVET | -0,1% | 0,1% | 0,1% | 96% | 98%
Class F (optional) | 0,0% | 0,2% | 0,2% | 92% | 98%
JVET-C0080

## Slide 4: BIO application in LD cases (loseless)
Random Access Main 10 |  |  |  |  |  | 
 |  | Y | U | V | EncT | DecT
Class A1 |  | 0,0% | 0,0% | 0,0% | 95% | 97%
Class A2 |  | 0,0% | 0,0% | 0,0% | 92% | 94%
Class B |  | 0,0% | 0,0% | 0,0% | 100% | 98%
Class C |  | 0,0% | 0,0% | 0,0% | 96% | 100%
Class D |  | 0,0% | 0,0% | 0,0% | 102% | 100%
Overall JVET |  | 0,0% | 0,0% | 0,0% | 97% | 98%
Class F (optional) |  | 0,0% | 0,0% | 0,0% | 92% | 98%
 |  | Low delay B Main10 |  |  |  | 
 |  | Y | U | V | EncT | DecT
Class B |  | 0,0% | 0,0% | 0,0% | 96% | 94%
Class C |  | 0,0% | 0,0% | 0,0% | 98% | 100%
Class D |  | 0,0% | 0,0% | 0,0% | 95% | 100%
Class E |  | 0,0% | 0,0% | 0,0% | 102% | 101%
Overall JVET |  | 0,0% | 0,0% | 0,0% | 97% | 98%
Class F (optional) |  | 0,0% | 0,0% | 0,0% | 91% | 99%
Low delay B Main10 |  |  |  |  |  | 
 |  | Y | U | V | EncT | DecT
Class B |  | 0,0% | 0,0% | 0,0% | 96% | 94%
Class C |  | 0,0% | 0,0% | 0,0% | 98% | 100%
Class D |  | 0,0% | 0,0% | 0,0% | 95% | 100%
Class E |  | 0,0% | 0,0% | 0,0% | 102% | 101%
Overall JVET |  | 0,0% | 0,0% | 0,0% | 97% | 98%
Class F (optional) |  | 0,0% | 0,0% | 0,0% | 91% | 99%
JVET-C0065

## Slide 5: BIO extension to 1/16 MV resolution
 |  |  | Random Access Main 10 |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
Class A1 |  |  | 0,0% | 0,2% | 0,1% | 98% | 99%
Class A2 |  |  | -0,1% | -0,1% | 0,0% | 98% | 97%
Class B |  |  | 0,0% | 0,0% | 0,1% | 106% | 113%
Class C |  |  | 0,0% | 0,0% | -0,1% | 94% | 103%
Class D |  |  | -0,2% | -0,1% | -0,1% | 101% | 102%
Overall JVET |  |  | -0,1% | 0,0% | 0,0% | 100% | 103%
Class F (optional) |  |  | 0,0% | -0,1% | -0,1% | 94% | 101%
 |  |  | Low delay B Main10 |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
Class B |  |  | 0,0% | -0,2% | 0,2% | 98% | 99%
Class C |  |  | 0,0% | -0,1% | -0,3% | 98% | 103%
Class D |  |  | 0,0% | -0,1% | -0,2% | 94% | 100%
Class E |  |  | -0,2% | 0,3% | -0,5% | 101% | 100%
Overall JVET |  |  | 0,0% | 0,0% | -0,2% | 98% | 100%
Class F (optional) |  |  | -0,1% | 0,4% | -0,1% | 92% | 100%
 |  |  | Low delay B Main10 |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
Class B |  |  | 0,0% | -0,2% | 0,2% | 98% | 99%
Class C |  |  | 0,0% | -0,1% | -0,3% | 98% | 103%
Class D |  |  | 0,0% | -0,1% | -0,2% | 94% | 100%
Class E |  |  | -0,2% | 0,3% | -0,5% | 101% | 100%
Overall JVET |  |  | 0,0% | 0,0% | -0,2% | 98% | 100%
Class F (optional) |  |  | -0,1% | 0,4% | -0,1% | 92% | 100%
JVET-C0072

## Slide 6: 3 modifications together
 |  |  | Random Access Main 10 |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
Class A1 |  |  | -0,2% | 0,2% | 0,2% | 95% | 97%
Class A2 |  |  | -0,3% | 0,1% | 0,2% | 93% | 94%
Class B |  |  | -0,1% | 0,2% | 0,2% | 102% | 103%
Class C |  |  | -0,1% | 0,1% | 0,0% | 94% | 105%
Class D |  |  | -0,1% | -0,1% | -0,1% | 101% | 102%
Overall JVET |  |  | -0,2% | 0,1% | 0,1% | 97% | 101%
Class F (optional) |  |  | 0,0% | 0,1% | 0,1% | 95% | 102%
 |  |  | Low delay B Main10 |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
Class B |  |  | 0,0% | -0,2% | 0,2% | 98% | 99%
Class C |  |  | 0,0% | -0,1% | -0,3% | 98% | 103%
Class D |  |  | 0,0% | -0,1% | -0,2% | 94% | 100%
Class E |  |  | -0,2% | 0,3% | -0,5% | 101% | 100%
Overall JVET |  |  | 0,0% | 0,0% | -0,2% | 98% | 100%
Class F (optional) |  |  | -0,1 | 0,4% | -0,1% | 92% | 100%
 |  |  | Low delay B Main10 |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
Class B |  |  | 0,0% | -0,2% | 0,2% | 98% | 99%
Class C |  |  | 0,0% | -0,1% | -0,3% | 98% | 103%
Class D |  |  | 0,0% | -0,1% | -0,2% | 94% | 100%
Class E |  |  | -0,2% | 0,3% | -0,5% | 101% | 100%
Overall JVET |  |  | 0,0% | 0,0% | -0,2% | 98% | 100%
Class F (optional) |  |  | -0,1 | 0,4% | -0,1% | 92% | 100%
JVET-C0065
JVET-C0072

## Slide 7: Acknowledgement
Would like to thank cross-checkers
  TDF, Bcom, Orange (JVET-C0080),
  Qualcomm (JVET-C0072),
  LGE (JVET-C0065)
  for their help!

## Slide 8: Conclusion
By minor fix of BIO implementation according to the recent JEM modifications we can achieve 0,2% avg. Luma BD-rate gain in RA with few lines code modifications, w/o complexity implication
Why not?

## Slide 9: Backup slides

## Slide 10: General equation for BIO
Ref L1
predicted block
Ref L0

## Slide 11: Motion refinement vector calculation
Step 1
  Input: luminance, gradients , POC difference ,
  Output:
 -surrounding
of refined sample

## Slide 12: Motion refinement vector calculation
Step 2
  Input:
  Output:
  BIO regularization parameters:
  m – minimal allowed denominator;
  r – avoid division by 0 in case zero gradients:
  l– maximum allowed magnitude for MV refinement: l
,
l<<1

## Slide 13: BIO extension to 1/16 MV resolution
Fractional position | Interpolation filter for gradient
0 | { 8, -39, -3, 46, -17, 5 },
1/16 | { 8, -32, -13, 50, -18, 5,}
1/8 | { 7, -27, -20, 54, -19, 5,}
3/16 | { 6, -21, -29, 57, -18, 5,}
1/4 | { 4, -17, -36, 60, -15, 4 },
5/16 | { 3, -9, -44, 61, -15, 4,
3/8 | { 1, -4, -48, 61, -13, 3,}
7/16 | { 0, 1, -54, 60, -9, 2,}
1/2 | { -1, 4, -57, 57, -4, 1 },
 | Interpolation filter for signal
 | { 0, 0, 64, 0, 0, 0,},
 | { 1, -3, 64, 4, -2, 0,}
 | { 1, -6, 62, 9, -3, 1,},
 | { 2, -8, 60, 14, -5, 1,}
 | { 2, -9, 57, 19, -7, 2,}
 | { 3, -10, 53, 24, -8, 2,}
 | { 3, -11, 50, 29, -9, 2,}
 | { 3, -11, 44, 35, -10, 3,}
 | { 3, -10, 35, 44, -11, 3,}