## Slide 1
BIO improvement to reduce the encoder and decoder complexities
(JVET-C0031)
May 2016
LG Electronics
Jaeho Lee (jhlee.lee@lge.com)

## Slide 2: Introduction
BIO (Bi-directional optical flow)
  Large coding gain (-2.4% BD-rate)
  Significant complexity (EncT: 134% & DecT: 224%)
  Need to reduce the complexity.
Proposal
  BIO skip method to reduce the encoding and decoding time.
  Time saving (EncT: 4~24% & DecT: 15%~45%) with negligible BD rate increment.

## Slide 3: Proposed Method (1/3)
Motivation
  BIO assumption: moving object with constant speed during the short time (constant motion condition).
  BIO predictor: the above constant motion condition satisfied refinement predictor.
  Additional assumption: bi-prediction (block-based) MV represents the object (pixel-based) motion when coding block is small enough.
  Skip BIO if the constant motion condition is satisfied from bi-prediction MVs for small block.

## Slide 4: Proposed Method (2/3)
BIO is skipped if the following (block-based) constant motion condition is satisfied.
  True bi-prediction: Two predictions come from different time directions.
  Distances to reference frames are same.
  Two bi-prediction MVs are opposite to each other and have the same magnitude.

## Slide 5: Proposed Method (3/3)
BIO skip method can be applied for enough small block sizes
  Test description: 4 cases according to the applied block sizes
Test | BIO skip condition description
Test 1 | Skip BIO when constant motion condition is satisfied and sub-PU is 4x4.
Test 2 | Skip BIO when constant motion condition is satisfied and sub-PUs are <= 8x8.
Test 3 | Skip BIO when constant motion condition is satisfied and sub-PUs are <= 16x16.
Test 4 | Skip BIO when constant motion condition is satisfied.

## Slide 6: Experimental results (1/2)
Results for Random Access Main 10: Time saving with negligible BD rate increase.
Results for Low Delay Main 10: No runtime increment for low delay B main 10
 | Random Access Main 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Test 1 |  |  |  |  | Test 2 |  |  |  |  | Test 3 |  |  |  |  | Test 4 |  |  |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.16% | 0.07% | 100% | 88% | 0.01% | 0.12% | 0.04% | 99% | 87% | 0.03% | 0.20% | 0.09% | 97% | 86% | 0.06% | 0.11% | 0.03% | 92% | 77%
Class A2 | 0.01% | -0.05% | -0.07% | 97% | 89% | -0.02% | -0.09% | -0.05% | 95% | 88% | 0.01% | 0.00% | 0.00% | 93% | 88% | 0.11% | 0.02% | 0.04% | 89% | 78%
Class B | 0.06% | 0.09% | 0.11% | 95% | 86% | 0.06% | 0.03% | 0.04% | 95% | 85% | 0.08% | 0.05% | 0.09% | 93% | 81% | 0.17% | 0.06% | 0.13% | 89% | 75%
Class C | 0.10% | -0.04% | -0.02% | 95% | 82% | 0.12% | 0.04% | -0.08% | 95% | 81% | 0.20% | 0.04% | 0.02% | 93% | 80% | 0.31% | 0.14% | 0.07% | 89% | 71%
Class D | 0.15% | 0.05% | -0.05% | 94% | 80% | 0.23% | 0.16% | 0.00% | 95% | 80% | 0.37% | 0.02% | -0.13% | 93% | 78% | 0.59% | 0.36% | 0.22% | 89% | 71%
Overall | 0.07% | 0.04% | 0.01% | 96% | 85% | 0.08% | 0.05% | -0.01% | 96% | 84% | 0.14% | 0.06% | 0.01% | 94% | 83% | 0.25% | 0.14% | 0.10% | 90% | 74%
Low delay B Main10 |  |  |  |  | 
Class | Y | U | V | EncT | DecT
Class B | 0.00% | 0.00% | 0.00% | 0% | 0%
Class C | 0.00% | 0.00% | 0.00% | 0% | 0%
Class D | 0.00% | 0.00% | 0.00% | 0% | 0%
Class E | 0.00% | 0.00% | 0.00% | 0% | 0%
Overall | 0.00% | 0.00% | 0.00% | 0% | 0%

## Slide 7: Experimental results (2/2)
Crosscheck
  JVET-C0052 by Samsung

## Slide 8: Conclusion
BIO skip method is proposed.
Encoder & decoder time saving with negligible BD-rate increase.
We recommend that the proposed method is adopted into JEM.