## Slide 1: JVET EE 2.6 Modification of Merge Candidate Derivation: ATMVP Simplification and Merge Pruning
Sungwon Lee, Wei-Jung Chien, Li Zhang, Jianle Chen, Marta Karczewicz

## Slide 2: EE 2.6 Modification
Further study about two tools introduced in JVET-B0058.
ATMVP simplification
  Use the first merge candidate to determine where to fetch the temporal motion vector
    Remove neighboring blocks scan
  More aligned sub-PU temporal motion vector derivation
    Disallow mirror motion derivation, when
    Temporal motion vector is from co-located reference picture
    or LDC flag is on (i.e. no future frames in both reference lists)
Merge Pruning
  Use POC instead of RefIdx when comparing two merge candidates
  Combined bi-predictive and Zero motion vector merge candidates are pruned
  ATMVP is pruned when all sub-PU MVs are identical
Thanks to Huawei, Samsung, and Sharp for the crosscheck

## Slide 3: Summary of Results
 | Anchor | Test | Cross-check
Test. 1-1 | HM16.6 + ATMVP + HPMV | Anchor + ATMVP simplification | Huawei, Sharp
Test. 1-2 | HM16.6 + ATMVP + HPMV | Anchor + merge pruning | Huawei, Sharp
Test. 1-3 | HM16.6 + ATMVP + HPMV | Anchor + ATMVP simplification + merge pruning | Huawei, Sharp
Test. 2-1 | JEM2.0 | Anchor + ATMVP simplification | Samsung
Test. 2-2 | JEM2.0 | Anchor + merge pruning | Samsung
Test. 2-3 | JEM2.0 | Anchor + ATMVP simplification + merge pruning | Samsung

## Slide 4: JVET EE 2.6 over HM16.6 + ATMVP + HPMV
Tool-on Test
Overall performance
Crosschecked by JVET-C0073 (Sharp) and JVET-C0085 (Huawei)

## Slide 5: JVET EE 2.6 over JEM2.0
Overall performance
Tool-on Test
Crosschecked by JVET-C0060 (Samsung)