## Slide 1: EE2.4: Dequantization and scaling for next generation containers
Jie Zhao, Andrew Segall and Seung-Hwan Kim

## Slide 2
Overview
Response to EE2.4 – “De-quantization and scaling for next generation containers”
  Answers to some of the questions raised as part of the EE process.
  Additionally, report/propose a new weighted PSNR metric to measure the performance of the EE2.4-like tools that attempt to re-shape the quantization noise.
  Using this weighted PSNR, obtained gains of ~1.9% vs. luma adaptive quantization with deltaQP signalling for SDR content in ST-2084 container (AI coding)

## Slide 3: Background
In Oct. 2015 meeting, a study was presented suggesting that QP should vary relative to luma value when coding content in a ST-2084 container
Tested and confirmed by MPEG/JCT-VC CE1 to provide (significant) benefit
Incorporated into the MPEG/JCT-VC HDR anchors
QP adaptation has draw backs
  Bit-rate overhead
  Limited granularity
Relationship between Y2020 and Y709 for a collection of 20 sequences
Source: COM16-C1030 / m37439 “Performance Investigation of high dynamic range and wide color gamut video coding techniques”

## Slide 4: Background
Proposal - JCTVC-B0054
  Allow decoder to infer quantization change
  Estimate the mean of the reconstructed TU at the decoder
    Use reconstructed DC coefficient
    Mean of prediction
  Determine scale factor from LUT
  Scale the coefficients after the secondary transform (Scaling applied to luma AC coefficients and all chroma coefficients)
  Showed 2.0% gain comparing to delta QP approach at CTU16x16 granularity.

## Slide 5: Questions raised in EE Process
How complex is the function f() in the proposal?
How much overhead is required for delta QP signaling at different granularities?
What is performance of tool for SDR content in an ST-2084 container?
Compare with other techniques studied in HDR JCTVC activity.

## Slide 6
Q1: How complex is the function f() in the proposal?
The f() function converts DC transform coefficient to DC pixel value. It consists compare, add and shift, which we assert that the complexity is low.
Int TComTrQuant::xConvertDCCoeffToDCVal (TComTU &rTu, Int DCCoeff, Int uiWidth, const ComponentID compID)
{
Int DCVal;
const TComSPS *pSPS = rTu.getCU()->getSlice()->getSPS();
const Int channelBitDepth = pSPS->getBitDepth(toChannelType(compID));
const Int maxLog2TrDynamicRange = pSPS->getMaxLog2TrDynamicRange(toChannelType(compID));
Int iTransformShift = getTransformShift (channelBitDepth, rTu.GetEquivalentLog2TrSize(compID), maxLog2TrDynamicRange);
if (iTransformShift > 0)
DCVal = (DCCoeff + (1<<(iTransformShift-1)) ) >> iTransformShift;
else
DCVal = DCCoeff << iTransformShift;
Int rounding = 1<<(g_aucConvertToBit[uiWidth]+1);
DCVal = (DCVal+rounding)>>(g_aucConvertToBit[uiWidth]+2); // DCVal/uiWidth
return DCVal;
}

## Slide 7: Q2. What is overhead for delta QP signaling at different granularities
Incorporated a bit-count of the delta QP signaling bits the luma adaptive, delta QP decoder in our EE software.
Test:
  JCT-VC HDR test sequences;
  Random Access with fixed QP fixed QP 21, 25, 29 and 33;
  Delta QP signaled at a CTU level
  CTU size of 64x64, 32x32 and 16x16, respectively

## Slide 8: Q3. What is performance for SDR content in an ST-2084 container
We converted the JVET sequences to ST-2084 using HDRTools
Evaluated the performance of the proposed method versus the delta QP approach.
Developed a test methodology that uses a weighted PSNR calculation, where the weights capture the target weighting of the QP variation.
Fig. System for testing the models developed in the document

## Slide 9: Q3. Performance for SDR content in an ST-2084 container (Cont.)
Observe that the quantization noise in the original BT.1886/BT.709 domain is changed when converted to the ST-2084/BT.709 domain
Derive weighting function to convert distortion in ST-2084 to BT.1886.
Collected the MSE in the BT.1886/BT.709 domain and MSE in the ST-2084/BT.709 domain according luma value, and plotted their ratios.
There is a clear trend between the MSE ratio and luma.
Fig 2. MSE ratio in BT.1886/ST-2084 vs. pixel value in luma, Cb, Cr

## Slide 10: Q3. Performance for SDR content in an ST-2084 container (Cont.)
For sqrt of MSE ratio Y, use fitted curve and obtain weight LUT
  y = p1*x^2 + p2*x + p3
  where p1 = 9.5743e-006, p2 = 0.00061068, and p3 = 0.90209
Incorporate Weighted SSE in encoder RD cost calculation
  weight = LUTW[org[i]];
  Diff = org[i]-rec[i];
  weightedSSE = weight* (Diff^2);
Calculate the weighted PSNR of the output.
Fig. 3. Fitted curve for sqrt(MSE ratio Y)

## Slide 11: Q3. Performance for SDR content in an ST-2084 container (Cont.)
To confirm the weighted PSNR calculation, we computed PSNR measured in BT.1886 (i.e. A vs. A’), and PSNR in ST-2084 (i.e. B vs. A”) and their differences.
Without weighting PSNR difference in two domains is around 5 to 6 dB.
With the weighted PSNR, the PSNR difference averages only 0.15dB
Fig. 3. PSNR differences in ST-2084 vs. BT.1886

## Slide 12: Experimental Results
Coded JVET sequences in ST-2084 using the EE2.4 software with the following two configurations
  1) Luma-adaptive QP approach which explicitly signalling Delta QP at CTU level
  2) Proposed Luma adaptive coefficient scaling
Note
  For 1) QP LUT ranges [0 to -12] as shown in the Fig. 4, input slice QP 22, 27, 32, 37
  For 2) We added 6 to LUT QP, and reduced slice QP by 6 in order to adjust the DC quantization in the proposed system
Fig.4. QpOffset Luma relation for SDR data in ST-2084

## Slide 13: Experimental Results
All Intra Results: explicit delta QP approach vs. CTC (converted to ST-2084, and using weighted PSNR)
All Intra Results: Proposed coefficient scaling approach vs. CTC (converted to ST-2084, and using weighted PSNR)
As shown in the result, the proposed coefficient scaling method has a bit-rate savings of ~1.9% compared to a delta QP based approach.

## Slide 14
Conclusion
Addressed questions previously recommended in EE document.
Moreover, provide more analysis and result for coding SDR data in ST-2084 container.
Shows the method proposed in JVET-B0054 outperforms explicit, delta QP signaling by approximately 1.9% for AI.
Propose to further investigate this technology and continue to include it in EE study.

## Slide 15: EE2.4 Dequantization and scaling for next generation containers
Jie Zhao, Andrew Segall and Seung-Hwan Kim