## Slide 1: Parallel deblocking filter for QTBT (JVET-D0044)
Hyeongmoon Jang (hyeongmoon.jang@lge.com)

## Slide 2: Summary
Parallel deblocking filter for QTBT
Disable deblock filtering on block boundaries
  Block width < 8 (for vertical boundaries)
  Block height < 8 (for horizontal boundaries)
Experimental results
Crosscheck
  JVET-D0080 (MediaTek)
 | AI10 | RA10 | LDB10 | LDP10
Class A1 | -0.1% | 0.0% |  | 
Class A2 | -0.1% | -0.1% |  | 
Class B | -0.2% | 0.0% | 0.1% | 0.0%
Class C | -0.1% | 0.1% | 0.0% | 0.1%
Class D | -0.1% | 0.0% | 0.0% | 0.0%
Class E | -0.1% |  | 0.1% | 0.2%
Overall | -0.1% | 0.0% | 0.1% | 0.1%
Enc[T] | 100% | 100% | 101% | 102%
Dec[T] | 100% | 101% | 104% | 99%

## Slide 3: Introduction
In HEVC
  Parallel processing for deblocking filter is already used
    Deblocking filter is not applied to 4x4 TU and PU boundaries
In current JEM
  Deblocking filter is applied to all CU block boundaries
  Effect of filtering on Nx4, 4xN block boundaries
    Filtered pixels can affect filtering decision of consecutive block boundary
    Adjacent boundaries cannot be processed in parallel

## Slide 4: Proposed method
Proposed method
  Disable deblock filtering on block boundaries
    Block width < 8 (for vertical boundaries)
    Block height < 8 (for horizontal boundaries)
Example of proposed parallel filtering method

## Slide 5: Experimental results
 | All Intra main10 |  |  | Random Access Main10 |  |  | Low-delay B mian10 |  |  | Low-delay P main10 |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A1 | -0.1% | 0.0% | 0.0% | 0.0% | 0.1% | -0.1% |  |  |  |  |  | 
Class A2 | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% |  |  |  |  |  | 
Class B | -0.2% | -0.1% | -0.1% | 0.0% | -0.2% | -0.1% | 0.1% | 0.0% | 0.1% | 0.0% | -0.1% | -0.1%
Class C | -0.1% | -0.1% | -0.1% | 0.1% | -0.1% | 0.2% | 0.0% | 0.3% | 0.1% | 0.1% | 0.2% | 0.4%
Class D | -0.1% | -0.1% | -0.1% | 0.0% | -0.2% | -0.3% | 0.0% | 0.1% | -0.3% | 0.0% | -0.4% | -0.1%
Class E | -0.1% | 0.0% | 0.0% |  |  |  | 0.1% | -0.1% | -0.3% | 0.2% | 0.1% | 1.4%
Overall | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 0.1% | 0.0% | -0.1% | 0.1% | -0.1% | 0.3%
Enc [%] | 100% |  |  | 100% |  |  | 101% |  |  | 102% |  | 
Dec [%] | 100% |  |  | 101% |  |  | 104% |  |  | 99% |  | 

## Slide 6: Experimental results
Encoded QTBT structure by JEM3.1 (ClassA1, Campfire, QP22)

## Slide 7: Experimental results
Reconstructed picture by JEM3.1 (ClassA1, Campfire, QP22)

## Slide 8: Experimental results
Reconstructed picture by proposed method (ClassA1, Campfire, QP22)

## Slide 9: Experimental results
Encoded QTBT structure by JEM3.1 (ClassA1, ToddlerFountain, QP22)

## Slide 10: Experimental results
Reconstructed picture by JEM3.1 (ClassA1, ToddlerFountain, QP22)

## Slide 11: Experimental results
Reconstructed picture by proposed method (ClassA1, ToddlerFountain, QP22)

## Slide 12: Conclusion
Recommendation
  It is recommended to parallel deblocking filter which is only applied to block boundaries
    Block width is a greater than 4 samples for vertical boundaries
    Block height is a greater than 4 samples for horizontal boundaries