## Slide 1: Cross-Component Peak Signal to Noise Ratio (xPSNR) support in the HM and JEM software
10/18/2016

## Slide 2: Video Standardization using Peak Signal to Noise Ratio (PSNR)
PSNR traditionally used to measure quality for video standardization
  First compute mean square error for each color plane
  Then PSNR for each color plane can be computed as:
  An overall PSNR cost across all frames computed using two alternative methods
  Accounting for colour is performed using weighted average:

## Slide 3: Observations
Computations are based on Luma (Y’), Cb, and Cr planes
  Essentially, compute how much these planes have changed
Unfortunately Luma, Cb, and Cr are not exactly physical quantities.
  Luma is an approximation of the Luminance component in CIE 1931 (XYZ)
  Considerably impacted by the transfer function (e.g. BT.709, BT.2100) used
  Cb and Cr are just difference signals for achieving colour de-correlation
    However, distortions in Chroma could result in distortions in luminance
      Chroma Leakage
  Averaging separate plane distortion does not consider interactions of colour samples
We should care more about the actual pixels, not planes

## Slide 4: HDR/WCG Observations: Looking at plane averaging

## Slide 5: HDR/WCG Observations: Looking at pixel distortion

## Slide 6: Distortion computations per pixel
DE2000 metric
  Convert image data to L*a*b* space and L*C*h* (lightness, chroma, hue) space
  Per pixel distortion:
Per pixel distortion can also be computed in CIE 1931 XYZ space, as well as RGB

## Slide 7: Distortion computations per pixel in Y’CbCr domain
  for 4:4:4
  for 4:2:0

## Slide 8: Support of xPSNR added in HM & JEM
HM vs JVET comparison using xPSNR
  performance for Open GOPs
  performance for Closed GOPs

## Slide 9: Suggestion
xPSNR “might” be able to better capture or account for distortion in colour
Simple to compute (almost as simple as PSNR)
xPSNR code available for both the HM and JEM, as well as for HDRTools
  suggest adopting this code into the official HM and JEM
Encourage use of xPSNR instead of or in addition to weighted colour PSNR
However, note this is still a PSNR “like” metric
  It does not follow any psychovisual model
  Does not account for texture/structure
  Does not account for edges, brightness sensitivity, or other spatial characteristics
  Does not account for temporal distortions