## Slide 1: Samsung’s response to CfE on Video Compression with Capability beyond HEVC (360 category)
E.Alshina, K.Choi, V.Zakharchenko
S.N.Akula, A. Dsouza, C. Pujara, KK Ramkumaar, A. Singh

## Slide 2: Technology Description
Goal: Study potential of 360 video compression system w/o low-level tools
Key elements:
  New layout for Compact Icosahedral Projection (ISP)
    Friendlier for tiles
  Sphere rotation prior to conversion to ISP
    Reduces discontinuity on a boarder
  General purpose engine
    With lesser coding tools as compared to JEM 6.0 demonstrated better compression than JEM 6.0

## Slide 3: New layout for CISP
Non-compact ISP
Proposed compact ISP
Proposed layout

## Slide 4: CISP layout with dimensions
WCISP = 5  W + 2  ph + 2  pd
HCISP = 2  H+ pv

## Slide 5: Comparison of current and proposed frame packing
Proposed frame packing
Current frame packing
Discontinuities | Proposed | Current
Total | 11 | 9
Angular | 4 | 4
Horizontal | 3 | 5
Vertical | 4 | 0
Major idea
  All angular discontinuities are in the same region (poles)
  No content between poles and equators are interleaved

## Slide 6: Sphere rotation
Below table shows the optimal (X,Y,Z) rotation for CISP for CfE bit-streams and one frame output of optimal rotation
Test sequence | SVideoRotation |  | 
 | X | Y | Z
Trolley | 30 | 4 | 3
Skateboarding_in_lot | 333 | 181 | 0
Chairlift | 13 | 21 | 353
KiteFlite | 63 | 0 | 354
Harbor | 167 | 0 | 0
Harbor before Rotation
Harbor After Rotation
SPIE 2017: “Discontinuity Minimization for Omnidirectional Video Projections ”

## Slide 7: Results
Detailed results are available in contribution excel sheet
Test sequence | E2EWS-PSNR BD-rate |  | 
 | Y | Cb | Cr
Trolley | -21% | -28% | -39%
Skateboarding_in_lot | -36% | -46% | -56%
Chairlift | -42% | -51% | -43%
KiteFlite | -23% | -42% | -52%
Harbor | -27% | -46% | -47%
Average | -30% | -43% | -47%
BD-rate performance relative to CfE anchor

## Slide 8: Results (Contd…)
Conversion only result
Test sequence | E2EWS-PSNR BD-rate |  | 
 | Y | Cb | Cr
Trolley | 45.15 | 56.57 | 56.48
Skateboarding_in_lot | 49.51 | 61.32 | 60.97
Chairlift | 50.05 | 59.45 | 59.52
KiteFlite | 46.21 | 56.34 | 56.37
Harbor | 48.46 | 57.75 | 56.72
Average | 47.88 | 58.29 | 58.01

## Slide 9: Recommend EVPs
Below image shows two pain points with many seams

## Slide 10: EVP subjective quality
Evil Viewport targeting to the problematic point at the picture boundary: left proposed, right – CfE anchor (Rate = 2400)

## Slide 11: EVP subjective quality (Contd…)
Evil Viewport targeting to the problematic point in the middle of the coded picture: left proposed, right – CfE anchor (Rate = 2400).

## Slide 12: Conclusion
Contribution demonstrated 30%, 43% and 46% performance gain over CfE anchor in 360 category for Y, Cb and Cr components respectively
Codec engine uses at most 20 tools on the top of HEVC
There is no 360 specific modification of the codec at block level
New compact layout for ISP is used as coding projection along with optimal sphere rotation

## Slide 13: Thank You