## Slide 1: AHG5 External Memory Access Evaluation with the Consideration of Cache
JVET-G0061
Xiang Li, Ted Hsieh, Jianle Chen, Marta Karczewicz

## Slide 2: Impact of Memory Access by Video Codec
Average memory access – Big impact on power consumption of mobile devices
  Higher memory access in average lead to higher power consumption
Worst case memory access – Impact on set-top-box applications
  Worst case memory access may lead to frame dropping during decoding

## Slide 3: Memory Access with and without Cache
Decoder memory access without cache (theoretical worst case)
Decoder memory access with cache
Reading from cache is with lower latency and lower power cost
Reading from external memory is with high delay and more power cost
External memory access is the focus

## Slide 4: Study External Memory Data Access with Valgrind
Valgrind is a widely used free memory profiling tool under GNU General Public License
  It supports PC and mobile platforms including X86/Linux, AMD64/Linux, ARM64/Linux, MIPS64/Linux, ARM64/Android, X86/MacOSX 10.10, etc.
As a sub-tool of Valgrind, Cachegrind [4] is a cache profiler which simulates first-level and last-level caches.
Analysis on external memory data access
  Decode JEM-6.0 4K anchor bitstreams and use Cachegrind to measure the external memory data reading (last level cache data reading misses) by the JEM-6.0 decoder with different size settings of last level cache.
  Only data reading is considered
    External memory data writing of a practical decoder is almost constant for given resolution and frame rate

## Slide 5: Simulation Settings
 | D1 (level 1 cache) |  |  | LL (last level cache) |  | 
 | size(B) | associativity | line size (B) | size (B) | associativity | line size (B)
LL size 128B | 128 | 2 | 64 | 128 | 2 | 64
LL size 1KB | 128 | 2 | 64 | 1024 | 2 | 64
LL size 16KB | 128 | 2 | 64 | 16384 | 2 | 64
LL size 128KB | 128 | 2 | 64 | 131072 | 2 | 64
LL size 512KB | 128 | 2 | 64 | 524288 | 2 | 64
LL size 1MB | 128 | 2 | 64 | 1048576 | 2 | 64
LL size 2MB | 128 | 2 | 64 | 2097152 | 2 | 64
Seven sets of setting with different sizes of last level cache

## Slide 6: External memory reading for ClassA sequences

## Slide 7: External memory reading vs cache size
Cache size has a significant impact on external memory reading
  Different cache sizes may lead to over 500 times difference in external memory reading

## Slide 8: Conclusions
Average external memory data access has big impact on power consumption of mobile devices
JEM-6 decoder external memory data access (reading) is measured by a widely used cache profiling tool – Valgrind
Simulations show that cache size has a significant impact on decoder external memory data access
  Different cache sizes lead to over 500 times difference in external memory data reading by JEM-6 decoder for 4K sequences
  Cache size is implementation dependent
Theoretical worst case of memory access looks like an upper bound which is too far away from practical implementations
Propose: further study external memory data access with the consideration of cache