## Slide 1: Stereoscopic 360 video compression with the next generation video codec
JVET-G0064
Félix Henry, Joël Jung, Ali Ouach, Bappaditya Ray, Philipp Schwellenbach – ORANGE LABS

## Slide 2: Stereoscopic 360 video
Monoscopic 360
  Your two eyes are inside a « sphere » where the video is projected
Stereoscopic 360
  Each eye is inside its own sphere

## Slide 3: Stereoscopic 360 video
360 video is about immersion
    True immersion comes with depth sensation
    Monoscopic is acceptable when the subject is distant, but if the subject get « closer », it only gets larger on the projection surface
Suggestion
  Please look at existing high quality mono and stereo 360 videos
  Come and see a few videos I have on HMD
What we believe at Orange
  Stereo 360 is a very important format to address in the Next Generation Video Codec because
    it provides excellent immersive sensation
    it does so at a very small cost (a 2D codec)

## Slide 4: Multiview formats in previous standards
Stereo 360 video is essentially a multiview format
Multiview compression in the two past standards of ISO & ITU-T
  First a core 2D video compression algorithm is standardized (V1)
  Then an extension re-uses the core 2D engine to compress multiple views
This made sense
  The « formats of introduction » of the standard were 2D video
  Multiview extensions had limited success compared to V1
Things may change if stereo 360 is a format of introduction for Next Generation Video Coding (NVGC)

## Slide 5: Stereo 360 in the NGVC
Possible approaches in increasing order of consideration for Stereo 360
  1. We could decide to only handle monoscopic 360 in NGVC V1 and keep stereoscopic 360 work for a later MV-NGVC.
  2. We could introduce stereoscopic 360 video as an option in our Common Testing Conditions (CTCs) while allowing only non-normative changes (frame packing, temporal multiplex, …)
  3. We could introduce stereoscopic 360 video as an option in CTCs while allowing normative
  4. NGVC could be a multiview format from the beginning (with the appropriate profiles for pure 2D and stereoscopic 360)
In our opinion, the usual approach (option 1) is risky

## Slide 6: Why taking the « usual » approach may be risky
From experience, once V1 encoders and decoders get deployed, it is very difficult or impossible to upgrade the existing equipment.
      A potential rapid introduction of NGVC V1 codecs in devices, before Multiview NGVC is released would make the upgrade difficult and delayed.
From experience, the industrial effort spent on extension encoders and decoders is smaller than the one spent on the 2D “basis”.
      “optimal” compression of stereoscopic 360 would be missed.
It would be a bad message if we issued a new codec that only does part of the work for real 360 immersion
If stereoscopic 360 is not handled efficiently in V1, we run the risk of interoperability issues.
      Worst scenario: stereoscopic 360 format is scattered between V1 (using frame packing or other non-normative approaches) and V2 (MV-NGVC).

## Slide 7
Simulations and results

## Slide 8: Test sequences
Sequence | FPS | Frames encoded | Resolution per view | Comment
Dancer | 30 | 32 | 4096x2048 | 
BearAttack | 30 | 32 | 1920x1920 | Left and right parts of images were strictly similar (960 pixels on each side of the original 3840x1920). A cropped version of the BearAttack sequence is used limited to the center half. The disparity is very high.
Sheriff | 30 | 32 | 4320x2160 | Synthetic
LRRH | 30 | 32 | 3840x1920 | Same characteristics as BearAttack but the video was kept as is.
Driving | 30 | 32 | 4096x2048 | 
JamSession | 60 | 64 | 4096x2048 | Downsampled from 8K original using 360Lib. Disparity is low in most areas.
SkateBoardTrick | 60 | 64 | 4096x2048 | Downsampled from 8K original using 360Lib. Disparity is low in most areas.
Train | 60 | 64 | 4096x2048 | Downsampled from 8K original using 360Lib. Disparity is low in most areas.

## Slide 9: Dancer sequence

## Slide 10: BearAttack sequence

## Slide 11: Sheriff sequence

## Slide 12: JamSession sequence

## Slide 13: Driving sequence

## Slide 14: SkateboardTrick sequence

## Slide 15: LRRH sequence

## Slide 16: Train sequence

## Slide 17: Tests performed
Test Name | Input format | Software | Remarks
Anchor: Simulcast HEVC | Left and right views encoded separately | HM15.0 | 
Test 1: 3D-HEVC |  | HTM 13.0 | No depth map encoded.
Test 2: MV-HEVC |  | HTM 13.0 | 
Test 3: Frame packing HEVC | Full resolution top/bottom | HM14.0 | 
Test 4: Temporal multiplexing of views HEVC | One sequence with double FPS, alternating left and right views | HM14.0 | We kept the default GOP16 coding structure for RA.
Test 5: Frame Packing HEVC + IBC on | Full resolution top/bottom | HEVC SCC 16.15_SCM8.4 | Only IBC switched on (we checked that switching it off produces HM-decodable bitstreams). No optimization of IBC.
  Random Access (GOP 8 structures except for Test 4)
  Low Delay B

## Slide 18: Results
Test Name | Random Access |  |  | Low Delay B |  | 
Measure | Y-BDR | Enc T | Dec T | Y-BDR | Enc T | Dec T
Test 1: 3D-HEVC | -32.7% | 65.0% | 183.3% | -32.3% | 63.6% | 168.8%
Test 2: MV-HEVC | -31.9% | 103.4% | 124.1% | -31.1% | 109.5% | 129.1%
Test 3: Frame packing | +1.7% | 124.6% | 136.9% | +4.8% | 114,6% | 128,5%
Test 4: Temporal multiplexing of views | +39.5% | 133,6% | 172,5% | +45.4% | 134,8% | 152,9%
Test 5: Frame Packing + IBC on | -19.3% | 111.8% | 219.7% | -16.4% | 114.0% | 225.1%
In each experiment:
Rate = total bit rate
PSNR = mean PSNR per view

## Slide 19: Results (RA, sequence by sequence)

## Slide 20: Remarks on results
PSNRs of both views are always very close (usually 0.1 dB difference).
Test 4 (temporal multiplex) is very far from optimal
    Coding structure not adapted
    Ratio of intra pixels different from other test because of first frame and short duration
    The BDR measure varies from +235% to -51% across sequences.
In Test 5, Intra Block Copy is not optimized for frame packing

## Slide 21: Conclusions
We believe that stereo 360 is a very important format to address
We would prefer that the format is considered in V1 of the Next Generation Video Codec
  The way it is handled is to be discussed
  We suggest stereo 360 videos are added to the CTCs (after CfP)
We are ready to do more testing
  Looking for feedback and suggestions
    Additional sequences
    Better coding structure for Test 4
    New tests (frame packing with subsampling)

## Slide 22: Thank you