## Slide 1: Unified-PDPC
JVET-G0068
Advanced Technology Team
Sony Europe Ltd.
Magali Philippe
Sony Corp.

## Slide 2: Background
  ARSS and PDPC are tools used in JEM6.0 to help the intra prediction, by sometimes filtering reference samples. They are both quite similar and cannot be used at the same time for a same TU.
  ARSS is a choice between a 3-tap low pass filter, or a 5-tap low pass filter. However there isn’t a big difference by fixing it to a 3-tap filter
    By fixing ARSS, we can notice it is the same filter as PDPC, with different parameters
    This will be detailed on the next slide

## Slide 3: Background: PDPC filtering
With {p1,p2,p3,p4,p5,p6} as in PDPC table : g_pdpc_pred_param

## Slide 4: Background: ARSS and PDPC filtering schemes
  As shown on the previous slide, ARSS and PDPC use the same type of filtering:
    PDPC applies a first reference sample filtering, then adds extra steps
    ARSS can be interpreted as a PDPC-filter, with different coefficients(0 for the “extra steps”)
  Why not unify them as the same filter, with different parameters under different conditions?

## Slide 5: Proposed Scheme
Instead of filtering sometimes with PDPC, sometimes with ARSS, sometimes not:
  Sometimes filter with UPDPC, otherwise use unfiltered reference samples
  If UPDPC is applied, filter with PDPC coefficients sometimes, derived coefficients(“ARSS” case) other times
    Use the NSST condition to decide which type of filtering is better
    Code the “UPDPC flag” with 4 contexts, depending on the MDIS conditions, and NSST value
    Only code the “UPDPC flag” when 3 or more coefficients are present in the TU

## Slide 8: Results
The proposed scheme was tested under AI configuration, over JEM6.0
  This is “version 2” in the document
  Overall the BD-rate is unchanged
  Encoding time is overall reduced by 16%. Note that it is reduced by 18% for class A1(which is one of the slowest to encode)
Thank you to Qualcomm for cross-checking (JVET-G0134)

## Slide 9: Results
The following P-UPDPC version was tested under AI configuration, over JEM6.0
  P-UPDPC : no flag signalling for planar mode

## Slide 10: Results
The proposed scheme was tested in combination with UW-planar(JVET-E0068) and W66(JVET-F0104), under AI configuration, over JEM6.0

## Slide 11: Results
The proposed scheme was tested in combination with UW-planar(JVET-E0068) and W66(JVET-F0104), CARSS, and CPDPC, under AI configuration, over JEM6.0
  Other combinations are presented in the word document

## Slide 12: Conclusion
We believe the propose scheme shows that ARSS can be replaced by PDPC
  A modification to the current JEM intra prediction filtering tools has been presented:
    It is a unification of ARSS and PDPC. In effect they were both combined in one tool called “unified-PDPC”
      Without any BD-rate loss on intra configuration
      With an improvement of about 15% on runtime
  The tool is compatible with other EE1-related changes, presented in the contribution word document
We propose that ARSS is removed, and PDPC is enabled even when NSST is present