## Slide 1
Geert Van der Auwera, Muhammed Coban, Marta Karczewicz (Qualcomm)
AHG8: ACP with padding for 360-degree video (JVET-G0071)

## Slide 2: Introduction
Adjusted cubemap projection (ACP)
  Target is uniform sphere sampling with limited texture deformation
  Simple packing (3x2 same as CMP packing schemes)
  Perturbed cubemap lookup vector
Adjustment functions
  Approximate uniform sphere sampling by adjustment functions
  Forward (2D-to-3D) conversion adjustment function
  Inverse (3D-to-2D) conversion adjustment function

## Slide 3: ACP vs. CMP
Example 3x2 packing
CMP
ACP

## Slide 4: ACP Seam Artifacts
ACP 3x2 packing has continuous and discontinuous boundaries
Influenced by motion intensity, in-loop filtering
Examples of viewports:
Viewport1 (-135°, 35°)
Viewport2 (45°, -35°)
Motion
seam
Filtering
seam

## Slide 5: ACP Padding Proposal
Top and bottom picture halves are padded; coding size is unchanged (CTC)
Adjacent faces not padded
Geometry padding; width is configurable in software
Padding width 4 is reasonable trade-off between quality and coding efficiency
padding
padding

## Slide 6: Viewport examples
Viewport 1
Not padded
Padded

## Slide 7: Viewport examples
Viewport 2
Not padded
Padded

## Slide 8: Results
BD-rates (RA) for ACP with padding width 4 (CTC)
Thanks to Interdigital for cross check (JVET-G0132).
ACP with padding vs. ERP |  |  | SPSNR-NN (End to End) |  |  | SPSNR-I (End to End) |  |  | CPP-PSNR (End to End) |  |  | WS-PSNR (End to End) |  | 
 | Face W | Face H | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Trolley | 1184 | 1184 | -6.7% | 3.1% | -1.1% | -6.9% | 2.9% | -1.2% | -6.9% | 2.9% | -1.2% | -6.8% | 3.0% | -1.2%
GasLamp | 1184 | 1184 | -3.6% | 2.3% | 7.4% | -3.7% | 2.2% | 7.2% | -3.7% | 2.2% | 7.3% | -3.6% | 2.4% | 7.4%
Skateboarding_in_lot | 1184 | 1184 | -16.0% | -16.4% | -17.1% | -16.1% | -16.6% | -17.2% | -16.0% | -16.6% | -17.3% | -15.9% | -16.4% | -17.2%
Chairlift | 1184 | 1184 | -25.0% | -18.1% | -18.3% | -25.0% | -18.1% | -18.3% | -25.1% | -18.1% | -18.4% | -25.0% | -18.1% | -18.4%
KiteFlite | 1184 | 1184 | -9.3% | -2.5% | -4.2% | -9.5% | -2.7% | -4.3% | -9.4% | -2.7% | -4.3% | -9.2% | -2.6% | -4.2%
Harbor | 1184 | 1184 | -8.7% | -3.8% | -2.9% | -8.9% | -3.9% | -2.9% | -9.2% | -3.9% | -2.9% | -9.0% | -3.8% | -2.8%
PoleVault | 960 | 960 | -8.9% | -9.9% | -9.8% | -8.5% | -9.7% | -9.7% | -8.5% | -9.7% | -9.9% | -8.8% | -9.8% | -9.8%
AerialCity | 960 | 960 | -3.3% | -1.8% | -1.4% | -3.5% | -2.1% | -1.7% | -3.4% | -2.1% | -1.7% | -3.2% | -1.8% | -1.4%
DrivingInCity | 960 | 960 | -4.5% | 4.4% | 4.1% | -3.9% | 4.0% | 3.6% | -3.7% | 4.0% | 3.6% | -4.4% | 4.4% | 4.1%
DrivingInCountry | 960 | 960 | -20.7% | -18.2% | -19.0% | -20.1% | -18.4% | -19.1% | -20.1% | -18.4% | -19.0% | -20.7% | -18.2% | -18.9%
Overall |  |  | -10.7% | -6.1% | -6.2% | -10.6% | -6.2% | -6.4% | -10.6% | -6.2% | -6.4% | -10.7% | -6.1% | -6.2%

## Slide 9: Results
Conversion-only results for padded ACP (width 4)
ACP conversion (with padding) |  |  | WS-PSNR (End to End) |  | 
 | Face W | Face H | Y | U | V
Trolley | 1184 | 1184 | 45.21 | 57.94 | 57.83
GasLamp | 1184 | 1184 | 50.09 | 58.76 | 57.62
Skateboarding_in_lot | 1184 | 1184 | 49.66 | 61.39 | 61.06
Chairlift | 1184 | 1184 | 49.91 | 59.50 | 59.57
KiteFlite | 1184 | 1184 | 46.32 | 57.66 | 57.65
Harbor | 1184 | 1184 | 48.91 | 59.09 | 58.06
PoleVault | 960 | 960 | 48.99 | 50.20 | 52.00
AerialCity | 960 | 960 | 46.85 | 55.11 | 54.41
DrivingInCity | 960 | 960 | 50.61 | 58.81 | 58.29
DrivingInCountry | 960 | 960 | 46.94 | 59.44 | 59.41
Overall |  |  | 48.35 | 57.79 | 57.59

## Slide 10: Conclusion
Padded ACP was proposed
Reported coding gain is 10.7% (e2e WS-PSNR) compared with ERP for RA conditions
Seam artifacts in rendered viewports are adequately reduced
Request to include padded ACP into the next version of 360Lib for further exploration of 360-degree video coding