## Slide 1: Comparisons between UWP, W66 and Planar, Angular mode 66 under the same coding conditions (JVET-G0081) K. Panusopone, S. Hong, Y. Yu, and L. Wang

## Slide 2: Unequal Weight Planar (UW-Planar)
Bottom-right position adjustment
  Maintain slopes for bottom row and right column
  Set bottom right to be weighted average of top-right and bottom-left
  Set bottom row to be weighted average of BR and BL
  Set right column to be weighted average of BR and TR
Unequal weight assignment for final predictor calculation
  Weight horizontal and vertical predictors by block dimensions
  P(x,y) = (verWeight*W*PV(x,y) + horWeight*H*PH(x,y) + Scal) >> (10 + log2H + log2W)
  verWeight = 512, when x=y=0
  = (x+1)*S[x+y-1], when x<y
  = 1024 – horWeight, otherwise
  horWeight = 1024 – verWeight, when x ≤ y
  = (y+1)*S[x+y-1], otherwise

## Slide 3: Weighted Angular Prediction
JVET angular predictor generation
  65 modes allowed in JVET
  Predictor from neighbor pixel on one side (either top of left)
Weighted angular prediction
  Aim to improve predictor accuracy
  Generate predictor using neighbor pixels on both sides (top and left)
  Modify mode 66 to use weighted angular prediction (no change to other modes)
  Each predictor pixel is determined by weighted average of corresponding top and left neighbors
  P[x,y] = {(((x+1)*R[x+y+2,-1])) + ((y+1)*(R[-1,x+y+2])) + (y+x+2)/2}/ (y+x+2))
  Division operations can be replaced by shift operations (as in UW-Planar)
  P[x,y] = (((horWeight*Recon[x+y+2,-1]) + (verWeight*Recon[-1,x+y+2]) + (y+x+2)/2) >> ShiftDenom)

## Slide 4: Mode 66 Modifications
Current JVET Weighted Angular Prediction

## Slide 5: Setting 1 Comparison
Based on HM-16.6-JEM-6.0-EE1-Test1-2and10
  Disable PDPC, MOD_PDPC, ARSS
  Set EE1_TEST1, EE1_TEST2, EE1_TEST2_1, EE1_TEST10, EE1_TEST10_1, COM16_C1046_PDPC_INTRA, and COM16_C983_RSAF macros to 0
 | Over JEM 6.0 all tools ON |  |  |  |  | Over EE1 Test 1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.60% | 0.12% | 0.40% | 53% | 98% | -0.79% | -0.87% | -0.88% | 101% | 100%
Class A2 | 0.86% | 0.91% | 0.72% | 55% | 99% | -0.62% | -0.28% | -0.52% | 101% | 100%
Class B | 0.63% | 0.54% | 0.61% | 53% | 99% | -0.56% | -0.56% | -0.57% | 101% | 100%
Class C | 0.67% | 0.71% | 0.60% | 54% | 99% | -0.26% | -0.22% | -0.20% | 100% | 100%
Class D | 0.17% | 0.06% | 0.07% | 54% | 100% | -0.23% | -0.13% | -0.08% | 100% | 99%
Class E | 0.74% | 0.78% | 0.87% | 55% | 98% | -0.50% | -0.41% | -0.25% | 100% | 100%
Overall (Ref) | 0.61% | 0.51% | 0.53% | 54% | 99% | -0.50% | -0.42% | -0.43% | 100% | 100%
Class F (optional) | 0.50% | 0.53% | 0.98% | 55% | 100% | -0.14% | 0.15% | 0.25% | 101% | 100%

## Slide 6: Setting 2 Comparison
Based on HM-16.6-JEM-6.0-EE1-Test1-2and10
  Disable PDPC, MOD_PDPC
  Set EE1_TEST1, EE1_TEST2, EE1_TEST2_1, EE1_TEST10, EE1_TEST10_1, and COM16_C1046_PDPC_INTRA macros to 0
 | Over JEM 6.0 all tools ON |  |  |  |  | Over JEM 6.0 no PDPC |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.16% | -0.25% | -0.08% | 82% | 100% | -0.88% | -0.93% | -0.96% | 99% | 100%
Class A2 | 0.10% | 0.15% | -0.04% | 84% | 100% | -0.78% | -0.42% | -0.62% | 99% | 101%
Class B | 0.13% | -0.06% | 0.00% | 82% | 100% | -0.65% | -0.67% | -0.69% | 99% | 100%
Class C | 0.03% | -0.09% | -0.13% | 84% | 100% | -0.39% | -0.31% | -0.20% | 99% | 100%
Class D | 0.04% | -0.20% | -0.18% | 83% | 100% | -0.34% | -0.20% | -0.20% | 99% | 100%
Class E | 0.18% | 0.05% | 0.05% | 83% | 100% | -0.60% | -0.38% | -0.48% | 98% | 101%
Overall (Ref) | 0.11% | -0.07% | -0.06% | 83% | 100% | -0.61% | -0.50% | -0.53% | 99% | 100%
Class F (optional) | -0.19% | -0.18% | -0.07% | 85% | 100% | -0.09% | 0.10% | -0.15% | 100% | 101%

## Slide 7: Setting 3 Comparison
Based on HM-16.6-JEM-6.0-EE1-Test3-7
  Enable MOD_PDPC, disable ARSS
  Set EE1_TEST3 macro to 1
  Modify to use PDPC with UWP, no boundary filter and no PDPC combination for W66
 | Over JEM 6.0 all tools ON |  |  |  |  | Over EE1 Test 3 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.55% | -0.46% | -0.33% | 78% | 101% | -0.22% | -0.28% | -0.25% | 100% | 101%
Class A2 | -0.29% | 0.45% | 0.26% | 79% | 101% | -0.16% | -0.03% | -0.18% | 99% | 101%
Class B | -0.19% | 0.20% | 0.22% | 78% | 101% | -0.12% | -0.09% | -0.07% | 100% | 101%
Class C | 0.00% | 0.49% | 0.46% | 78% | 98% | -0.06% | -0.11% | -0.06% | 100% | 98%
Class D | -0.32% | 0.12% | 0.13% | 79% | 95% | -0.03% | -0.11% | -0.20% | 100% | 96%
Class E | -0.27% | 0.27% | 0.25% | 79% | 100% | -0.05% | 0.03% | 0.06% | 100% | 100%
Overall (Ref) | -0.27% | 0.17% | 0.16% | 78% | 99% | -0.11% | -0.10% | -0.12% | 100% | 99%
Class F (optional) | -0.21% | -0.17% | 0.26% | 81% | 99% | 0.03% | 0.02% | 0.03% | 100% | 99%

## Slide 8: Setting 4 Comparison
Based on HM-16.6-JEM-6.0-EE1-Test1-2and10
  Enable PDPC, ARSS
  Set EE1_TEST1, EE1_TEST2, EE1_TEST2_1, EE1_TEST10, EE1_TEST10_1 macros to 0
 | Over JEM 6.0 all tools ON |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.35% | -0.40% | -0.29% | 97% | 101%
Class A2 | -0.30% | -0.05% | -0.25% | 98% | 101%
Class B | -0.21% | -0.18% | -0.08% | 98% | 101%
Class C | -0.14% | -0.08% | -0.11% | 99% | 100%
Class D | -0.11% | -0.16% | -0.09% | 99% | 100%
Class E | -0.26% | -0.17% | -0.19% | 100% | 101%
Overall (Ref) | -0.23% | -0.17% | -0.16% | 99% | 100%
Class F (optional) | -0.07% | -0.10% | 0.18% | 100% | 101%

## Slide 9: EE1 Test 7 vs Setting 5
 | EE1 Test 7 | Setting 5
Code base | HM-16.6-JEM-6.0-EE1-Test3-7 | 
Planar | JEM Planar | UWP
PDPC | On only for Planar | On only for UWP
PDPC flag | Not sent | 
Mode 66 | JEM Angular 66 | W66
Boundary filter | On | Off for W66
BD-rate vs JEM-6.0 | +0.47% | +0.34%
Encoding Time | 54% | 54%

## Slide 10: Setting 5 Comparison
Based on HM-16.6-JEM-6.0-EE1-Test3-7
  Enable MOD_PDPC, disable ARSS
  Set EE1_TEST7 macro to 1
  Modify to use PDPC with UWP, no boundary filter and no PDPC combination for W66
 | Over JEM 6.0 all tools ON |  |  |  |  | Over EE1 Test 7 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.38% | -0.17% | 0.08% | 53% | 100% | -0.25% | -0.46% | -0.38% | 63% | 99%
Class A2 | 0.42% | 0.52% | 0.31% | 55% | 100% | -0.21% | -0.16% | -0.31% | 61% | 99%
Class B | 0.38% | 0.26% | 0.36% | 53% | 100% | -0.14% | -0.29% | -0.28% | 60% | 99%
Class C | 0.39% | 0.51% | 0.51% | 54% | 100% | -0.07% | -0.02% | -0.01% | 66% | 99%
Class D | 0.10% | 0.06% | 0.20% | 54% | 100% | -0.03% | 0.02% | 0.06% | 61% | 98%
Class E | 0.36% | 0.51% | 0.54% | 55% | 100% | -0.07% | -0.04% | 0.01% | 62% | 99%
Overall (Ref) | 0.34% | 0.27% | 0.33% | 54% | 100% | -0.13% | -0.17% | -0.16% | 62% | 99%
Class F (optional) | 0.37% | 0.27% | 0.82% | 54% | 100% | 0.01% | 0.19% | 0.20% | 66% | 98%

## Slide 11: Results from 5 Settings
PDPC | ARSS | UWP and W66 gains | UWP and W66 gains, Class A | UWP and W66 |  | Planar and Angular 66 | 
 |  |  |  | AI Y BD-rate | Enc. Time | AI Y BD-rate | Enc. Time
Disable | Disable | -0.50% | -0.7% | +0.61% | 54% | +1.11% | 54%
Disable | Enable | -0.61% | -0.8% | +0.11% | 83% | +0.72% | 83%
MOD_PDPC | Disable | -0.11% | -0.2% | -0.27% | 78% | -0.16% | 78%
PDPC | Enable | -0.23% | -0.3% | -0.23% | 100% | 0.00% | 100%
Partial | Disable | -0.13% | -0.2% | +0.34% | 54% | +0.47% | 54%

## Slide 12: JVET Intra Prediction
3 steps in JEM intra prediction
  Neighbor smoothing (MDIS, ARSS, PDPC)
  Predictor generation (Planar, DC, Angular)
  Boundary smoothing (Boundary filter, PDPC)
Neighbor smoothing
Neighbor smoothing
Boundary smoothing
Boundary smoothing
Planar Prediction
Boundary smoothing

## Slide 13: UWP, W66 Role in Intra Prediction
UWP
  Impact predictor generation of Planar mode only
  Better estimate of right and bottom neighbor references
  Include boundary smoothing effect, no additional step needed (same as JEM Planar)
W66
  Impact predictor generation of Angular mode 66 only
  Use weighted average, instead of direct copy top right neighbor for predictor
  Include boundary smoothing effect, no additional step needed (unlike JEM Angular mode 66)

## Slide 14: Conclusions
UWP and W66 provides coding gain over Planar and Angular 66
  Coding gains, range from 0.1%-0.6%, from 5 settings
  Larger gains as resolution gets larger
  Coding gains, range from 0.2%-0.8%, for class A sequences
UWP and W66 works well with any combination of ARSS and PDPC
  UWP, W66 benefits come from unique feature helpful for large CU
  Independent of neighbor smoothing, boundary smoothing
Recommend adoption of UWP, W66 in JEM-7.0

## Slide 15
Thanks Huawei (G0122) for cross-checking
Questions?