## Slide 1: JVET-G0112 Arithmetic coding with context-dependent double-window adaptation response
Amir Said, Marta Karczewicz, Li Zhang, Vadim Seregin, Xin Zhao
Qualcomm Inc.

## Slide 2: Problem statement
In JEM-6, the binary arithmetic coder multi-parameter probability update method* is defined by
  Where P[k] is the probability estimate, scaled by 215
  All contexts apply the same update speed (window sizes 16 and 256)
  Each context has its own statistical properties
Better results with per-context adaptation speed
bin = 1 →
bin = 0 →
* VCEG-AZ05, Multi-parameter CABAC

## Slide 3: Proposal
Per-context initialization of probability adaptation speed
  Fixed table for initialization of a and b for each context
  Initialization of a and b depends on QP (whether QP<30)
  Shift parameters (a and b) are reinitialized together with context (per-slice)
  Value of a and b are limited as: 2 ≤ a ≤ b ≤ 9
bin = 1 →
bin = 0 →

## Slide 4: CTC simulation results – JEM-6.0
 | All Intra Main10 |  |  |  | 
 | Over JEM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.12% | -0.07% | -0.04% | 104% | 96%
Class A2 | -0.14% | -0.12% | -0.14% | 97% | 97%
Class B | -0.12% | -0.19% | -0.29% | 100% | 99%
Class C | -0.09% | -0.49% | -0.66% | 100% | 101%
Class D | -0.15% | -0.79% | -0.85% | 100% | 101%
Class E | -0.20% | -0.35% | -0.39% | 100% | 101%
Overall | -0.13% | -0.33% | -0.39% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over JEM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.20% | 0.80% | 0.69% | 99% | 99%
Class A2 | -0.34% | -0.06% | 0.04% | 99% | 99%
Class B | -0.38% | -0.02% | -0.25% | 100% | 97%
Class C | -0.27% | -0.02% | -0.24% | 100% | 99%
Class D | -0.41% | -0.28% | -0.85% | 100% | 97%
Class E |  |  |  |  | 
Overall (Ref) | -0.32% | 0.08% | -0.13% | 100% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over JEM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.15% | 1.30% | 0.68% | 102% | 101%
Class C | -0.10% | 0.72% | -0.10% | 99% | 101%
Class D | 0.01% | 1.40% | 1.10% | 100% | 100%
Class E | -0.17% | -0.12% | -0.24% | 100% | 98%
Overall (Ref) | -0.10% | 0.91% | 0.42% | 100% | 100%
 | Low delay P Main10 |  |  |  | 
 | Over JEM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.17% | 1.37% | 0.73% | 102% | 99%
Class C | -0.06% | 0.91% | 0.02% | 100% | 101%
Class D | -0.09% | 0.83% | 1.27% | 101% | 98%
Class E | -0.11% | -0.38% | 0.68% | 100% | 98%
Overall (Ref) | -0.11% | 0.79% | 0.68% | 101% | 99%