## Slide 1: Priority List Based Intra Mode Coding with 5 MPM (JVET-H0051) Y. Yu, L. Wang, K. Panusopone

## Slide 2: Intra Mode Coding in JEM7
67 intra modes: planar, DC and 65 angular modes;
Three mode sets: 6 MPM, 16 selected modes and 45 non-selected modes
Three steps to form 6 MPM in the JEM7:
From available spatial blocks plus planar and DC. The order is left, above, planar, DC, below-left, above-right and above-left.
Adding -1 or +1 to the angular modes that are already included in the MPM list.
Adding default modes {planar, DC, vertical, horizontal, mode 2, mode 34 }
The process can be stopped at any point once an unique list of 6MPM is generated.

## Slide 3: Intra Mode Coding in JEM7
The selected modes set: 16 modes evenly sub-sampling the 61 non-MPM modes with interval 4.
Non-selected modes: the remaining 45 modes.
Note: the first 19 and the subsequent 26 modes in the non-selected modes set are coded with 7 bins and 8 bins, respectively.
Intra prediction modes | MPM flag | Selected flag | Bin string
MPM modes (6) | 1 |  | 0
 |  |  | 10
 |  |  | 110
 |  |  | 1110
 |  |  | 11110
 |  |  | 11111
Selected modes (16) | 0 | 1 | 4 bins fixed length code
Non-selected modes (45) | 0 | 0 | 5-6 bins truncated binary code

## Slide 4: 5 MPM
The last two entries of MPM list require the same number (six) bins with 16 selected modes.
Propose five MPM, 16 selected modes and 46 non-selected modes.
Intra prediction modes | MPM flag | Selected flag | Bin string
MPM modes (5) | 1 |  | 0
 |  |  | 10
 |  |  | 110
 |  |  | 1110
 |  |  | 1111
Selected modes (16) | 0 | 1 | 4 bins fixed length code
Non-selected modes (46) | 0 | 0 | 5-6 bins truncated binary code

## Slide 5: Priority List Based Intra Mode Coding
MPM generation is kind of the process which generates candidates according to assumed priority.
Propose to continue this process till we find 5 MPM, 16 selected modes and 18 non-selected modes (the first part of non-selected modes).
DC mode may be put after above-left like JVET-G0060 suggested.

## Slide 6: Simulation Results
Implemented on the top of JEM 7. Test is under CTC.
Table 1. Priority list based with five MPMs
 | All Intra |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.1% | -0.1% | -0.1% | 101% | 100%
Class A2 | -0.1% | -0.1% | -0.1% | 101% | 100%
Class B | -0.1% | -0.1% | -0.1% | 100% | 100%
Class C | -0.1% | -0.1% | -0.1% | 98% | 100%
Class D | -0.2% | -0.1% | -0.1% | 98% | 99%
Class E | -0.3% | -0.4% | -0.2% | 98% | 100%
Overall | -0.1% | -0.1% | -0.1% | 99% | 100%
Class F (optional) | -0.1% | 0.3% | -0.2% | 99% | 100%

## Slide 7: Simulation Results
Implemented on the top of JEM 7. Test is under CTC.
Table 2. Priority list based with five MPMs and DC after above-left block
 | All Intra |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.1% | -0.1% | -0.1% | 100% | 99%
Class A2 | -0.2% | -0.2% | -0.2% | 99% | 100%
Class B | -0.1% | -0.1% | -0.1% | 99% | 100%
Class C | -0.1% | -0.1% | 0.0% | 97% | 100%
Class D | -0.1% | -0.1% | -0.1% | 98% | 100%
Class E | -0.4% | -0.3% | -0.3% | 97% | 100%
Overall | -0.2% | -0.1% | -0.1% | 98% | 100%
Class F (optional) | -0.1% | 0.2% | 0.0% | 98% | 100%

## Slide 8: Conclusions
Propose five MPM, 16 selected modes and 46 non-selected modes for intra mode coding.
Propose to continue MPM generation process so that we have a priority list. Map this priority list to 5 MPM, 16 selected modes and 18 non-selected modes.
Simulation results show that there are 0.1% and 0.2% gain for priority list based intra mode coding with 5MPM and priority list based intra mode coding with 5MPM plus putting DC mode after above-left, respectively with a little bit faster encoding time and no decoding time change.

## Slide 9
Thanks to Sharp for cross-checking (JVET-H0075)
Questions?