## Slide 1: Chroma Artifact Reduction by New Sample Adaptive Offset method for Chroma
Eiichi Sasaki, Jun Ono

## Slide 2: Chroma Artifact Problem
Chroma distortion in colorless area significantly degrades subjective quality.
  In YUV format, chroma pixel values of the colorless area are median of gamut.
  Even if the distortion is not large, subjective quality is affected.
  HDR/WCG content are affected more strongly than SDR contents

## Slide 3: Reduce Chroma Artifacts by chroma qp offset
JCTVC-Z1017 and JVET-G0084 reported appropriate chroma qp offset can reduce Chroma Artifact.
  Viewing session was held in previous meeting to check Chroma Artifact and improvement of subjective quality by using chroma qp offset method.
In the snow field, cyan Chroma Artifact appears.

## Slide 4: Motivation of proposal
However, using chroma qp offset must degrade the luma quality relatively.
To reduce Chroma Artifacts without degrading luma, a new Sample Adaptive Offset (SAO) method for chroma is proposed in this contribution
 | QPISlice | EncR | DecR | bitrate-ratio (%) |  | Y | U | V
HLG1 | 31 | 1.00 | 1.01 | 2.41 |  | 3.49% | -66.09% | -71.27%
(Flyng Birds) | 34 | 1.01 | 1.00 | 2.81 |  |  |  | 
 | 38 | 0.97 | 0.96 | 3.81 |  |  |  | 
 | 42 | 0.97 | 0.93 | 5.89 |  |  |  | 

## Slide 5: Chroma Artifact Reduction SAO (CAR SAO)
1<<(bitdepth – 1)
Proposed new SAO method (CAR SAO) is based on Band Offset and modified to make it more suitable to reduce Chroma Artifact
  CAR SAO’s band position is fixed around median of chroma gamut and the band is continuous 6 classes
  Length of each classes is (1 << bit depth) >> 7 (in 10bit case, 1 class length is 8)
0
1<<bitdepth
BO classes
CAR SAO classes

## Slide 6: Chroma Artifact Reduction SAO (CAR SAO)
  Signaling and adding only 3 offsets: Count up numbers of pixels that belong to each class and select 3 classes in descending order of numbers of pixels.
  Example:
  In this case, offsets in class index 0, 1 and 3 are signaled and added
class index | range of class (in 10bit) | number of pixels in CTB
0 | 488 - 495 | 2327
1 | 496 - 503 | 1134
2 | 504 - 511 | 134
3 | 512 - 519 | 158
4 | 520 - 527 | 0
5 | 528 - 535 | 0

## Slide 7: Modify RDCost calculation of CAR SAO
According to subjective evaluation, proposed CAR SAO can reduce Chroma Artifact.
  However, for HDR contents, it’s seems CAR SAO should be more strongly applied in blight area to more improve subjective quality.
  We have modified RDCost calculation for SAO type decision as below,

## Slide 8: Simulation results
Test RA SDR CTC and 3 HLG sequences with Chroma Artifact
Modify HM-16.6-JEM-7.1
  Test1: Apply CAR SAO and remove other SAO TYPE(BO, EO) in chroma
  Test2: Test1 and modify of RDCost calculation
  Thank Sharp and Hikvision for the cross-checking
 | Test1 |  |  |  | 
 | BDRate |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.49% | 0.12% | 100% | 100%
Class C | -0.02% | 0.95% | 1.33% | 100% | 100%
Class D | 0.00% | 0.73% | 0.40% | 100% | 100%
Class E |  |  |  |  | 
HLG-1 | 0.06% | -0.36% | -2.64% | 100% | 109%
HLG-4 | -0.01% | -1.77% | -16.62% | 99% | 100%
HLG-5 | 0.02% | -11.75% | -36.54% | 96% | 92%
 | Test2 |  |  |  | 
 | BDRate |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C |  |  |  |  | 
Class D |  |  |  |  | 
Class E |  |  |  |  | 
HLG-1 | 0.05% | -1.05% | -4.73% | 101% | 108%
HLG-4 | -0.02% | -2.16% | -19.13% | 100% | 100%
HLG-5 | 0.03% | -13.92% | -41.74% | 98% | 98%

## Slide 9: Simulation results
HLG-1
  Chroma Artifact around snow field is reduced
Reference
Test2

## Slide 10: Simulation results
HLG-4
  Chroma Artifact around water is reduced
Reference
Test2

## Slide 11: Simulation results
HLG-5
  Chroma Artifact around water is reduced
Reference
Test2

## Slide 12: Conclusion
Proposed CAR SAO provides subjective quality improvement by reducing Chroma Artifact.
Continuously investigate CAR SAO, and Chroma Artifact problem
To investigate Chroma Artifact, continuously evaluate the contents show Chroma Artifact like HLG1, HLG4 and HLG5