## Slide 1: [JVET-I0023] Methods of padding inactive regions for segmented sphere projection (SSP)
Yong-Uk Yoon, Do-Hyeon Park, Jae-Gon Kim (KAU),
Yongjo Ahn, Donggyu Sim (Digital Insights)
@ 9th JVET meeting, Gwangju, KR

## Slide 2: Backgrounds
Segmented sphere projection (SSP)
  Three segments
    One equatorial segment
    Two pole segments
  A reconstructed viewport frame has visual artifacts along the latitude of ±45°
    The corners of the two pole segments are inactive samples and filled with the default gray color
    The inactive areas projected in circles cause the visual artifact and the reduction of coding efficiency

## Slide 3: Backgrounds
The problem can be solved if the inactive area is filled with pixels having high correlation with the active area
In JVET-G0097, a padding method for inactive areas was proposed
  However, since there are still inactive regions, further improvement may be possible
The north and south pole segments
The south pole and equatorial segments

## Slide 4: Proposed methods
Motivation
  Assume that if the inactive regions are filled with adjacent pixels
   Keep the high correlation between active regions and inactive regions
The inactive regions are filled with the pixels obtained by two different ways
  Test 1: the average of the pixels at the top and bottom parts of the corresponding rectangular faces
  Test 2: the average of the pixels at the boundaries of the corresponding circle faces
Test 2:
Test 1:

## Slide 5: Experimental results
Test conditions
  JVET common test conditions
  Reference software: HM-16.16 and 360Lib-5.0
  Encoding configuration: Random access
  Test sequences: JVET common test sequences
Anchor: PERP |  | E2E S-PSNR |  |  | E2E WS-PSNR |  |  | CL WS-PSNR |  |  | CL S-PSNR |  | 
 |  | Y | U | V | Y | U | V | Y | U | V | Y | U | V
SSP | 8K | -11.8% | -6.4% | -6.6% | -11.9% | -6.4% | -6.6% | -4.0% | -6.8% | -7.0% | -3.9% | -6.7% | -6.8%
 | 6K | -7.3% | -4.0% | -5.3% | -7.3% | -4.1% | -5.3% | -5.8% | -4.5% | -5.7% | -5.8% | -4.4% | -5.6%
 | 4K | -7.6% | -6.8% | -7.2% | -7.6% | -6.9% | -7.2% | 2.6% | 5.6% | 5.8% | 2.7% | 5.7% | 5.8%
 | Overall | -9.6% | -5.7% | -6.3% | -9.7% | -5.7% | -6.3% | -3.5% | -4.0% | -4.4% | -3.4% | -3.9% | -4.3%
Test 1 | 8K | -12.1% | -6.9% | -6.8% | -12.1% | -6.9% | -6.8% | -4.2% | -7.4% | -7.2% | -4.2% | -7.2% | -7.1%
 | 6K | -7.2% | -4.2% | -5.5% | -7.2% | -4.2% | -5.5% | -5.7% | -4.7% | -6.0% | -5.7% | -4.6% | -5.9%
 | 4K | -7.8% | -9.1% | -8.5% | -7.8% | -9.1% | -8.5% | -3.1% | -6.3% | -6.7% | -2.9% | -6.3% | -6.7%
 | Overall | -9.8% | -6.3% | -6.7% | -9.8% | -6.4% | -6.7% | -4.5% | -6.3% | -6.7% | -4.5% | -6.2% | -6.6%
Test 2 | 8K | -12.1% | -6.8% | -6.9% | -12.1% | -6.8% | -6.9% | -4.2% | -7.3% | -7.3% | -4.2% | -7.1% | -7.1%
 | 6K | -7.3% | -4.1% | -5.6% | -7.3% | -4.2% | -5.7% | -5.8% | -4.6% | -6.1% | -5.8% | -4.6% | -6.0%
 | 4K | -7.5% | -8.8% | -8.3% | -7.6% | -8.8% | -8.4% | -2.9% | -6.1% | -6.6% | -2.7% | -6.0% | -6.5%
 | Overall | -9.7% | -6.2% | -6.7% | -9.8% | -6.3% | -6.7% | -4.5% | -6.2% | -6.8% | -4.4% | -6.1% | -6.7%
Anchor: SSP | E2E S-PSNR |  |  | E2E WS-PSNR |  |  | CL S-PSNR |  |  | CL WS-PSNR |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Test 1 | -0.1% | -0.7% | -0.4% | -0.1% | -0.7% | -0.5% | -1.1% | -2.4% | -2.4% | -1.1% | -2.4% | -2.4%
Test 2 | 0.0% | -0.6% | -0.5% | 0.0% | -0.6% | -0.5% | -1.1% | -2.3% | -2.4% | -1.1% | -2.3% | -2.4%

## Slide 6: Experimental results
Test conditions
  JVET common test conditions
  Reference software: HM-16.16 and 360Lib-5.0
  Encoding configuration: Random access
  Test sequences: Five CfP test sequences
Anchor: PERP |  | E2E S-PSNR |  |  | E2E WS-PSNR |  |  | CL WS-PSNR |  |  | CL S-PSNR |  | 
 |  | Y | U | V | Y | U | V | Y | U | V | Y | U | V
SSP | 8K | -10.9% | -4.7% | -6.6% | -12.0% | -4.7% | -6.5% | -3.5% | -5.2% | -7.0% | -3.5% | -5.0% | -6.8%
 | 6K | -7.0% | -2.8% | -5.2% | -7.0% | -2.9% | -5.3% | -8.1% | -3.7% | -5.9% | -8.1% | -3.6% | -5.8%
 | Overall | -10.9% | -4.3% | -6.3% | -11.0% | -4.3% | -6.3% | -4.5% | -4.9% | -6.8% | -4.4% | -4.7% | -6.6%
Test 1 | 8K | -12.1% | -5.2% | -6.8% | -12.2% | -5.2% | -6.8% | -3.8% | -5.7% | -7.3% | -3.8% | -5.5% | -7.1%
 | 6K | -6.9% | -2.8% | -5.4% | -6.9% | -2.9% | -5.5% | -8.0% | -3.7% | -6.2% | -8.0% | -3.6% | -6.1%
 | Overall | -11.1% | -4.7% | -6.6% | -11.2% | -4.7% | -6.6% | -4.7% | -5.3% | -7.1% | -4.7% | -5.1% | -6.9%
Test 2 | 8K | -12.1% | -5.1% | -6.9% | -12.2% | -5.1% | -6.9% | -3.8% | -5.6% | -7.4% | -3.8% | -5.4% | -7.2%
 | 6K | -7.0% | -2.9% | -5.6% | -7.0% | -3.0% | -5.7% | -8.1% | -3.8% | -6.4% | -8.1% | -3.7% | -6.3%
 | Overall | -11.1% | -4.6% | -6.6% | -11.2% | -4.6% | -6.6% | -4.7% | -5.2% | -7.2% | -4.7% | -5.0% | -7.0%
Anchor: SSP | E2E S-PSNR |  |  | E2E WS-PSNR |  |  | CL S-PSNR |  |  | CL WS-PSNR |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Test 1 | -0.3% | -0.4% | -0.3% | -0.3% | -0.4% | -0.3% | -0.3% | -0.4% | -0.3% | -0.3% | -0.4% | -0.3%
Test 2 | -0.3% | -0.3% | -0.4% | -0.3% | -0.3% | -0.4% | -0.3% | -0.4% | -0.3% | -0.3% | -0.4% | -0.3%

## Slide 7: Experimental results – Subjective quality
  Viewport size: 1816x1816
  Static viewport 1 centered at vertex 2: (yaw, pitch) = (90°, -45°)
Original SSP
Current SSP
(JVET-G0097)
Proposed (Test 2)

## Slide 8: Conclusion
In this contribution, methods of padding inactive regions are proposed to improve coding efficiency and reduce visual artifact in SSP
The experimental results show the average 0.3% BD-rate reduction in terms of end-to-end WS-PSNR
In addition, the visual artifact can be reduced by padding inactive regions

## Slide 9: End of presentation
Q&A