## Slide 1: [JVET-I0024] Efficient frame packing method for Icosahedral Projection (ISP)
Hyun-Ho Kim, Yong-Uk Yoon, Do-Hyeon Park, Jae-Gon Kim (KAU),
Yongjo Ahn, Donggyu Sim (Digital Insights)
@ 9th JVET meeting, Gwangju, KR

## Slide 2: Backgrounds
Icosahedral projection (ISP)
  ISP segments the sphere into 20 triangles
  Inactive-region and discontinuity between triangles reduce coding efficiency
Compact ISP (CISP)
  All 20 triangle faces are compacted to the rectangular frame
  Contains 8 discontinuous edges
Non-compact ISP
Compact ISP
(a) Initial version
(b) Current version (JVET-D0028)

## Slide 3: Backgrounds
[JVET-G0156] AhG8: Efficient frame packing method for Icosahedral projection (ISP)
  The main idea of this proposal is to keep the similar region
  Not to interleave the content of poles and equator

## Slide 4: Proposed method
Motivation
  In 360 video, the equator part contains major information
    Conventional frame packing methods for ISP divide the equator part into two parts
    It has a potential visual artifact in the equator part
  It can reduce visual artifacts by removing discontinuous edges in the equator part
Conventional frame packing methods for ISP

## Slide 5: Proposed method
In the proposed method, a frame consists of three rectangular regions
  Equator region:
    The equator triangles are rearranged in a line on the bottom row
  Pole regions:
    Diagonal discontinuous edges place only in the pole regions
South pole
North pole
Equator region
Proposed frame packing

## Slide 6: Proposed method
Padding size
  To prevent possible visual artifacts caused by discontinuous edges
  Copy padding: Top of the north pole, sides of the equator
  Bilinear padding: others
The proposed method can reduce the input image size about 2.4% compared to CISP

## Slide 7: Comparison of discontinuities
The proposed method contains an additional vertical discontinuity compared to CISP
However, the proposed method can remove discontinuities of the equator region
CSIP
JVET-G0156
Proposed
Discontinuities | CISP | JVET-G0156 | Proposed
Diagonal (D) | 4 | 4 | 4
Horizontal (H) | 4 | 3 | 4
Vertical (V) | - | 4 | 1
Total | 8 | 11 | 9

## Slide 8: Experimental results
Test condition
  JVET common test conditions
  Reference software: HM-16.16 and 360Lib-5.0
  Encoding configuration: Random access
  Test sequences: JVET common test sequences
The proposed method can achieve 0.6% BD-rate gain in terms of end-to-end performance (E2E WS-PSNR)
Anchor: PERP |  | E2E S-PSNR Y | E2E WS-PSNR Y | CL WS-PSNR Y | CL S-PSNR Y
CISP | 8K | -7.4% | -7.5% | 0.8% | 0.6%
 | 6K | 2.5% | 2.4% | 4.7% | 4.4%
 | 4K | -1.7% | -1.8% | 1.8% | 1.4%
 | Overall | -3.1% | -3.3% | 2.3% | 2.0%
Proposed | 8K | -8.4% | -3.5% | 0.2% | -0.7%
 | 6K | 3.3% | 3.2% | 5.8% | 5.5%
 | 4K | -3.4% | -3.5% | 0.2% | -0.7%
 | Overall | -3.7% | -3.8% | 2.1% | 1.5%
Anchor: CISP |  | E2E S-PSNR Y | E2E WS-PSNR Y | CL WS-PSNR Y | CL S-PSNR Y
Proposed | 8K | -1.0% | -1.0% | -0.5% | -1.1%
 | 6K | 0.6% | 0.6% | 1.0% | 1.0%
 | 4K | -1.8% | -1.7% | -1.6% | -2.1%
 | Overall | -0.6% | -0.6% | -0.2% | -0.6%

## Slide 9: Experimental results
Test condition
  JVET common test conditions
  Reference software: HM-16.16 and 360Lib-5.0
  Encoding configuration: Random access
  Test sequences: Five CfP test sequences
The proposed method can achieve 0.6% BD-rate gain in terms of end-to-end performance (E2E WS-PSNR)
Anchor: CISP |  | E2E SPSNR-NN Y | E2E WS-PSNR Y | C-WS-PSNR Y | C-S-PSNR-NN Y
8K | Trolley | -1.2% | -1.2% | -1.4% | -1.9%
 | Chairlift | -1.7% | -1.7% | -1.3% | -1.3%
 | KiteFlite | -0.4% | -0.5% | -0.8% | -2.1%
 | Harbor | -0.9% | -0.8% | 0.6% | -0.5%
6K | Balboa | 1.0% | 1.0% | 1.9% | 1.3%
 | All | -0.6% | -0.6% | -0.2% | -0.9%

## Slide 10: Conclusion
The proposed method rearranges equator triangles in a line on the bottom row
  It is possible to remove discontinuities on the equator part
  Coding gain: 0.6% BD-rate gain in terms of end-to-end performance

## Slide 11: End of presentation
Q&A