## Slide 1: JVET-J0024 and JVET-J0025 Description of 360° video coding technology proposal by Samsung, Huawei, GoPro, and HiSilicon
April 13, 2018

## Slide 2: Rotated Sphere Projection (RSP)
ERP image
Rotated ERP image
Crop
RSP image
Crop
RSP image with circular padding
Goal: Design 360° video compression system without any low-level tools
Response is based on Rotated Sphere Projection (RSP)
Two perfectly continuous faces, with a stitch line similar to Tennis ball
Same math as ERP – one face cropped from ERP, other cropped from rotated ERP
RSP to ERP conversion is simple and avoids interpolation for half of sphere

## Slide 3: Padding
W+16
H
Increase picture width by 16 pixels, adding 8 pixels padding on each side
Step Padding:
  Align circular discontinuities with 8x8 CU boundaries
  Presented in JVET-H0056 where similar technique showed 0.7% gain
Compact RSP with step padding
Zoomed step padding

## Slide 4: Rotation
  Since RSP is constructed from rotating ERP, use rotation as a coding tool.
  Downsize the RSP image and search along yaw space at 10° angles, from 0° to 350°
  Compute gradient magnitudes and angles for each of these 36 RSP image
  Find the image with maximum number of vertical and horizontal gradients.
  Further refinement to 1° is possible by searching around best 10° angle.
  Computed on only first frame of sequence
Input image
36 RSP image
Generation
(Lower Resolution)
Compute
gradient angles
Find angle
with maximum
vertical and
horizontal gradients

## Slide 5: Rotation
RSP image without rotation
RSP image with best rotation angle
RSP edge map without rotation
RSP edge map with best rotation angle

## Slide 6: Rotation - Results
Correlation between gradients and BD-rate
Rotation angles
Sequence | Yaw | Pitch | Roll
Balboa | 90 | 0 | 0
ChairliftRide | 0 | 0 | 0
KiteFlite | 0 | 0 | 0
Harbor | 310 | 0 | 0
Trolley | 10 | 0 | 0

## Slide 7: Rotation - Results
360lib-5.0-HM16.16 using CTC conditions.
Average BD-rate gain of 1.53% for Luma component.
Maximum Luma gain of 4.34% for Balboa.
Sequence | E2E WS PSNR Anchor |  |  | E2E WS PSNR - Rotation |  | 
 | Y | U | V | Y | U | V
Balboa | −4.93% | −0.89% | −2.49% | −9.27% | −3.98% | −5.77%
ChairliftRide | −24.16% | −20.21% | −21.27% | −24.16% | −20.21% | −21.27%
KiteFlite | −6.13% | −8.41% | −10.06% | −6.13% | −8.41% | −10.06%
Harbor | −4.35% | −6.64% | −5.64% | −7.31% | −7.71% | −8.46%
Trolley | −4.99% | −1.42% | −7.54% | −5.34% | −1.35% | −7.23%
Average | −8.91% | −7.51% | −9.51% | −10.44% | −8.33% | −10.56 %

## Slide 8: Colored Filling
Section with inactive region
Non filled inactive region
Color filled inactive region
Look at active/inactive area boundary pixels and fill inactive region with certain value
Median value used for filling Luma, while mode is used for filling Chroma
Average 0.2% coding efficiency for Luma
Improved subjective quality

## Slide 9: Colored Filling Example
Balboa sequence with inactive region filling

## Slide 10: Inactive Region Filling - Results
BD-rate gains
360lib-5.0-HM16.16 using CTC conditions.
Average BD-rate gain of 0.22% for Luma component.
Maximum Luma gain of 0.47% for ChairliftRide.
Sequence | E2E WS PSNR Anchor |  |  | E2E WS PSNR - Filling |  | 
 | Y | U | V | Y | U | V
Balboa | −4.93% | −0.89% | −2.49% | −5.23% | −1.03% | −3.10%
ChairliftRide | −24.16% | −20.21% | −21.27% | −24.63% | −20.54% | −21.34%
KiteFlite | −6.13% | −8.41% | −10.06% | −6.22% | −8.25% | −10.76%
Harbor | −4.35% | −6.64% | −5.64% | −4.56% | −6.62% | −5.67%
Trolley | −4.99% | −1.42% | −7.54% | −5.03% | −1.35% | −7.68%
Average | −8.91% | −7.51% | −9.51% | −9.13% | −7.56% | −9.71%

## Slide 11: Disable Deblocking on Seam Boundary
Disable deblocking at seam boundary to improve subjective quality.
Signaled as 1-bit flag (can also be implemented with slices or tiles)

## Slide 12: Deblocking - Results
With Deblocking (Harbor)
No Deblocking (Harbor)

## Slide 13: Blending
8 pixels are modified along horizontal seam areas only
Weighted blending of pixels by modifying pixels on the horizontal seam:
0.2% loss in objective numbers but subjective improvement
Horizontal Seam

## Slide 14: Blending Results
Without blending (Balboa)
With blending (Balboa)

## Slide 15: Adjustment
360 images generally have more details in equator than in poles
Stretch equator and shrink poles by the similar proportion
Useful in situations where poles do not have much content
ERP to RSP Conversion
RSP to ERP Conversion
W is a function of concentration of variance/texture in image
Average BD-rate gain of 0.20% for Luma component
Can be turned off (in favor of having simple ERP math)
* No adjustment is applied
when is zero

## Slide 16: RSP before adjustment

## Slide 17: RSP after adjustment

## Slide 18: CFP Response Results (J0024)
 | Over HM |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V)
Balboa | -43.1% | -52.3% | -55.7%
Chairlift | -45.0% | -63.4% | -56.1%
KiteFlite | -22.3% | -49.8% | -54.2%
Harbor | -27.9% | -54.8% | -56.4%
Trolley | -21.0% | -40.2% | -44.8%
Average | -31.8% | -52.1% | -53.4%
Over JEM |  | 
BD-rate(Y) | BD-rate(U) | BD-rate(V)
-11.8% | -12.3% | -10.2%
-20.7% | -26.7% | -18.8%
-5.8% | -1.2% | -1.0%
-9.4% | -14.0% | -16.2%
-6.0% | -3.4% | -7.2%
-10.7% | -11.5% | -10.7%
Face Size: 1280x1280

## Slide 19: CFP Response Results (J0025)
 | Over HM |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V)
Balboa | -45.1% | -54.8% | -58.0%
Chairlift | -46.0% | -64.2% | -57.3%
KiteFlite | -23.6% | -50.4% | -55.1%
Harbor | -29.1% | -55.4% | -57.1%
Trolley | -21.5% | -41.4% | -46.0%
Average | -33.1% | -53.2% | -54.7%
Over JEM |  | 
BD-rate(Y) | BD-rate(U) | BD-rate(V)
-15.1% | -17.4% | -15.3%
-22.2% | -28.9% | -21.9%
-7.4% | -2.5% | -3.3%
-11.1% | -15.1% | -17.5%
-6.6% | -5.7% | -9.3%
-12.5% | -13.9% | -13.5%
Face Size: 1280x1280

## Slide 20: Summary
  An efficient projection format helps in improved coding performance for 360° video
  Rotated Sphere Projection (RSP) was used in CfP response
  Other algorithms developed on top of RSP
    Rotation
    Colored Filling
    Disabled Deblocking filter on RSP seam
    Blending seam boundaries
    Adjustment
  All algorithms are agnostic of coding engine, i.e. are only pre/post processing
  Propose to include in Test Model

## Slide 21
Thank you