## Slide 1: SDR and HDR video coding technology proposal by NHK and SHARP
JVET-J0027
Contact: Shunsuke Iwamura (iwamura.s-gc@nhk.or.jp)
Tomohiro Ikai (ikai.tomohiro@sharp.co.jp)

## Slide 2: Introduction
Additional coding tools in combination with J0026 coding tools are proposed as an intermediate complexity configuration.
Flexible Rectangular Partitioning Structure
Picture Boundary Partitioning
Switchable separate and shared trees for intra coding
Bitdepth adjusted cost function
chroma DM bin
bug fix
Bi-pred optimized TS
MVPlanar
PDIntrafilter
Luma-adaptive deblocking filter
Block structure
Prediction/Transform
Loop filter
Others
coeff/binarization
J0027-only tools
*
* enabled in I-slice only
Implicit luma base coefficient scaling in HDR
Implicit luma base coefficient scaling in HDR
Sharp’s
tools

## Slide 3
Summary of results (Submitted software)
HDR
 |  |  | Y psnr | U psnr | V psnr | Enc | Dec
vsHM | CS1 | SDR-A | -36.8% | -44.0% | -43.9% | 1693% | 1506%
 |  | SDR-B | -32.3% | -48.0% | -48.8% | 2110% | 1764%
 | CS2 | SDR-B | -26.2% | -43.7% | -44.3% | 1293% | 667%
vsJEM | CS1 | SDR-A | -1.8% | -3.3% | -3.4% | 212% | 198%
 |  | SDR-B | -2.5% | -7.8% | -7.9% | 265% | 231%
 | CS2 | SDR-B | -2.2% | -2.0% | -3.8% | 161% | 100%
 |  |  | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV | Enc | Dec
vsHM | CS1 | HDR-A | -58.4% | -32.3% | -29.7% | -68.2% | -70.9% | 1147% | 1775%
 |  | HDR-B | -44.9% | -31.9% | -31.1% | -61.0% | -60.4% | 2330% | 1698%
vsJEM | CS1 | HDR-A | -9.5% | -2.5% | -2.2% | -11.7% | -15.2% | 144% | 233%
 |  | HDR-B | -13.9% | -5.4% | -4.4% | -18.1% | -24.8% | 292% | 223%
SDR
This proposal achieves:
34.6% BD-rate gain with 18.9x encoding time and 16.3x decoding time over HM for SDR-CS1
30.6% BD-rate gain with 17.9x encoding time and 17.3x decoding time over HM for HDR

## Slide 4: Overview of J0027-only tools
Paritition
Transform
Quant.
Entropy coding
Dequant.
Inv. transform
In-loop filter
Inter prediction
Intra prediction
Bi-pred optimized transform skip
Interpolated motion compensation prediction (MVPlanar)
Luma-adaptive deblocking filter
Position dependent intra interpolation filter
Chroma DM binarization bug-fix

## Slide 5
Reference0
Reference1
Prediction
(Weighted average of both ref 0 and 1)
-
Current CU
Residual
Drawback of the convectional TS
Residual
When the residual has high ampli- tude in the bottom-right corner.  the amount of generated bits becomes higher
(e.g. lastposition, sig_coeff_flag..)
Reconstructed residual
量子化
Residual coding
+
Reconstruct
Difference of references
Derive the estimated energy distribution by taking difference between the reference blocks used for bi-prediction
Proposal
Estimate energy distribution of the residual and reorder it in the descending order of the estimated energy
Residual coding
Residual
Reordered residual
Reconstructed reordered residual
Reconstructed residual
The amplitude of the bottom-right corner becomes lower
Bi-pred optimized transform skip

## Slide 6
Interpolated MC prediction (MVPlanar)
Sub-block MVs are derived by interpolating MVs of all the neighboring blocks.
The interpolation is carried out in a similar way as intra planar prediction except that x and y values of each sub-MV are calculated separately
If needed, substitution process of neighboring MV is invoked also in a similar way as intra reference sample substitution.
intra

## Slide 7
Interpolated MC prediction (MVPlanar)
intra
Signaling for this mode:
- MVPlanar_flag
specifies whether MVPlanar is applied
- Inter_pred_idc
specifies whether L0, L1 or bi-pred is applied
- ref_idx
specifies an index into a reference list
` |  | Y | U | V | EncT | DecT
CS1 | SDR-A | 0.4% | 0.3% | 0.4% | 84% | 106%
 | SDR-B | 0.2% | 0.2% | 0.2% | 119% | 97%
CS2 | SDR-B | 0.2% | 0.4% | 0.5% | 97% | 96%
CS1 | HDR-A | 0.2% | 0.1% | 0.1% | 81% | 108%
 | HDR-B | 0.3% | 0.5% | 0.7% | 114% | 101%
Experimental results of Tool-off test

## Slide 8: Position dependent intra interpolation filter
This proposal alternatively applies the interpolation filter according to the position of the prediction samples.
For the first N lines, cubic filter is applied, and thereafter Gaussian filter is applied. (N is set equal to 16 in the submitted software)
Note: In JEM, two types of intra interpolation filters are alternatively applied only according to the block size of the current CU. Same interpolation filter is used to the same prediction block.
Interpolate by the Gaussian filter
Interpolate by the cubit filter

## Slide 9: Luma-adaptive deblocking filter
Quantization error in the video signal domain would be enhanced by OETF
Blocking artifact is more visible at bright area, especially for HDR contents, this artifact becomes salient due to its strong non-linearity.
This proposal controls filter strength based on the averaged luma level of reconstructed samples at the deblocking filter
Averaged Luma level

## Slide 10
transfer_characteristics == 16 (HLG format) |  | transfer_characteristics == 18 (PQ format) |  | Otherwise (conventional SDR format) | 
Conditions | qpOffset | Conditions | qpOffset | Conditions | qpOffset
LL <= 0.84 | 0 | LL <= 0.8 | 0 | LL <= 0.875 | 0
0.84 < LL <= 0.91 | 1 | 0.8 < LL <= 0.9 | 1 | 0.875 < LL | 1
0.91 < LL <= 0.99 | 2 | 0.9 < LL | 2 |  | 
0.99 < LL | 3 |  |  |  | 
Luma-adaptive deblocking filter
In HEVC, deblocking filter strength is controlled by the average of QP values of current and neighboring CU
qPL = ( ( QPQ + QPP +1 ) >> 1 )
In this proposal, additional QP offset based on averaged luma level is introduced
qPL = ( ( QPQ + QPP +1 ) >> 1 ) + qpOffset
Stronger deblocking filter is applied to the bright area.

## Slide 11: Chroma DM binarization bug fix
(the same as reported in JVET-H0071)
In the pruning process of chroma DM mode, one redundant CABAC-bit is signaled in JEM
Bug

## Slide 12: Chroma DM binarization bug fix
(the same as reported in JVET-H0071)
 | Over HM-16.6-JEM-7.0 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.0% | 0.0% | 0.0% | 99% | 98%
Class A2 | 0.0% | -0.1% | -0.1% | 100% | 99%
Class B | 0.0% | -0.1% | -0.1% | 100% | 101%
Class C | 0.0% | 0.0% | 0.0% | 100% | 97%
Class D | 0.0% | 0.0% | 0.0% | 99% | 100%
Class E | 0.0% | -0.3% | -0.1% | 100% | 99%
Overall | 0.0% | -0.1% | 0.0% | 100% | 99%
Class F | 0.0% | 0.1% | 0.0% | 99% | 104%
Fixed

## Slide 13: Encoder optimization
Luma chroma quality balance adjustment is introduced to balance luma and chroma gain.
In addition to default chroma QP offset which is set equal to 1 in JEM software, chroma weight is adjusted
 | ChromaWeight | note
JEM | 3.0 | 
SDR constraint set 1 (RA) | 3.2 | chroma bits are shifted to luma
SDR constraint set 2 (LB) | 3.1 | chroma bits are shifted to luma
HDR-A HLG | 3.0 | same as JEM
HDR-B PQ | 3.1 | chroma bits are shifted to luma

## Slide 14: SDR CS1 result (Submitted software)
 | Constraint Set 1 |  |  |  |  |  |  | Constraint Set 1 |  |  |  |  | 
 | Over HM16.16 |  |  |  |  |  |  | Over JEM7.0 |  |  |  |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
FoodMarket4 | -34.64% | -46.00% | -49.93% | 1.73 | 1.35 | 1.61 |  | -2.06% | -4.26% | -5.99% | 0.08 | 0.09 | 0.14
CatRobot1 | -39.09% | -53.80% | -46.84% | 1.53 | 0.99 | 1.33 |  | 0.31% | -3.76% | -2.37% | -0.01 | 0.04 | 0.04
DaylightRoad2 | -41.06% | -60.30% | -44.57% | 1.15 | 1.33 | 0.84 |  | -1.30% | -8.85% | -6.34% | 0.02 | 0.11 | 0.08
ParkRunning3 | -32.79% | -24.99% | -27.82% | 1.06 | 0.42 | 0.39 |  | -2.48% | 0.23% | -0.58% | 0.07 | 0.00 | 0.01
Campfire | -36.45% | -34.64% | -50.30% | 1.08 | 1.29 | 1.55 |  | -3.34% | -0.07% | -1.56% | 0.07 | 0.00 | 0.03
BQTerrace | -33.93% | -50.92% | -59.01% | 1.03 | 0.97 | 1.15 |  | -5.21% | -12.02% | -11.83% | 0.12 | 0.15 | 0.13
RitualDance | -29.31% | -40.74% | -46.16% | 1.58 | 1.19 | 1.57 |  | -2.80% | -6.57% | -9.91% | 0.13 | 0.14 | 0.25
MarketPlace | -30.45% | -51.28% | -49.09% | 1.07 | 0.93 | 0.93 |  | -1.86% | -8.11% | -8.55% | 0.05 | 0.10 | 0.12
BasketballDrive | -33.30% | -49.56% | -46.67% | 1.21 | 1.12 | 1.44 |  | -3.20% | -7.93% | -5.90% | 0.09 | 0.11 | 0.13
Cactus | -34.64% | -47.37% | -42.81% | 1.42 | 0.77 | 1.12 |  | 0.60% | -4.16% | -3.05% | -0.02 | 0.04 | 0.06
Average SDR-A | -36.81% | -43.95% | -43.89% | 1.31 | 1.08 | 1.14 |  | -1.78% | -3.34% | -3.37% | 0.05 | 0.05 | 0.06
Average SDR-B | -32.33% | -47.98% | -48.75% | 1.26 | 1.00 | 1.24 |  | -2.50% | -7.76% | -7.85% | 0.07 | 0.11 | 0.14
Average all | -34.57% | -45.96% | -46.32% | 1.29 | 1.04 | 1.19 |  | -2.14% | -5.55% | -5.61% | 0.06 | 0.08 | 0.10
Enc Time[%] | 1890% |  |  |  |  |  |  | 237% |  |  |  |  | 
Dec Time[%] | 1630% |  |  |  |  |  |  | 214% |  |  |  |  | 

## Slide 15: SDR CS2 result (Submitted software)
 | Constraint Set 2 |  |  |  |  |  |  | Constraint Set 2 |  |  |  |  | 
 | Over HM16.16 |  |  |  |  |  |  | Over JEM7.0 |  |  |  |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
BQTerrace | -28.75% | -47.87% | -54.21% | 0.86 | 0.57 | 0.65 |  | -3.51% | -1.27% | -6.82% | 0.08 | 0.01 | 0.04
RitualDance | -23.43% | -36.60% | -38.80% | 1.21 | 0.89 | 1.09 |  | -2.20% | -3.60% | -5.17% | 0.10 | 0.07 | 0.12
MarketPlace | -22.75% | -43.60% | -42.99% | 0.73 | 0.57 | 0.62 |  | -2.64% | -1.27% | -3.50% | 0.08 | 0.01 | 0.04
BasketballDrive | -27.06% | -46.94% | -45.01% | 1.02 | 1.01 | 1.34 |  | -1.99% | -2.16% | -2.02% | 0.06 | 0.03 | 0.04
Cactus | -28.84% | -43.31% | -40.44% | 1.16 | 0.62 | 0.91 |  | -0.80% | -1.56% | -1.64% | 0.03 | 0.01 | 0.03
Average SDR-B | -26.17% | -43.67% | -44.29% | 1.00 | 0.73 | 0.92 |  | -2.23% | -1.97% | -3.83% | 0.07 | 0.03 | 0.05
Enc Time[%] | 1293% |  |  |  |  |  |  | 161% |  |  |  |  | 
Dec Time[%] | 667% |  |  |  |  |  |  | 100% |  |  |  |  | 

## Slide 16: SDR CS1 result (Bug-fixed software)
 | Constraint Set 1 |  |  |  |  |  |  | Constraint Set 1 |  |  |  |  | 
 | Over HM16.16 |  |  |  |  |  |  | Over JEM7.0 |  |  |  |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
FoodMarket4 | -34.99% | -46.15% | -50.16% | 1.76 | 1.36 | 1.62 |  | -2.58% | -4.54% | -6.43% | 0.10 | 0.09 | 0.15
CatRobot1 | -40.95% | -55.45% | -48.61% | 1.62 | 1.03 | 1.40 |  | -2.78% | -7.43% | -5.70% | 0.07 | 0.08 | 0.11
DaylightRoad2 | -42.13% | -60.83% | -45.32% | 1.19 | 1.35 | 0.86 |  | -3.10% | -10.03% | -7.61% | 0.06 | 0.12 | 0.10
ParkRunning3 | -33.07% | -25.24% | -28.01% | 1.07 | 0.43 | 0.40 |  | -2.90% | -0.10% | -0.84% | 0.08 | 0.00 | 0.01
Campfire | -36.50% | -34.65% | -50.42% | 1.08 | 1.29 | 1.55 |  | -3.42% | -0.10% | -1.80% | 0.07 | 0.00 | 0.04
BQTerrace | -33.93% | -50.84% | -59.00% | 1.03 | 0.97 | 1.15 |  | -5.21% | -11.89% | -11.79% | 0.12 | 0.15 | 0.13
RitualDance | -29.46% | -40.79% | -46.28% | 1.59 | 1.19 | 1.57 |  | -3.01% | -6.64% | -10.10% | 0.14 | 0.14 | 0.25
MarketPlace | -31.09% | -51.64% | -49.67% | 1.10 | 0.94 | 0.94 |  | -2.80% | -8.84% | -9.60% | 0.08 | 0.11 | 0.13
BasketballDrive | -33.47% | -49.63% | -46.91% | 1.21 | 1.12 | 1.45 |  | -3.45% | -8.03% | -6.31% | 0.10 | 0.12 | 0.14
Cactus | -37.16% | -49.00% | -44.20% | 1.55 | 0.81 | 1.17 |  | -3.36% | -7.23% | -5.49% | 0.10 | 0.08 | 0.10
Average SDR-A | -37.53% | -44.47% | -44.50% | 1.34 | 1.09 | 1.17 |  | -2.96% | -4.44% | -4.48% | 0.08 | 0.06 | 0.08
Average SDR-B | -33.02% | -48.38% | -49.21% | 1.30 | 1.01 | 1.26 |  | -3.56% | -8.53% | -8.66% | 0.11 | 0.12 | 0.15
Average all | -35.28% | -46.42% | -46.86% | 1.32 | 1.05 | 1.21 |  | -3.26% | -6.48% | -6.57% | 0.09 | 0.09 | 0.12
Enc Time[%] | 2175% |  |  |  |  |  |  | 273% |  |  |  |  | 
Dec Time[%] | 1955% |  |  |  |  |  |  | 257% |  |  |  |  | 

## Slide 17: SDR CS2 result (Bug-fixed software)
 | Constraint Set 2 |  |  |  |  |  |  | Constraint Set 2 |  |  |  |  | 
 | Over HM16.16 |  |  |  |  |  |  | Over JEM7.0 |  |  |  |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
BQTerrace | -28.76% | -47.20% | -53.62% | 0.86 | 0.55 | 0.64 |  | -3.54% | 0.83% | -4.31% | 0.08 | -0.01 | 0.02
RitualDance | -23.60% | -36.67% | -38.98% | 1.22 | 0.90 | 1.10 |  | -2.41% | -3.74% | -5.48% | 0.11 | 0.07 | 0.12
MarketPlace | -23.11% | -43.40% | -42.47% | 0.75 | 0.57 | 0.61 |  | -3.10% | -1.10% | -2.66% | 0.09 | 0.01 | 0.03
BasketballDrive | -27.35% | -47.24% | -45.40% | 1.04 | 1.02 | 1.35 |  | -2.38% | -2.71% | -2.70% | 0.07 | 0.04 | 0.06
Cactus | -30.25% | -43.84% | -40.76% | 1.22 | 0.63 | 0.92 |  | -2.79% | -2.39% | -1.91% | 0.09 | 0.02 | 0.03
Average SDR-B | -26.61% | -43.67% | -44.25% | 1.02 | 0.73 | 0.92 |  | -2.84% | -1.82% | -3.41% | 0.09 | 0.03 | 0.05
Enc Time[%] | 1602% |  |  |  |  |  |  | 199% |  |  |  |  | 
Dec Time[%] | 942% |  |  |  |  |  |  | 141% |  |  |  |  | 

## Slide 18: Submitted vs Bug-fixed
 |  | Over HM16.16 |  |  |  |  |  |  | Over JEM7.0 |  |  |  |  | 
CS1 |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
CatRobot1 | Submitted | -39.09% | -53.80% | -46.84% | 1.53 | 0.99 | 1.33 |  | 0.31% | -3.76% | -2.37% | -0.01 | 0.04 | 0.04
 | Bug-fixed | -40.95% | -55.45% | -48.61% | 1.62 | 1.03 | 1.40 |  | -2.78% | -7.43% | -5.70% | 0.07 | 0.08 | 0.11
Daylight Road2 | Submitted | -41.06% | -60.30% | -44.57% | 1.15 | 1.33 | 0.84 |  | -1.30% | -8.85% | -6.34% | 0.02 | 0.11 | 0.08
 | Bug-fixed | -42.13% | -60.83% | -45.32% | 1.19 | 1.35 | 0.86 |  | -3.10% | -10.03% | -7.61% | 0.06 | 0.12 | 0.10
Cactus | Submitted | -34.64% | -47.37% | -42.81% | 1.42 | 0.77 | 1.12 |  | 0.60% | -4.16% | -3.05% | -0.02 | 0.04 | 0.06
 | Bug-fixed | -37.16% | -49.00% | -44.20% | 1.55 | 0.81 | 1.17 |  | -3.36% | -7.23% | -5.49% | 0.10 | 0.08 | 0.10
CS2 |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
Cactus | Submitted | -34.64% | -47.37% | -42.81% | 1.42 | 0.77 | 1.12 |  | 0.60% | -4.16% | -3.05% | -0.02 | 0.04 | 0.06
 | Bug-fixed | -37.16% | -49.00% | -44.20% | 1.55 | 0.81 | 1.17 |  | -3.36% | -7.23% | -5.49% | 0.10 | 0.08 | 0.10
CS1 | Submitted | Bug-fixed
Enc Time[%] | 1890% | 2175%
Dec Time[%] | 1630% | 1955%
CS2 | Submitted | Bug-fixed
Enc Time[%] | 1293% | 1602%
Dec Time[%] | 667% | 942%

## Slide 19: HDR CS1 result (Submitted software) over HM
 | BD-rate |  |  |  |  |  |  | 
 | DE100 | PSNR L100 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV
DayStreet | -60.8% | -37.9% | -36.4% | -58.2% | -70.7% | -35.4% | -56.8% | -69.2%
PeopleInShoppingCenter | -53.5% | -32.0% | -30.7% | -62.8% | -58.5% | -30.5% | -60.4% | -58.4%
SunsetBeach | -60.8% | -27.2% | -22.1% | -83.7% | -83.5% | -22.9% | -78.9% | -84.9%
Market | -45.3% | -27.9% | -28.0% | -54.4% | -50.7% | -25.1% | -45.9% | -40.1%
ShowGirl2 | -43.8% | -30.2% | -30.6% | -74.8% | -61.8% | -28.1% | -74.6% | -61.6%
Hurdles | -55.4% | -38.2% | -37.0% | -65.3% | -58.3% | -33.6% | -59.0% | -53.2%
Starting | -41.0% | -34.6% | -32.8% | -41.2% | -47.0% | -30.4% | -38.5% | -32.5%
Cosmos1 | -38.8% | -28.3% | -27.3% | -69.3% | -84.1% | -25.3% | -68.9% | -83.6%
Average HDR-A | -58.4% | -32.3% | -29.7% | -68.2% | -70.9% | -29.6% | -65.3% | -70.8%
Average HDR-B | -44.9% | -31.9% | -31.1% | -61.0% | -60.4% | -28.5% | -57.4% | -54.2%
Average all | -49.9% | -32.0% | -30.6% | -63.7% | -64.3% | -28.9% | -60.4% | -60.4%
Enc Time[%] | 1786% |  |  |  |  |  |  | 
Dec Time[%] | 1726% |  |  |  |  |  |  | 

## Slide 20: HDR CS1 result (Submitted software) over JEM
 | BD-rate |  |  |  |  |  |  | 
 | DE100 | PSNR L100 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV
DayStreet | -7.1% | -2.5% | -2.1% | -7.0% | -9.3% | -2.0% | -7.0% | -9.6%
PeopleInShoppingCenter | -7.5% | -3.5% | -3.2% | -12.4% | -10.5% | -3.2% | -11.2% | -11.2%
SunsetBeach | -13.8% | -1.4% | -1.3% | -15.7% | -25.7% | -1.1% | -12.9% | -29.9%
Market | -9.4% | -4.7% | -4.1% | -13.9% | -15.9% | -2.3% | -10.8% | -11.4%
ShowGirl2 | -23.9% | -5.3% | -4.3% | -41.8% | -51.7% | -3.3% | -45.8% | -55.5%
Hurdles | -13.1% | -5.9% | -5.5% | -15.2% | -8.7% | -4.2% | -10.3% | -6.3%
Starting | -10.9% | -5.6% | -3.7% | -11.0% | -15.3% | -2.5% | -9.9% | -12.2%
Cosmos1 | -12.1% | -5.6% | -4.2% | -8.5% | -32.2% | -3.4% | -8.4% | -26.7%
Average HDR-A | -9.5% | -2.5% | -2.2% | -11.7% | -15.2% | -2.1% | -10.4% | -16.9%
Average HDR-B | -13.9% | -5.4% | -4.4% | -18.1% | -24.8% | -3.1% | -17.0% | -22.4%
Average all | -12.2% | -4.3% | -3.6% | -15.7% | -21.2% | -2.7% | -14.5% | -20.3%
Enc Time[%] | 224% |  |  |  |  |  |  | 
Dec Time[%] | 227% |  |  |  |  |  |  | 

## Slide 21: HDR CS1 result (Bug-fixed software) over HM
 | BD-rate |  |  |  |  |  |  | 
 | DE100 | PSNR L100 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV
DayStreet | -61.4% | -38.7% | -37.2% | -58.8% | -71.2% | -36.2% | -57.4% | -69.8%
PeopleInShoppingCenter | -53.6% | -32.1% | -30.9% | -62.8% | -58.7% | -30.6% | -60.5% | -58.5%
SunsetBeach | -60.9% | -27.3% | -22.2% | -83.8% | -83.6% | -22.9% | -79.0% | -85.1%
Market | -45.3% | -27.9% | -28.1% | -54.4% | -50.7% | -25.2% | -45.8% | -40.3%
ShowGirl2 | -43.8% | -30.3% | -30.7% | -75.1% | -61.6% | -28.1% | -74.9% | -61.2%
Hurdles | -55.5% | -38.4% | -37.2% | -65.4% | -58.1% | -33.9% | -59.0% | -53.2%
Starting | -41.4% | -35.1% | -33.4% | -41.4% | -47.4% | -31.0% | -38.6% | -33.0%
Cosmos1 | -39.0% | -28.5% | -27.4% | -69.5% | -84.2% | -25.5% | -69.0% | -83.6%
Average HDR-A | -58.6% | -32.7% | -30.1% | -68.5% | -71.2% | -29.9% | -65.6% | -71.1%
Average HDR-B | -45.0% | -32.1% | -31.4% | -61.2% | -60.4% | -28.7% | -57.5% | -54.3%
Average all | -50.1% | -32.3% | -30.9% | -63.9% | -64.4% | -29.2% | -60.5% | -60.6%
Enc Time[%] | 2073% |  |  |  |  |  |  | 
Dec Time[%] | 1958% |  |  |  |  |  |  | 

## Slide 22: HDR CS1 result (Bug-fixed software) over JEM
 | BD-rate |  |  |  |  |  |  | 
 | DE100 | PSNR L100 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV
DayStreet | -8.4% | -3.8% | -3.4% | -8.3% | -10.6% | -3.3% | -8.2% | -11.0%
PeopleInShoppingCenter | -7.7% | -3.7% | -3.4% | -12.5% | -10.7% | -3.4% | -11.4% | -11.4%
SunsetBeach | -14.0% | -1.5% | -1.4% | -15.9% | -26.3% | -1.1% | -13.1% | -30.4%
Market | -9.4% | -4.7% | -4.2% | -13.7% | -15.9% | -2.3% | -10.5% | -11.4%
ShowGirl2 | -24.0% | -5.4% | -4.4% | -42.4% | -51.8% | -3.3% | -46.3% | -55.3%
Hurdles | -13.2% | -6.2% | -5.8% | -15.3% | -8.3% | -4.6% | -10.4% | -6.3%
Starting | -11.5% | -6.3% | -4.5% | -11.3% | -15.9% | -3.3% | -10.2% | -12.8%
Cosmos1 | -12.3% | -5.8% | -4.4% | -8.6% | -33.3% | -3.7% | -8.5% | -27.8%
Average HDR-A | -10.1% | -3.0% | -2.8% | -12.2% | -15.9% | -2.6% | -10.9% | -17.6%
Average HDR-B | -14.1% | -5.7% | -4.7% | -18.3% | -25.1% | -3.4% | -17.2% | -22.7%
Average all | -12.6% | -4.7% | -3.9% | -16.0% | -21.6% | -3.1% | -14.8% | -20.8%
Enc Time[%] | 260% |  |  |  |  |  |  | 
Dec Time[%] | 257% |  |  |  |  |  |  | 

## Slide 23: Conclusion
This contribution presents SDR and HDR video coding technologies containing:
  Bi-pred optimized transform skip
  MVPlanar
  Position dependent intra interpolation filter
  Luma-adaptive deblocking filter
  Chroma DM binarization bug fix
Performance
  35% and 31% BD-rate gain with 20x encoding and decoding time increase for SDR and HDR, respectively
Propose to establish CEs to study the proposed coding tools.
Chart: Coding Gain (%)
| 6.4443148704799453
JVET-J0026 | 0.081525
JVET-J0027 | 0.032599
JVET-J0026
JVET-J0027
Encoding Times (compared to JEM)

## Slide 24: Summary of coding tools
Tool names | Short description
Bi-pred optimized TS | Transform-skipped coefficients are reordered using the estimated prediction accuracy calculated by the difference between L0 and L1 reference blocks when bi-prediction is applied.
MVPlanar | Sub-block motion vector derivation by interpolating the neighboring MV predictors with explicit signaling of inter prediction indices and reference frame indices.
PDIntrafilter | Two types of intra interpolation filters are alternatively applied depending on the position of the prediction samples.
Luma-adaptive deblocking filter | Deblocking filter strength increment according to the luma level
chroma DM binarization bug fix | The bug-fix reported in JVET-H0077 on binarization for chroma intra prediction modes.

## Slide 25
 | Random Access Main 10 |  |  |  | 
 | JEM6 w/o DMVR,ATMVP,FRUC,MVPrecision,IC,BIO,AFFINE |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.3% | -0.3% | -0.2% | 96% | 99%
Class A2 | -0.6% | -0.3% | -0.4% | 94% | 99%
Class B | -0.4% | -0.3% | -0.2% | 102% | 108%
Class C | -0.2% | -0.3% | -0.2% | 97% | 108%
Class D | -0.2% | -0.1% | 0.0% | 87% | 99%
Class E | -0.4% | -0.2% | -0.2% | 103% | 102%
Overall (Ref) | -0.4% | -0.3% | -0.2% | 96% | 103%
Class F(Optional) | -0.1% | -0.2% | -0.2% | 99% | 101%
` |  | Y | U | V | EncT | DecT
CS1 | SDR-A | 0.4% | 0.3% | 0.4% | 84% | 106%
 | SDR-B | 0.2% | 0.2% | 0.2% | 119% | 97%
CS2 | SDR-B | 0.2% | 0.4% | 0.5% | 97% | 96%
CS1 | HDR-A | 0.2% | 0.1% | 0.1% | 81% | 108%
 | HDR-B | 0.3% | 0.5% | 0.7% | 114% | 101%
-Alternative temporal motion vector prediction
-Higher motion vector storage accuracy
-Local illumination compensation
-Affine motion compensation prediction
-Pattern matched motion vector derivation
-Bi-directional optical flow
-Decoder-side motion vector refinement
For tool-on test, following tools were disabled.
Interpolated MC prediction (MVPlanar)
Tool-off test
Tool-on test