## Slide 1: Description of SDR video coding technology proposal by Tencent (JVET-J0029)
X. Li, X. Xu, X. Zhao, J. Ye, L. Zhao, S. Liu
2018/04

## Slide 2: Introduction
On top of Next Software 1.8.5
Coding structure improvement
  256×256 CTU
  QT + BT + TT
Intra block copy
Intra coding
  Intra mode coding
  Simplified PDPC
  Multi-line intra prediction
Inter coding
  Improved merge candidate list construction
Transform
  Improved primary transform

## Slide 3: Coding Structure
256×256 CTU
  256-point transform is supported for 256×256 CTU
Triple tree structure
  Vertical/horizontal triple tree proposed in JVET-D0117 is implemented

## Slide 4: Intra Block Copy (IBC)
IBC is a well known tool for screen content coding
IBC flag is signaled at block level in non-chroma tree, before merge flag
  For merge IBC mode
    a separate merge list is constructed for IBC candidates with 5 spatial neighbors.
  For non-merge IBC mode
    Block vector predictor has two candidates, one from left neighbor and one from above neighbor
    Block vector difference is coded in the same way as MVD.
Luma-Chroma separate split tree (DualTree)
  A chroma CU may choose IBC mode or other modes or split further only when all its corresponding luma sub-blocks are coded in IBC mode
  Otherwise, chroma CU cannot choose IBC mode
Hash based search for blocks with both sides <=16
  Hash key is calculated based on 4x4 blocks; larger blocks will rely on all its sub-blocks’ matching results
  When there is no valid block vector found in hash search, local search is used with range 128 to the left and on the top

## Slide 5: Intra Coding (1)
Intra mode coding (JVET-H0024/H0029)
  For MPM, DC is checked after above and left
  Non-MPM modes are put into 2 sets
    16 selected modes: loop MPM lists and add adjacent directional modes with offset 2, -2, 4, -4, 6, -6…
    Remaining 45 modes
Simplified PDPC (JVET-E0057)
  For planar, DC, horizontal and vertical
  pred[x][y] = wL * R-1,y + wT * Rx,-1 + wTL * R-1,-1 + (64 – wL – wT
  – wTL) * pred[x][y] + 32 ) >> 6
  wT = 32 >> ( ( y<<1 ) >> shift ),
  wL = 32 >> ( ( x<<1 ) >> shift),
  wTL = – ( wL>>4 ) – ( wT>>4 ),
  shift = ( log2( width ) + log2( height ) + 2 ) >> 2

## Slide 6: Intra Coding (2)
Multiline intra prediction (Arbitrary reference tier JVET-D0099)
  Prediction with 1st reference line is the intra prediction in Next
  Four reference lines are supported
  NSST is off for 3rd and 4th lines
  Planar and DC modes are off for 2nd, 3rd, and 4th lines
  Slice level on/off

## Slide 7: Inter Coding
Merge candidate list construction
  Max candidate number is increased to 23
  New candidates are
  inserted after TMVP
  Grid (16x16) based scan
  from close to far away
  until (-96,-96)
    Top region: from bottom to
    top, from left to right
    Left region: from right to
    left, from top to bottom
    Top left region: from bottom
    to top, from right to left

## Slide 8: Transform
Primary transform
  From 2-pt transform to 256-pt transform
  Block size dependent zero-out
    For 64-pt, 128-pt and 256-pt transforms, only the first 32, 16 and 4 coefficients are kept, respectively
  Supported transforms (JVET-D0065, JVET-D0126)
Secondary transform
  HyGT is replaced by matrix multiplication
Transform size | Transform type
2-pt | DCT-2
4-pt, 8-pt | DCT-2/5/8, DST-1/4, ID, DST4, 2 KLTs
16-pt | DCT-2/5/8, DST-1/7, ID, 2 KLT
32-pt, 64-pt | DCT-2/5/8, DST-1/7
128-pt | DCT-2
256-pt | HWT

## Slide 9: Simulation Results
 | Constraint Set 1 |  |  |  |  |  |  | Constraint Set 1 |  |  |  |  | 
 | Over HM16.16 |  |  |  |  |  |  | Over JEM7.0 |  |  |  |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
FoodMarket4 | -36.09% | -46.50% | -50.41% | 1.82 | 1.37 | 1.63 |  | -4.32% | -5.24% | -6.89% | 0.17 | 0.11 | 0.16
CatRobot1 | -42.41% | -57.15% | -50.41% | 1.68 | 1.07 | 1.47 |  | -5.31% | -11.68% | -9.67% | 0.14 | 0.12 | 0.19
DaylightRoad2 | -43.94% | -60.47% | -45.61% | 1.24 | 1.34 | 0.87 |  | -6.18% | -9.71% | -8.54% | 0.12 | 0.12 | 0.12
ParkRunning3 | -33.87% | -29.76% | -34.13% | 1.10 | 0.52 | 0.50 |  | -4.07% | -6.39% | -9.64% | 0.11 | 0.09 | 0.12
Campfire | -36.98% | -36.83% | -53.21% | 1.09 | 1.40 | 1.67 |  | -4.26% | -3.34% | -7.54% | 0.09 | 0.11 | 0.15
BQTerrace | -34.33% | -50.84% | -58.87% | 1.04 | 0.97 | 1.16 |  | -5.76% | -11.81% | -12.06% | 0.14 | 0.15 | 0.13
RitualDance | -30.44% | -41.69% | -45.56% | 1.65 | 1.23 | 1.54 |  | -4.38% | -8.32% | -8.88% | 0.20 | 0.18 | 0.22
MarketPlace | -31.30% | -51.94% | -49.61% | 1.11 | 0.94 | 0.93 |  | -3.14% | -9.10% | -8.96% | 0.09 | 0.11 | 0.12
BasketballDrive | -34.74% | -50.34% | -48.00% | 1.27 | 1.14 | 1.49 |  | -5.35% | -9.54% | -8.25% | 0.15 | 0.14 | 0.18
Cactus | -37.62% | -49.41% | -45.71% | 1.57 | 0.81 | 1.22 |  | -4.24% | -8.23% | -8.70% | 0.13 | 0.09 | 0.16
Average SDR-A | -38.66% | -46.14% | -46.76% | 1.39 | 1.14 | 1.23 |  | -4.83% | -7.27% | -8.46% | 0.13 | 0.11 | 0.15
Average SDR-B | -33.69% | -48.85% | -49.55% | 1.33 | 1.02 | 1.27 |  | -4.57% | -9.40% | -9.37% | 0.14 | 0.13 | 0.16
Average all | -36.17% | -47.49% | -48.15% | 1.36 | 1.08 | 1.25 |  | -4.70% | -8.34% | -8.91% | 0.13 | 0.12 | 0.15
Enc Time[%] | 1928% |  |  |  |  |  |  | 242% |  |  |  |  | 
Dec Time[%] | 954% |  |  |  |  |  |  | 125% |  |  |  |  | 
Max Delta Rate[%] | -0.01% |  |  |  |  |  |  |  |  |  |  |  | 
Min Delta Rate[%] | -0.73% |  |  |  |  |  |  |  |  |  |  |  | 
Max Delta PSNR (YUV) | 2.19 |  | 1.61 |  | 1.95 |  |  | 0.21 |  | 0.20 |  | 0.25 | 
Min Delta PNSR (YUV) | 0.73 |  | 0.50 |  | 0.48 |  |  | 0.06 |  | 0.06 |  | 0.09 | 
 | Constraint Set 2 |  |  |  |  |  |  | Constraint Set 2 |  |  |  |  | 
 | Over HM16.16 |  |  |  |  |  |  | Over JEM7.0 |  |  |  |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
BQTerrace | -29.44% | -52.08% | -58.16% | 0.89 | 0.65 | 0.72 |  | -4.57% | -11.30% | -16.92% | 0.11 | 0.09 | 0.11
RitualDance | -24.55% | -38.39% | -39.59% | 1.28 | 0.95 | 1.13 |  | -3.69% | -6.41% | -6.49% | 0.17 | 0.12 | 0.15
MarketPlace | -24.41% | -48.25% | -47.21% | 0.80 | 0.65 | 0.70 |  | -4.76% | -8.94% | -9.66% | 0.14 | 0.09 | 0.12
BasketballDrive | -28.67% | -51.39% | -49.18% | 1.09 | 1.15 | 1.51 |  | -4.20% | -10.69% | -9.48% | 0.13 | 0.17 | 0.22
Cactus | -31.83% | -47.80% | -46.00% | 1.30 | 0.71 | 1.07 |  | -5.16% | -10.02% | -11.54% | 0.17 | 0.10 | 0.19
Average SDR-B | -27.78% | -47.58% | -48.03% | 1.07 | 0.82 | 1.03 |  | -4.47% | -9.47% | -10.82% | 0.14 | 0.11 | 0.16
Enc Time[%] | 1951% |  |  |  |  |  |  | 242% |  |  |  |  | 
Dec Time[%] | 754% |  |  |  |  |  |  | 113% |  |  |  |  | 
Max Delta Rate | -0.03% |  |  |  |  |  |  |  |  |  |  |  | 
Min Delta Rate | -0.82% |  |  |  |  |  |  |  |  |  |  |  | 
Max Delta PSNR (YUV) | 1.39 |  | 1.23 |  | 1.63 |  |  | 0.21 |  | 0.18 |  | 0.23 | 
Min Delta PNSR (YUV) | 0.62 |  | 0.55 |  | 0.57 |  |  | 0.05 |  | 0.05 |  | 0.07 | 

## Slide 10: Highlighted Aspect – IBC
JVET-J0029 with IBC off vs JVET-J0029
  CfP sequences
    Luma BD-rate increase for camera
    sequences with textures when IBC is
    off (1.4% for BQTerrance)
    Minor impact on coding time
  SCC sequences
    Over 52% luma BD-rate increase
    Small impact on coding time
Sequences | RA | Enc Time | Dec Time
FoodMarket4 | -0.01% | 101% | 100%
CatRobot1 | 0.37% | 102% | 100%
DaylightRoad2 | 0.54% | 97% | 96%
ParkRunning3 | -0.06% | 100% | 93%
CampfireParty2 | 0.06% | 98% | 96%
BQTerrace | 1.42% | 98% | 100%
RitualDance | 0.00% | 106% | 99%
MarketPlace | 0.02% | 100% | 98%
BasketballDrive | 0.15% | 99% | 93%
Cactus | 0.33% | 102% | 100%
Average | 0.28% | 100% | 98%
Sequences | RA | Enc Time | Dec Time
Console | 54.67% | 91% | 127%
Desktop | 100.79% | 93% | 115%
FlyingGraphics | 18.42% | 94% | 106%
ChinaEditing | 35.05% | 96% | 105%
HD Average | 52.23% | 94% | 113%

## Slide 11: Further work on top of JVET-J0029
JVET-J0047: -7.67% luma BD-rate reduction over JEM anchor for random access
 | Constraint Set 1 |  |  |  |  |  |  | Constraint Set 1 |  |  |  |  | 
 | Over HM16.16 |  |  |  |  |  |  | Over JEM7.0 |  |  |  |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
FoodMarket4 | -36.61% | -46.51% | -50.33% | 1.85 | 1.37 | 1.62 |  | -5.13% | -5.31% | -6.73% | 0.20 | 0.11 | 0.15
CatRobot1 | -42.69% | -56.38% | -49.50% | 1.69 | 1.05 | 1.44 |  | -5.74% | -10.02% | -7.87% | 0.15 | 0.10 | 0.15
DaylightRoad2 | -44.07% | -60.70% | -45.60% | 1.25 | 1.35 | 0.87 |  | -6.39% | -10.19% | -8.49% | 0.12 | 0.12 | 0.11
ParkRunning3 | -38.51% | -21.07% | -25.57% | 1.29 | 0.34 | 0.35 |  | -10.77% | 6.17% | 3.13% | 0.31 | -0.08 | -0.04
Campfire | -45.78% | -28.91% | -54.07% | 1.41 | 1.04 | 1.70 |  | -17.74% | 8.15% | -8.62% | 0.39 | -0.25 | 0.18
BQTerrace | -35.89% | -51.94% | -60.06% | 1.10 | 0.99 | 1.18 |  | -8.02% | -13.38% | -13.74% | 0.19 | 0.17 | 0.15
RitualDance | -31.38% | -42.63% | -46.33% | 1.71 | 1.27 | 1.58 |  | -5.71% | -9.92% | -10.21% | 0.27 | 0.21 | 0.25
MarketPlace | -32.73% | -53.08% | -50.50% | 1.17 | 0.97 | 0.95 |  | -5.21% | -11.48% | -10.79% | 0.15 | 0.14 | 0.15
BasketballDrive | -35.51% | -51.43% | -48.79% | 1.30 | 1.18 | 1.52 |  | -6.49% | -11.61% | -9.64% | 0.18 | 0.17 | 0.22
Cactus | -38.45% | -49.61% | -45.98% | 1.61 | 0.82 | 1.24 |  | -5.53% | -8.71% | -9.32% | 0.17 | 0.09 | 0.17
Average SDR-A | -41.53% | -42.72% | -45.01% | 1.50 | 1.03 | 1.20 |  | -9.15% | -2.24% | -5.72% | 0.24 | 0.00 | 0.11
Average SDR-B | -34.79% | -49.74% | -50.33% | 1.38 | 1.04 | 1.29 |  | -6.19% | -11.02% | -10.74% | 0.19 | 0.16 | 0.19
Average all | -38.16% | -46.23% | -47.67% | 1.44 | 1.04 | 1.25 |  | -7.67% | -6.63% | -8.23% | 0.21 | 0.08 | 0.15
Enc Time[%] | 2247% |  |  |  |  |  |  | 282% |  |  |  |  | 
Dec Time[%] | 880% |  |  |  |  |  |  | 115% |  |  |  |  | 
Max Delta Rate[%] | 0.14% |  |  |  |  |  |  |  |  |  |  |  | 
Min Delta Rate[%] | -16.66% |  |  |  |  |  |  |  |  |  |  |  | 
Max Delta PSNR (YUV) | 2.16 |  | 1.64 |  | 1.89 |  |  | 0.23 |  | 0.22 |  | 0.28 | 
Min Delta PNSR (YUV) | 0.74 |  | 0.16 |  | 0.21 |  |  | 0.07 |  | -0.82 |  | -0.18 | 

## Slide 12: JVET-J0049: Structure only performance
SplitToSquare is proposed on top of QT + BT + TT
Coding performance over constraint set 1
Coding performance over constraint set 2
Multi-parameter CABAC was reportedly bring 1.2% gain in random access [JVET-B0022]
 | Over HM-16.6 |  |  |  | 
 | Y | U | V | EncT | DecT
Class UHD | -16.87% | -17.95% | -19.57% | 320% | 123%
Class HD | -12.66% | -22.41% | -25.48% | 266% | 114%
Overall (Ref) | -14.76% | -20.18% | -22.52% | 292% | 118%
 | Over HM-16.6 |  |  |  | 
 | Y | U | V | EncT | DecT
HD | -13.25% | -35.18% | -37.43% | 209% | 105%
Overall (Ref) | -13.25% | -35.18% | -37.43% | 213% | 106%

## Slide 13: Closing Remarks
Following modules are improved/proposed on top of Next Software 1.8.5
  Block structure
  Intra block copy
  Intra mode coding, simplified PDPC, multiline intra prediction
  Merge candidate list construction
  Transforms
Compared to anchors
  4.70% and 4.47% luma BD-rate saving over JEM for constraint set 1 and 2, respectively
  36.17% and 27.78% luma BD-rate saving over HM for constraint set 1 and 2, respectively
Significant BD-rate saving for SCC sequences